## Slide 1: CS 353 Internetworking: Routing Algorithms: DV
Spring 2016
Alefiya Hussain

## Slide 2: Outline
Least-cost path routing
Approach 1: link-state routing
Approach 2: distance-vector routing
Routing in the Internet

## Slide 3: Link-State

## Slide 4: Link State Routing
Each node maintains its local “link state” (LS)
Each node floods its local link state
Hence, each node learns the entire network topology
  Can use Dijkstra’s to compute the shortest paths between nodes
Host A
Host B
Host E
Host D
Host C
N1
N2
N3
N4
N5
N7
N6
A
B
E
D
C
A
B
E
D
C
A
B
E
D
C
A
B
E
D
C
A
B
E
D
C
A
B
E
D
C
A
B
E
D
C

## Slide 5: Dijkstra’s Shortest Path Algorithm
INPUT:
  Network topology (graph), with link costs
OUTPUT:
  Least cost paths from one node to all other nodes
Iterative: after k iterations, a node knows the least cost path to its k closest neighbors

## Slide 6: Dijkstra’s Algorithm
1 Initialization:
2 S = {A};
3 for all nodes v
4 if v adjacent to A
5 then D(v) = c(A,v);
6 else D(v) = ;
7
8 Loop
9 find w not in S such that D(w) is a minimum;
10 add w to S;
11 update D(v) for all v adjacent to w and not in S:
12 if D(w) + c(w,v) < D(v) then
// w gives us a shorter path to v than we’ve found so far
13 D(v) = D(w) + c(w,v); p(v) = w;
14 until all nodes in S;
c(i,j): link cost from node i to j
D(v): current cost source  v
p(v): v’s predecessor along path from source to v
S: set of nodes whose least cost path definitively known

## Slide 7: Distance Vector

## Slide 8: Example of Distributed Computation
I am one hop away
I am one hop away
I am one hop away
I am two hops away
I am two hops away
I am two hops away
I am two hops away
I am three hops away
I am three hops away
Destination
I am three hops away

## Slide 9: Distance Vector Routing
Each router knows the links to its neighbors
  Does not flood this information to the whole network
Each router has provisional “shortest path” to every other router
  E.g.: Router A: “I can get to router B with cost 11”
Routers exchange this distance vector information with their neighboring routers
  Vector because one entry per destination
Routers look over the set of options offered by their neighbors and select the best one
Iterative process converges to set of shortest paths

## Slide 10: Bellman-Ford Algorithm
INPUT:
  Link costs to each neighbor (Not full topology)
OUTPUT:
  Next hop to each destination and the corresponding cost
  (Not the complete path to the destination)
My neighbors tell me how far they are from dest’n
  Compute: (cost to nbr) plus (nbr’s cost to destination)
  Pick minimum as my choice
  Advertise that cost to my neighbors

## Slide 11: Bellman-Ford Overview
Each router maintains a table
  Best known distance from X to Y,
  via Z as next hop = DZ(X,Y)
Each local iteration caused by:
  Local link cost change
  Message from neighbor
Notify neighbors only if least cost path to any destination changes
  Neighbors then notify their neighbors if necessary
wait for (change in local link cost or msg from neighbor)
recompute distance table
if least cost path to any dest has changed, notify neighbors
Each node:
Notes: Note: for simplicity in this lecture examples we show only the shortest distances to each destination

## Slide 12: Bellman-Ford Overview
Each router maintains a table
  Row for each possible destination
  Column for each directly-attached neighbor to node
  Entry in row Y and column Z of node X  best known distance from X to Y, via Z as next hop = DZ(X,Y)
A
C
1
2
7
B
D
3
1
 | B | C
B | 2 | 8
C | 3 | 7
D | 4 | 8
Node A
Neighbor
(next-hop)
Destinations
DC(A, D)
Notes: Note: for simplicity in this lecture examples we show only the shortest distances to each destination

## Slide 13: Bellman-Ford Overview
Each router maintains a table
  Row for each possible destination
  Column for each directly-attached neighbor to node
  Entry in row Y and column Z of node X  best known distance from X to Y, via Z as next hop = DZ(X,Y)
A
C
1
2
7
B
D
3
1
 | B | C
B | 2 | 8
C | 3 | 7
D | 4 | 8
Node A
Smallest distance in row Y = shortest
Distance of A to Y, D(A, Y)
Notes: Note: for simplicity in this lecture examples we show only the shortest distances to each destination

## Slide 14: Distance Vector Algorithm (cont’d)
1 Initialization:
2 for all neighbors V do
3 if V adjacent to A
4 D(A, V) = c(A,V);
else
D(A, V) = ∞;
send D(A, Y) to all neighbors
loop:
8 wait (until A sees a link cost change to neighbor V /* case 1 */
9 or until A receives update from neighbor V) /* case 2 */
10 if (c(A,V) changes by ±d) /*  case 1 */
11 for all destinations Y that go through V do
12 DV(A,Y) = DV(A,Y) ± d
13 else if (update D(V, Y) received from V) /*  case 2 */
/* shortest path from V to some Y has changed */
14 DV(A,Y) = DV(A,V) + D(V, Y); /* may also change D(A,Y) */
15 if (there is a new minimum for destination Y)
16 send D(A, Y) to all neighbors
17 forever
c(i,j): link cost from node i to j
DZ(A,V): cost from A to V via Z
D(A,V): cost of A’s best path to V

## Slide 15: Distance Vector Algorithm (cont’d)
wait for (change in local link cost or msg from neighbor)
recompute distance table
if least cost path to any dest has changed, notify neighbors
Each node: initialize, then

## Slide 16: Distance Vector Algorithm (cont’d)
1 Initialization:
2 for all neighbors V do
3 if V adjacent to A
4 D(A, V) = c(A,V);
else
D(A, V) = ∞;
send D(A, Y) to all neighbors
loop:
8 wait (until A sees a link cost change to neighbor V /* case 1 */
9 or until A receives update from neighbor V) /* case 2 */
10 if (c(A,V) changes by ±d) /*  case 1 */
11 for all destinations Y that go through V do
12 DV(A,Y) = DV(A,Y) ± d
13 else if (update D(V, Y) received from V) /*  case 2 */
/* shortest path from V to some Y has changed */
14 DV(A,Y) = DV(A,V) + D(V, Y); /* may also change D(A,Y) */
15 if (there is a new minimum for destination Y)
16 send D(A, Y) to all neighbors
17 forever
c(i,j): link cost from node i to j
DZ(A,V): cost from A to V via Z
D(A,V): cost of A’s best path to V

## Slide 17: Example: Initialization
A
C
1
2
7
B
D
3
1
 | B | C
B | 2 | ∞
C | ∞ | 7
D | ∞ | ∞
Node A
 | A | C | D
A | 2 | ∞ | ∞
C | ∞ | 1 | ∞
D | ∞ | ∞ | 3
Node B
Node C
 | A | B | D
A | 7 | ∞ | ∞
B | ∞ | 1 | ∞
D | ∞ | ∞ | 1
 | B | C
A | ∞ | ∞
B | 3 | ∞
C | ∞ | 1
Node D
1 Initialization:
2 for all neighbors V do
3 if V adjacent to A
4 D(A, V) = c(A,V);
else
D(A, V) = ∞;
send D(A, Y) to all neighbors

## Slide 18: Example: C sends update to A
A
C
1
2
7
B
D
3
1
 | B | C
B | 2 | ∞
C | ∞ | 7
D | ∞ | ∞
Node A
 | A | C | D
A | 2 | ∞ | ∞
C | ∞ | 1 | ∞
D | ∞ | ∞ | 3
Node B
Node C
 | A | B | D
A | 7 | ∞ | ∞
B | ∞ | 1 | ∞
D | ∞ | ∞ | 1
 | B | C
A | ∞ | ∞
B | 3 | ∞
C | ∞ | 1
Node D
loop:
…
13 else if (update D(A, Y) from C)
14 DC(A,Y) = DC(A,C) + D(C, Y);
15 if (new min. for destination Y)
16 send D(A, Y) to all neighbors
17 forever
??

## Slide 19: Example: C sends update to A
A
C
1
2
7
B
D
3
1
 | B | C
B | 2 | ∞
C | ∞ | 7
D | ∞ | ∞
Node A
 | A | C | D
A | 2 | ∞ | ∞
C | ∞ | 1 | ∞
D | ∞ | ∞ | 3
Node B
Node C
 | A | B | D
A | 7 | ∞ | ∞
B | ∞ | 1 | ∞
D | ∞ | ∞ | 1
 | B | C
A | ∞ | ∞
B | 3 | ∞
C | ∞ | 1
Node D
loop:
…
13 else if (update D(A, Y) from C)
14 DC(A,Y) = DC(A,C) + D(C, Y);
15 if (new min. for destination Y)
16 send D(A, Y) to all neighbors
17 forever
DC(A, B) = DC(A,C) + D(C, B) = 7 + 1 = 8
DC(A, D) = DC(A,C) + D(C, D) = 7 + 1 = 8

## Slide 20: Example: C sends update to A
A
C
1
2
7
B
D
3
1
 | B | C
B | 2 | 8
C | ∞ | 7
D | ∞ | 8
Node A
 | A | C | D
A | 2 | ∞ | ∞
C | ∞ | 1 | ∞
D | ∞ | ∞ | 3
Node B
Node C
 | A | B | D
A | 7 | ∞ | ∞
B | ∞ | 1 | ∞
D | ∞ | ∞ | 1
 | B | C
A | ∞ | ∞
B | 3 | ∞
C | ∞ | 1
Node D
loop:
…
13 else if (update D(A, Y) from C)
14 DC(A,Y) = DC(A,C) + D(C, Y);
15 if (new min. for destination Y)
16 send D(A, Y) to all neighbors
17 forever
DC(A, B) = DC(A,C) + D(C, B) = 7 + 1 = 8
DC(A, D) = DC(A,C) + D(C, D) = 7 + 1 = 8

## Slide 21: Example: Now B sends update to A
A
C
1
2
7
B
D
3
1
 | B | C
B | 2 | 8
C | ∞ | 7
D | ∞ | 8
Node A
 | A | C | D
A | 2 | ∞ | ∞
C | ∞ | 1 | ∞
D | ∞ | ∞ | 3
Node B
Node C
 | A | B | D
A | 7 | ∞ | ∞
B | ∞ | 1 | 
D | ∞ | ∞ | 1
Node D
loop:
…
13 else if (update D(A, Y) from B)
14 DB(A,Y) = DB(A,B) + D(B, Y);
15 if (new min. for destination Y)
16 send D(A, Y) to all neighbors
17 forever
 | B | C
A | ∞ | ∞
B | 3 | ∞
C | ∞ | 1
??

## Slide 22: Example: Now B sends update to A
A
C
1
2
7
B
D
3
1
 | B | C
B | 2 | 8
C | ∞ | 7
D | ∞ | 8
Node A
 | A | C | D
A | 2 | ∞ | ∞
C | ∞ | 1 | ∞
D | ∞ | ∞ | 3
Node B
Node C
 | A | B | D
A | 7 | ∞ | ∞
B | ∞ | 1 | 
D | ∞ | ∞ | 1
Node D
loop:
…
13 else if (update D(A, Y) from B)
14 DB(A,Y) = DB(A,B) + D(B, Y);
15 if (new min. for destination Y)
16 send D(A, Y) to all neighbors
17 forever
DB(A, C) = DB(A,B) + D(B, C) = 2 + 1 = 3
DB(A, D) = DB(A,B) + D(B, D) = 2 + 3 = 5
 | B | C
A | ∞ | ∞
B | 3 | ∞
C | ∞ | 1

## Slide 23: Example: Now B sends update to A
A
C
1
2
7
B
D
3
1
 | B | C
B | 2 | 8
C | 3 | 7
D | 5 | 8
Node A
 | A | C | D
A | 2 | ∞ | ∞
C | ∞ | 1 | ∞
D | ∞ | ∞ | 3
Node B
Node C
 | A | B | D
A | 7 | ∞ | ∞
B | ∞ | 1 | 
D | ∞ | ∞ | 1
Node D
loop:
…
13 else if (update D(A, Y) from B)
14 DB(A,Y) = DB(A,B) + D(B, Y);
15 if (new min. for destination Y)
16 send D(A, Y) to all neighbors
17 forever
DB(A, C) = DB(A,B) + D(B, C) = 2 + 1 = 3
DB(A, D) = DB(A,B) + D(B, D) = 2 + 3 = 5
 | B | C
A | ∞ | ∞
B | 3 | ∞
C | ∞ | 1
why this is 5, not 4!
Notes: Because B does not yet know it can go thruogh C to D…..
B has not reeived the update from C

## Slide 24: Example: After 1st Full Exchange
A
C
1
2
7
B
D
3
1
 | B | C
B | 2 | 8
C | 3 | 7
D | 5 | 8
Node A
Node B
Node C
 | A | B | D
A | 7 | 3 | ∞
B | 9 | 1 | 4
D | ∞ | 4 | 1
Node D
 | B | C
A | 5 | 8
B | 3 | 2
C | 4 | 1
End of 1st Iteration All nodes knows the best two-hop paths
 | A | C | D
A | 2 | 8 | ∞
C | 9 | 1 | 4
D | ∞ | 2 | 3
Why is this 3?
Assume all send messages at same time
Notes: Receveid upldate first round, two hop patths…
Hence C –B –A

## Slide 25: Example: Now A sends update to B
A
C
1
2
7
B
D
3
1
 | B | C
B | 2 | 8
C | 3 | 7
D | 5 | 8
Node A
Node B
Node C
 | A | B | D
A | 7 | 3 | ∞
B | 9 | 1 | 4
D | ∞ | 4 | 1
Node D
 | B | C
A | 5 | 8
B | 3 | 2
C | 4 | 1
 | A | C | D
A | 2 | 8 | ∞
C | 5 | 1 | 4
D | 7 | 2 | 3
loop:
…
13 else if (update D(B, Y) from A)
14 DA(B,Y) = DA(B,A) + D(A, Y);
15 if (new min. for destination Y)
16 send D(B, Y) to all neighbors
17 forever
DA(B, C) = DA(B,A) + D(A, C) = 2 + 3 = 5
DA(B, D) = DA(B,A) + D(A, D) = 2 + 5 = 7
Notes: Talk about where the 5 and 7 come from!

## Slide 26: Example: Now A sends update to B
A
C
1
2
7
B
D
3
1
 | B | C
B | 2 | 8
C | 3 | 7
D | 5 | 8
Node A
Node B
Node C
 | A | B | D
A | 7 | 3 | ∞
B | 9 | 1 | 4
D | ∞ | 4 | 1
Node D
 | B | C
A | 5 | 8
B | 3 | 2
C | 4 | 1
 | A | C | D
A | 2 | 8 | ∞
C | 5 | 1 | 4
D | 7 | 2 | 3
loop:
…
13 else if (update D(B, Y) from A)
14 DA(B,Y) = DA(B,A) + D(A, Y);
15 if (new min. for destination Y)
16 send D(B, Y) to all neighbors
17 forever
DA(B, C) = DA(B,A) + D(A, C) = 2 + 3 = 5
DA(B, D) = DA(B,A) + D(A, D) = 2 + 5 = 7
Where does this 5 come from?
Where does this 7 come from?
What harm does this cause?
Notes: Talk about where the 5 and 7 come from!

## Slide 27: Example: End of 2nd Full Exchange
A
C
1
2
7
B
D
3
1
 | B | C
B | 2 | 8
C | 3 | 7
D | 4 | 8
Node A
 | A | C | D
A | 2 | 4 | 8
C | 5 | 1 | 4
D | 7 | 2 | 3
Node B
Node C
 | A | B | D
A | 7 | 3 | 6
B | 9 | 1 | 3
D | 12 | 3 | 1
Node D
 | B | C
A | 5 | 4
B | 3 | 2
C | 4 | 1
End of 2nd Iteration All nodes knows the best three-hop paths
Assume all send messages at same time

## Slide 28: Example: End of 3rd Full Exchange
A
C
1
2
7
B
D
3
1
 | B | C
B | 2 | 8
C | 3 | 7
D | 4 | 8
Node A
 | A | C | D
A | 2 | 4 | 7
C | 5 | 1 | 4
D | 6 | 2 | 3
Node B
Node C
 | A | B | D
A | 7 | 3 | 5
B | 9 | 1 | 3
D | 11 | 3 | 1
Node D
 | B | C
A | 5 | 4
B | 3 | 2
C | 4 | 1
End of 3rd Iteration: Algorithm Converges!
What route does this 11 represent?
Assume all send messages at same time

## Slide 29: Intuition
Initial state: best one-hop paths
One simultaneous round: best two-hop paths
Two simultaneous rounds: best three-hop paths
…
Kth simultaneous round: best (k+1) hop paths
Must eventually converge
  as soon as it reaches longest best path
…..but how does it respond to changes in cost?
The key: if the starting point is
not the initialization, but some other set of
entries. Convergence could be different!

## Slide 30: DV: Link Cost Changes
 | A | C
A | 4 | 6
C | 9 | 1
Node B
 | A | B
A | 50 | 5
B | 54 | 1
Node C
Link cost changes here
 | A | C
A | 1 | 6
C | 6 | 1
 | A | B
A | 50 | 5
B | 54 | 1
 | A | C
A | 1 | 6
C | 3 | 1
 | A | B
A | 50 | 5
B | 51 | 1
 | A | C
A | 1 | 6
C | 3 | 1
 | A | B
A | 50 | 2
B | 51 | 1
 | B | C
B | 4 | 51
C | 5 | 50
Node A
 | B | C
B | 1 | 51
C | 2 | 50
 | B | C
B | 1 | 51
C | 2 | 50
 | B | C
B | 1 | 51
C | 2 | 50
 | A | C
A | 1 | 3
C | 3 | 1
 | A | B
A | 50 | 2
B | 51 | 1
 | B | C
B | 1 | 51
C | 2 | 50
Stable state
A-B changed
A sends tables to B, C
B sends tables to C
C sends tables to B
A
C
1
4
50
B
1
“good news travels fast”

## Slide 31: DV: Count to Infinity Problem
 | A | C
A | 4 | 6
C | 9 | 1
Node B
 | A | B
A | 50 | 5
B | 54 | 1
Node C
Link cost changes here
 | A | C
A | 60 | 6
C | 65 | 1
 | A | B
A | 50 | 5
B | 54 | 1
 | A | C
A | 60 | 6
C | 110 | 1
 | A | B
A | 50 | 5
B | 101 | 1
 | A | C
A | 60 | 6
C | 110 | 1
 | A | B
A | 50 | 7
B | 101 | 1
 | B | C
B | 4 | 51
C | 5 | 50
Node A
 | B | C
B | 60 | 51
C | 61 | 50
 | B | C
B | 60 | 51
C | 61 | 50
 | B | C
B | 60 | 51
C | 61 | 50
 | A | C
A | 60 | 8
C | 110 | 1
 | A | B
A | 50 | 7
B | 101 | 1
 | B | C
B | 60 | 51
C | 61 | 50
Stable state
A-B changed
A sends tables to B, C
B sends tables to C
C sends tables to B
A
C
1
4
50
B
60
“bad news travels slowly”
(not yet converged)

## Slide 32: DV: Poisoned Reverse
 | A | C
A | 4 | ∞
C | ∞ | 1
Node B
 | A | B
A | 50 | 5
B | 54 | 1
Node C
Link cost changes here
 | A | C
A | 60 | ∞
C | ∞ | 1
 | A | B
A | 50 | 5
B | 54 | 1
 | A | C
A | 60 | ∞
C | 110 | 1
 | A | B
A | 50 | 5
B | ∞ | 1
 | A | C
A | 60 | ∞
C | 110 | 1
 | A | B
A | 50 | 61
B | ∞ | 1
 | B | C
B | 4 | 51
C | 5 | 50
Node A
 | B | C
B | 60 | 51
C | 61 | 50
 | B | C
B | 60 | 51
C | 61 | 50
 | B | C
B | 60 | 51
C | 61 | 50
 | A | C
A | 60 | 51
C | 110 | 1
 | A | B
A | 50 | 61
B | ∞ | 1
 | B | C
B | 60 | 51
C | 61 | 50
Stable state
A-B changed
A sends tables to B, C
B sends tables to C
C sends tables to B
A
C
1
4
50
B
60
If B routes through C to get to A:
  B tells C its (B’s) distance to A is infinite (so C won’t route to A via B)
Note: this converges after C receives another update from B
Notes: Explain full table version of DV in section from the other set of slides.

## Slide 33: A few other inconvenient aspects
What if we use a non-additive metric?
  E.g., maximal capacity
What if routers don’t use the same metric?
  I want low delay, you want low loss rate?
What happens if nodes lie?

## Slide 34: Can You Use Any Metric?
I said that we can pick any metric. Really?
What about maximizing capacity?

## Slide 35: No agreement on metrics?
If the nodes choose their paths according to different criteria, then bad things might happen
Example
  Node A is minimizing latency
  Node B is minimizing loss rate
  Node C is minimizing price
Any of those goals are fine, if globally adopted
  Only a problem when nodes use different criteria
Consider a routing algorithm where paths are described by delay, cost, loss

## Slide 36: What Happens Here?
Low price link
Low loss link
Low delay link
Low loss link
Low delay link
Low price link
Cares about price,
then loss
Cares about delay,
then price
Cares about loss,
then delay
Notes: Figure this out. Break into groups….

## Slide 37: Must agree on loop-avoiding metric
When all nodes minimize same metric
And that metric increases around loops
Then process is guaranteed to converge

## Slide 38: What happens when routers lie?
What if a router claims a 1-hop path to everywhere?
All traffic from nearby routers gets sent there
How can you tell if they are lying?
Can this happen in real life?
  It has, several times….

## Slide 39: Link State vs. Distance Vector
Core idea
  LS: tell all nodes about your immediate neighbors
  DV: tell your immediate neighbors about (your least cost distance to) all nodes

## Slide 40: Link State vs. Distance Vector
LS: each node learns the complete network map; each node computes shortest paths independently and in parallel
DV: no node has the complete picture; nodes cooperate to compute shortest paths in a distributed manner
  LS has higher messaging overhead
  LS has higher processing complexity
  LS is less vulnerable to looping

## Slide 41: Link State vs. Distance Vector
Message complexity
LS: O(NxE) messages;
  N is #nodes; E is #edges
DV: O(#Iterations x E)
  where #Iterations is ideally O(network diameter) but varies due to routing loops or the count-to-infinity problem
Processing complexity
LS: O(N2)
DV: O(#Iterations x N)
Robustness: what happens if router malfunctions?
LS:
  node can advertise incorrect link cost
  each node computes only its own table
DV:
  node can advertise incorrect path cost
  each node’s table used by others; error propagates through network

## Slide 42: Routing: Just the Beginning
Link state and distance-vector are the deployed routing paradigms for intra-domain routing
Next: inter-domain routing (BGP)
  new constraints: policy, privacy
  new solutions: path vector routing
  new pitfalls: truly ugly ones

## Slide 43: What are desirable goals for a routing solution?
“Good” paths (least cost)
Fast convergence after change/failures
  no/rare loops
Scalable
  #messages
  table size
  processing complexity
Secure
Policy
Rich metrics (more later)

## Slide 44: Metrics
Propagation delay
Congestion
Load balance
Bandwidth (available, capacity, maximal, bbw)
Price
Reliability
Loss rate
Combinations of the above
In practice, operators set abstract “weights” (much like our costs); how exactly is a bit of a black art

## Slide 45: Internet Routing
So far, only considered routing within a domain
Many issues can be ignored in this setting because there is central administrative control over routers
  Issues such as autonomy, privacy, policy
But the Internet is more than a single domain

## Slide 46: Recall from Lecture 3
“Interior Routers”
“Border Routers”
“Autonomous System (AS)” or “Domain” Region of a network under a single administrative entity
An “end-to-end” route

## Slide 47: Autonomous Systems (AS)
AS is a network under a single administrative control
  currently over 30,000 ASes
  Think AT&T, France Telecom, IBM, etc.
ASes are sometimes called “domains”.
  Hence, “interdomain routing”
Each AS is assigned a unique identifier
  16 bit AS Number (ASN)

## Slide 48: Routing between ASes
Two key challenges
Scaling
Administrative structure
  Issues of autonomy, policy, privacy

## Slide 49: Recall Also…
to MIT
to UW
UCB
to NYU
Destination | Next Hop
UCB | 4
UW | 5
MIT | 2
NYU | 3
Forwarding Table
111010010
MIT
switch#2
switch#5
switch#3
switch#4

## Slide 50: Scaling
Every router must be able to forward packets to any destination
  Given address, it needs to know “next hop” (table)
Naive: Have an entry for each address
  There would be over 10^8 entries!
  And routing updates per destination!
Any ideas on how to improve scalability?

## Slide 51: Scaling
Every router must be able to forward based on *any* destination address
  Given address, it needs to know “next hop” (table)
Naive: Have an entry for each address
  There would be 10^8 entries!
  And routing updates per destination!
Better: Have an entry for a range of addresses
  But can’t do this if addresses are assigned randomly
Addresses allocation is a big deal!
Host addressing is key to scaling

## Slide 52: Two Key Challenges
Scaling
Administrative structure
  Issues of policy, autonomy, privacy

## Slide 53: Administrative structure shapes Interdomain routing
ASes want freedom to pick routes based on policy
  “My traffic can’t be carried over my competitor’s network”
  “I don’t want to carry A’s traffic through my network”
  Not expressible as Internet-wide “shortest path”!
ASes want autonomy
  Want to choose their own internal routing protocol
  Want to choose their own policy
ASes want privacy
  choice of network topology, routing policies, etc.

## Slide 54: Choice of Routing Algorithm
Link State (LS) vs. Distance Vector (DV)?
LS offers no privacy -- global sharing of all network information (neighbors, policies)
LS limits autonomy -- need agreement on metric, algorithm
DV is a decent starting point
  per-destination advertisement gives providers a hook for finer-grained control over whether/which routes to advertise
  but DV wasn’t designed to implement policy
  and is vulnerable to loops if shortest paths not taken
The “Border Gateway Protocol” (BGP) extends distance-vector ideas to accommodate policy

## Slide 55: Next week
Addressing
BGP
  today: context and key ideas
  next lecture: details and issues