## Slide 1: CS 353 Interdomain Routing BGP
Spring 2016
Alefiya Hussain

## Slide 2: Recall… Autonomous Systems (AS)
AS is a network under a single administrative control
  ASes are called “domains”.
  Hence, “interdomain routing”
Two key challenges
Scaling
Administrative structure
  Issues of autonomy, policy, privacy

## Slide 3: Recall…Scaling
Every router must be able to forward based on *any* destination address
  Given address, it needs to know “next hop” (table)
Naive: Have an entry for each address
  There would be 10^8 entries with the classic addressing scheme!
  And routing updates per destination!
Better: Have an entry for a range of addresses
  But can’t do this if addresses are assigned randomly
Addresses allocation is key!

## Slide 4
“Interior Routers”
“Autonomous System (AS)” or “Domain” Region of a network under a single administrative entity
“Border Routers”

## Slide 5: Topology and routes shaped by the business relationships between ASes
Three basic relationships between two ASes
  A is a customer of B
  A is a provider of B
  A and B are peers
Business implications
  customer pays provider
  peers don’t pay each other

## Slide 6: Routing Follows the Money!
traffic allowed
traffic not allowed
A
B
C
D
E
F
Q
Pr
Cu
Peer
Peer

## Slide 7: Interdomain Routing: The Basics
Destinations are IP prefixes (12.0.0.0/8)
Nodes are Autonomous Systems (ASes)
  Internals of each AS are hidden
Links represent both physical links and business relationships
BGP (Border Gateway Protocol) is the Interdomain routing protocol
  Implemented by AS border routers

## Slide 8: BGP: Basic Idea
Each AS selects the “best” route it hears advertised for a prefix
An AS advertises its best routes to one or more IP prefixes
Where have heard this story before!
Notes: Arrows are routing message

## Slide 9: BGP inspired by Distance Vector
Per-destination route advertisements
No global sharing of network topology information
Iterative and distributed convergence on paths
With four crucial differences!

## Slide 10: Differences between BGP and DV (1) not picking shortest path routes
BGP selects the best route based on policy, not shortest distance (least cost)
How do we avoid loops?
2
3
1
Node 2 may prefer “2, 3, 1” over “2, 1”

## Slide 11: Differences between BGP and DV (2) path-vector routing
Key idea: advertise the entire path
  Distance vector: send distance metric per destination
  Path vector: send the entire path for each destination
C
B
A
d
“d: path (B,A)”
“d: path (A)”
data traffic
data traffic

## Slide 12: Differences between BGP and DV (2) path-vector routing
Key idea: advertise the entire path
  Distance vector: send distance metric per destination
  Path vector: send the entire path for each destination
Benefits
  loop avoidance is easy

## Slide 13: Differences between BGP and DV (3) Selective route advertisement
For policy reasons, an AS may choose not to advertise a route to a destination
Hence, reachability is not guaranteed even if graph is connected
AS 2
AS 3
AS 1
Example: AS#2 does not want to carry traffic between AS#1 and AS#3

## Slide 14: Differences between BGP and DV (4) BGP may aggregate routes
For scalability, BGP may aggregate routes for different prefixes
AT&T a.0.0.0/8
ISI a.b.0.0/16
USC a.c.0.0/16
a.*.*.* is this way
foo.com a.d.0.0/16
a.b.*.* is this way
a.c.*.* is this way
a.d.*.* is this way

## Slide 15: BGP four difference are:
Policy drives next hop in path
Path vector routing with full path advertised
Selective route advertisement can lead to disconnectedness
BGP may aggregate routes

## Slide 16: BGP: Outline
BGP policy
  typical policies, how they’re implemented
BGP protocol details
Issues with BGP

## Slide 17: Policy imposed in how routes are selected and exported
Selection: Which path to use?
  controls whether/how traffic leaves the network
Export: Which path to advertise?
  controls whether/how traffic enters the network
Can reach 128.3/16
Route selection
A
P
C
B
Q
Route export
Notes: Arrows: routing messages!

## Slide 18: Typical Selection Policy
In decreasing order of priority
  make/save money (send to customer > peer > provider)
  maximize performance (smallest AS path length)
  minimize use of my network bandwidth (“hot potato”)
  …
BGP uses “route attributes” for priroty
  LOCALPREF
  ASPATH
  MED

## Slide 19: Typical Export Policy
Destination prefix advertised by… | Export route to…
Customer | Everyone (providers, peers, other customers)
Peer | Customers
Provider | Customers
We’ll refer to these as the “Gao-Rexford” rules
(common -- but not required! -- practice!)

## Slide 20: BGP: Today
BGP policy
  typical policies, how they’re implemented
BGP protocol details
BGP issues

## Slide 21: Who speaks BGP?
Border router
Internal router
Border routers at an Autonomous System

## Slide 22: What does “speak BGP” mean?
Implement the BGP protocol standard
  read more here: http://tools.ietf.org/html/rfc4271
Specifies what messages to exchange with other BGP “speakers”
  message types (e.g., route advertisements, updates)
  message syntax
And how to process these messages
  e.g., “when you receive a BGP update, do…. “
  follows BGP state machine in the protocol spec + policy decisions, etc.

## Slide 23: BGP “sessions”
A border router speaks BGP with border routers in other ASes
“eBGP session”

## Slide 24: BGP “sessions”
A border router speaks BGP with other (interior and border) routers in its own AS
“iBGP session”

## Slide 25: eBGP, iBGP, IGP
eBGP: BGP sessions between border routers in different ASes
  Learn routes to external destinations
iBGP: BGP sessions between border routers and other routers within the same AS
  distribute externally learned routes internally
IGP: “Interior Gateway Protocol” = Intradomain routing protocol
  provide internal reachability
  e.g., OSPF, RIP

## Slide 26: Some Border Routers Don’t Need BGP
Customer that connects to a single upstream ISP
  The ISP can advertise prefixes into BGP on behalf of customer
  … and the customer can simply default-route to the ISP
Provider
Customer
Install default routes pointing to Provider
Install routes 130.132.0.0/16 pointing to Customer
130.132.0.0/16

## Slide 27: Putting the pieces together
Provide internal reachability (IGP)
Learn routes to external destinations (eBGP)
Distribute externally learned routes internally (iBGP)
Travel shortest path to egress (IGP)
6
2
4
9
2
1
3
3

## Slide 28: Basic Messages in BGP
Open
  Establishes BGP session
  BGP uses TCP [will make sense in 1-2weeks]
Notification
  Report unusual conditions
Update
  Inform neighbor of new routes
  Inform neighbor of old routes that become inactive
Keepalive
  Inform neighbor that connection is still viable

## Slide 29: Route Updates
Format <IP prefix: route attributes>
  attributes describe properties of the route
Two kinds of updates
  announcements: new routes or changes to existing routes
  withdrawal: remove routes that no longer exist

## Slide 30: Route Attributes
Routes are described using attributes
  Used in route selection/export decisions
Some attributes are local
  i.e., private within an AS, not included in announcements
Some attributes are propagated with eBGP route announcements
There are many standardized attributes in BGP
  We will discuss a few

## Slide 31: Attributes (1): ASPATH
Carried in route announcements
Vector that lists all the ASes a route advertisement has traversed (in reverse order)
AS 7018
AT&T
AS 12654
128.112.0.0/16
AS path = 7018 88
AS 88
Princeton, 128.112/16
IP prefix = 128.112.0.0/16
AS path = 88

## Slide 32: Attributes (2): LOCAL PREF
“Local Preference”
Used to choose between different AS paths
The higher the value the more preferred
Local to an AS; carried only in iBGP messages
AS4
AS2
AS3
AS1
140.20.1.0/24
BGP table at AS4:

## Slide 33: Example: iBGP and LOCAL PREF
Both routers prefer the path through AS 2 on the left
I-BGP
AS 4
AS 3
Local Pref = 100
Local Pref = 90
AS 2
AS1

## Slide 34: Attributes (3) : MED
“Multi-Exit Discriminator”
Used when ASes are interconnected via 2 or more links to specify how close a prefix is to the link it is announced on
Lower is better
AS announcing prefix sets MED
AS receiving prefix (optionally!) uses MED to select link
Link B
Link A
MED=10
MED=50
AS1
AS2
AS3
destination prefix

## Slide 35: Attributes (4): IGP cost
Used for hot-potato routing
  Each router selects the closest egress point based on the path cost in intra-domain protocol
hot potato
A
B
C
D
G
E
F
4
5
3
9
3
4
10
8
8
A
B
dst

## Slide 36: IGP may conflict with MED
Dsf
A
B
MED=100
MED=500

## Slide 37: Typical Selection Policy
In decreasing order of priority
  make/save money (send to customer > peer > provider)
  maximize performance (smallest AS path length)
  minimize use of my network bandwidth (“hot potato”)
  …
  …

## Slide 38: Using Attributes
Rules for route selection in priority order
Priority | Rule | Remarks
1 | LOCAL PREF | Pick highest LOCAL PREF
2 | ASPATH | Pick shortest ASPATH length
3 | MED | Lowest MED preferred
4 | eBGP > iBGP | Did AS learn route via eBGP (preferred) or iBGP?
5 | iBGP path | Lowest IGP cost to next hop (egress router)
6 | Router ID | Smallest next-hop router’s IP address as tie-breaker

## Slide 39: BGP UPDATE Processing
Best Route
Selection
Apply Import
Policies
Best Route
Table
Apply Export
Policies
forwarding
Entries
BGP
Updates
BGP
Updates
IP Forwarding Table
Open ended programming.
Constrained only by vendor configuration language
Data plane
Control plane
Data packets
Data packets

## Slide 40: BGP: Today
BGP policy
  typical policies, how they’re implemented
BGP protocol details
BGP issues

## Slide 41: Issues with BGP
Reachability
Security
Convergence
Performance
Anomalies

## Slide 42: Reachability
In normal routing, if graph is connected then reachability is assured
With policy routing, this does not always hold
AS 2
AS 3
AS 1
Provider
Provider
Customer

## Slide 43: Security
An AS can claim to serve a prefix that they actually don’t have a route to (blackholing traffic)
  Problem not specific to policy or path vector
  Important because of AS autonomy
  Fixable: make ASes “prove” they have a path
Note: AS may forward packets along a route different from what is advertised
  Tell customers about fictitious short path…
  Much harder to fix!

## Slide 44: Convergence
Result: If all AS policies follow “Gao-Rexford” rules, that is, are valley free,
  BGP is guaranteed to converge
  But all may not follow..
For arbitrary policies, BGP may fail to converge!

## Slide 45: Example of Policy Oscillation
1
2
3
1 3 0
1 0
3 2 0
3 0
2 1 0
2 0
0
“1” prefers “1 3 0”
over “1 0” to reach “0”

## Slide 46: Step-by-Step of Policy Oscillation
Initially: nodes 1, 2, 3 know only shortest path to 0
1
2
3
1 3 0
1 0
3 2 0
3 0
2 1 0
2 0
0

## Slide 47
1 advertises its path 1 0 to 2
1
2
3
1 3 0
1 0
3 2 0
3 0
2 1 0
2 0
0
advertise: 1 0
Step-by-Step of Policy Oscillation

## Slide 48
1
2
3
1 3 0
1 0
3 2 0
3 0
2 1 0
2 0
0
Step-by-Step of Policy Oscillation

## Slide 49
1
2
3
1 3 0
1 0
3 2 0
3 0
2 1 0
2 0
0
advertise: 3 0
3 advertises its path 3 0 to 1
Step-by-Step of Policy Oscillation

## Slide 50
1
2
3
1 3 0
1 0
3 2 0
3 0
2 1 0
2 0
0
Step-by-Step of Policy Oscillation

## Slide 51
1
2
3
1 3 0
1 0
3 2 0
3 0
2 1 0
2 0
0
withdraw: 1 0
1 withdraws its path 1 0 from 2
Step-by-Step of Policy Oscillation

## Slide 52
1
2
3
1 3 0
1 0
3 2 0
3 0
2 1 0
2 0
0
Step-by-Step of Policy Oscillation

## Slide 53
1
2
3
1 3 0
1 0
3 2 0
3 0
2 1 0
2 0
0
advertise: 2 0
2 advertises its path 2 0 to 3
Step-by-Step of Policy Oscillation

## Slide 54
1
2
3
1 3 0
1 0
3 2 0
3 0
2 1 0
2 0
0
Step-by-Step of Policy Oscillation

## Slide 55
1
2
3
1 3 0
1 0
3 2 0
3 0
2 1 0
2 0
0
withdraw: 3 0
3 withdraws its path 3 0 from 1
Step-by-Step of Policy Oscillation

## Slide 56
1
2
3
1 3 0
1 0
3 2 0
3 0
2 1 0
2 0
0
Step-by-Step of Policy Oscillation

## Slide 57
1
2
3
1 3 0
1 0
3 2 0
3 0
2 1 0
2 0
0
1 advertises its path 1 0 to 2
Step-by-Step of Policy Oscillation
advertise: 1 0

## Slide 58
1
2
3
1 3 0
1 0
3 2 0
3 0
2 1 0
2 0
0
Step-by-Step of Policy Oscillation

## Slide 59
1
2
3
1 3 0
1 0
3 2 0
3 0
2 1 0
2 0
0
withdraw: 2 0
2 withdraws its path 2 0 from 3
Step-by-Step of Policy Oscillation

## Slide 60
1
2
3
1 3 0
1 0
3 2 0
3 0
2 1 0
2 0
0
We are back to where we started!
Step-by-Step of Policy Oscillation

## Slide 61: Convergence
Result: If all AS policies follow “Gao-Rexford” rules, BGP is guaranteed to converge (safety)
For arbitrary policies, BGP may fail to converge!
Why should this trouble us?

## Slide 62: Performance Nonissues
Internal routing (non)
  Domains typically use “hot potato” routing
  Not always optimal, but economically expedient
Policy not about performance (non)
  So policy-chosen paths aren’t shortest
AS path length can be misleading (non)
  20% of paths inflated by at least 5 router hops
Notes: Lesson: not being optimal: who cares
Not being connected: we all care!!

## Slide 63: Performance (example)
AS path length can be misleading
  An AS may have many router-level hops
AS 4
AS 3
AS 2
AS 1
BGP says that
path 4 1 is better
than path 3 2 1

## Slide 64: Real Performance Issue: Slow convergence
BGP outages are biggest source of Internet problems
Labovitz et al. SIGCOMM’97
    10% of routes available less than 95% of time
    Less than 35% of routes available 99.99% of the time
Labovitz et al. SIGCOMM 2000
    40% of path outages take 30+ minutes to repair
But most popular paths are very stable
Notes: Lesson: not being optimal: who cares
Not being connected: we all care!!

## Slide 65: BGP Misconfigurations
BGP protocol is both bloated and underspecified
  lots of attributes
  lots of leeway in how to set and interpret attributes
  necessary to allow autonomy, diverse policies
  but also gives operators plenty of rope
Much of this configuration is manual and ad hoc
And the core abstraction is fundamentally flawed
  disjoint per-router configuration to effect AS-wide policy
  now strong industry interest in changing this! [later: SDN]
Notes: Lesson: not being optimal: who cares
Not being connected: we all care!!

## Slide 66: BGP: How did we get here?
BGP was designed for a different time
  before commercial ISPs and their needs
  before address aggregation
  before multi-homing
We don’t get a second chance: `clean slate’ designs virtually impossible to deploy
1989 : BGP-1 [RFC 1105]
  Replacement for EGP (1984, RFC 904)
1990 : BGP-2 [RFC 1163]
1991 : BGP-3 [RFC 1267]
1995 : BGP-4 [RFC 1771]
  Support for Classless Interdomain Routing (CIDR)
Notes: Lesson: not being optimal: who cares
Not being connected: we all care!!

## Slide 67: Next Time.
Wrap up the network layer!
  the IPv4 header
  Fragmentation
  End to end example