## Slide 1: Network Layer: Some Missing Pieces
Alefiya Hussain
Spring 2016

## Slide 2: Where Are We
Context (History, Goals, Principles, etc.)
  Done
Fundamental Challenges (Routing, Reliable Trans.)
  Done
Today’s Internet
  IP: Done
  Addressing: Done
  IP Header: Done
  IPv6, ICMP, LMP: Today
  Homework Review: Thursday
  Midterm: Friday

## Slide 3: Recall: End-Host How to Handle Packet
Application
Transport
Network
Data link
Physical
SMTP
HTTP
DNS
NTP
TCP
UDP
IP
Ethernet
FDDI
PPP
optical
copper
radio
PSTN

## Slide 4: Recall: Layer Encapsulation
transport
network
network
link
app
Alice
Bob
network
Router
Notes: Deepest level most header

## Slide 5: Review of Addressing
  Notation: dotted quad (set of four 8-bit numbers)
  16.45.231.117=00010000|00101101|11100111|01110101
Structure: (prefix, suffix)
  Network component (prefix)
  Host component (suffix)
  Use “slash” notation to denote the network component
    /8 means prefix is first 8 bits
Routers only look at network component
  L2 networks mostly look at host component

## Slide 6: History of Addressing Schemes
Original: prefix of length 8 (all addresses in /8s)
Classful: opening bits determined length of prefix
  0 meant /8
  10 meant /16
  110 meant /24
  1110 meant mcast
  1111 meant experimental
Classless (CIDR): explicit mask defines prefix

## Slide 7: CIDR Addressing
IP Address : 12.4.2.1 IP Mask: 255.254.0.0
00001100
00000100
00000010
00000001
11111111
11111110
00000000
00000000
Address
Mask
for hosts
Network Prefix
Use two 32-bit numbers to represent a network location
Address + Mask
Notes: What is slash notation for this prefix?

## Slide 8: CIDR Prefixes
Prefix: 12.4.0.0 IP Mask: 255.254.0.0
00001100
00000100
00000000
00000000
11111111
11111110
00000000
00000000
Address
Mask
for hosts
Network Prefix
Use two 32-bit numbers to represent a network prefix
Address + Mask
Written as 12.4.0.0/15 or 12.4/15
Notes: What is slash notation for this prefix?

## Slide 9: Let’s take a quick look at the IPv6 header…

## Slide 10: IPv6
Motivated by address exhaustion
  Addresses four times as big
Steve Deering focused on simplifying IP
  got rid of all fields that were not absolutely necessary
  “spring cleaning” for IP
Result is an elegant, if unambitious, protocol

## Slide 11: What “clean up” would you do?
4-bit
Version
4-bit
Header
Length
8-bit
Type of Service
16-bit Total Length (Bytes)
16-bit Identification
3-bit
Flags
13-bit Fragment Offset
8-bit Time to
Live (TTL)
8-bit Protocol
16-bit Header Checksum
32-bit Source IP Address
32-bit Destination IP Address
Options (if any)
Payload

## Slide 12: IPv4 and IPv6 Header Comparison
Version | IHL | Type of Service | Total Length |  | 
Identification |  |  | Flags | Fragment Offset | 
Time to Live |  | Protocol | Header Checksum |  | 
Source Address |  |  |  |  | 
Destination Address |  |  |  |  | 
Options |  |  |  |  | Padding
Version | Traffic Class | Flow Label |  | 
Payload Length |  |  | Next Header | Hop Limit
Source Address |  |  |  | 
Destination Address |  |  |  | 
IPv4
IPv6
Field name kept from IPv4 to IPv6
Fields not kept in IPv6
Name & position changed in IPv6
New field in IPv6

## Slide 13: Philosophy of Changes
Don’t deal with problems: leave to ends
  Eliminated fragmentation
  Eliminated checksum
  Why retain TTL?
Simplify handling:
  New options mechanism (uses next header approach)
  Eliminated header length
    Why couldn’t IPv4 do this?
Provide general flow label for packet
  Not tied to semantics
  Provides great flexibility

## Slide 14: Missing Pieces

## Slide 15: Where are we?
We have covered the “fundamentals”
  How to deliver packets (routing)
  How to build reliable delivery on an unreliable network
With this, we could build a decent network
How can we send/receive on the network
  Too many missing pieces
We now want to identify those pieces
  Will guide what we cover rest of semester

## Slide 16: Scenario: Joan Wants Her Music
Joan is sitting in her dorm room, with a laptop
  Wants to watch a video on youtube
What needs to happen to make this possible?
  Not in terms of today’s protocols…
  ……but in terms of basic tasks

## Slide 17: What Are The Steps Involved?
Accessing the network from laptop
  Wireless or ethernet
  Network management (someone needs to make it work)
Mapping “real world name” to “network name”
Mapping network name to location
Download content from location
Notes: Stop for input!

## Slide 18: What Are The Steps Involved?
Accessing the network from laptop
  Wireless or ethernet
  Network management (someone needs to make it work)
Mapping “real world name” to “network name”
Mapping network name to location
Download content from location

## Slide 19: Access Networks
If access network is “switched”, we understand it
  Just like any other packet-switched network
If the access network is shared medium, then we need to figure out how to share the medium
  Wireless
  Classical ethernet

## Slide 20: Media Access Control (MAC)
Carrier sense: (CSMA)
  Don’t send if someone else is sending
Collision detection: (CD)
  Stop if you detect someone else was also sending
Collision avoidance: (CA)
  How to arrange transmissions so that they don’t collide

## Slide 21: What Are The Steps Involved?
Accessing the network from laptop
  Wireless or ethernet
  Network management (need to make it work)
Mapping “real world name” to “network name”
Mapping network name to location
Download content from location
Addressing general security concerns
  Verifying that this is the right content
  And that no one can tell what she’s downloading
Notes: Stop for input!

## Slide 22: Network Management
Control how dorm network interconnects to Internet
  Intradomain routing
  Interdomain routing
Keep unwanted traffic off network
  Firewalls and access control
Share limited number of public addresses in dorm
  NAT
Keep links from overloading
  Traffic engineering through rate limiting
Autoconfiguration
  DHCP

## Slide 23: What Are The Steps Involved?
Accessing the network from laptop
  Wireless or ethernet
  Network management (someone needs to make it work)
Mapping “real world name” to “network name”
Mapping network name to location
Download content from location
Addressing general security concerns
  Verifying that this is the right content
  And that no one can tell what she’s downloading
Notes: Stop for input!

## Slide 24: “Real World Name” to “Network Name”
Joan knows what youtube video she wants
Doesn’t know how to tell network what she wants
Needs to map “real world name” (youtube.com)….
…..to a name that the infrastructure understands
  We will call this the “network name” but this isn’t a name at the IP level, but another portion of the infrastructure
Search engine!
  Maps keywords to URL
How can we do this?

## Slide 25: What is a “Network Name”?
HTTP://www.youtube.com/watch?v=hUJagb7hL0E
HTTP is host-to-host protocol
www.youtube.com is a “host name”
  Widely replicated, but still represents a host
  Need to convert youtube to IP address
watch?v=hUJagb7hL0E is meaningful to youtube

## Slide 26: What Are The Steps Involved?
Accessing the network from laptop
  Wireless or ethernet
  Network management (someone needs to make it work)
Mapping “real world name” to “network name”
Mapping network name to location
Download content from location
Addressing general security concerns
  Verifying that this is the right content
  And that no one can tell what she’s downloading
Notes: Stop for input!

## Slide 27: Map Network Name to Location
“Name resolution” converts name to location
  Location is IP address of host
We would like location to be nearby copy
  Speeds up download
  Reduce load on backbone and access networks

## Slide 28: How is this done today?
Name resolution: Domain Name System (DNS)
  Hand in a hostname, get back an IP address
Nearby copy of the data?
  CDNs: content distribution networks (like Akamai)
  3/22 : Talk from Akamai on CDNs
P2P systems can also point you to nearby content

## Slide 29: What Are The Steps Involved?
Accessing the network from laptop
  Wireless or ethernet
  Network management (someone needs to make it work)
Mapping “real world name” to “network name”
Mapping network name to location
Download content from location
Notes: Stop for input!

## Slide 30: Download Data from Location
Need a reliable transfer protocol: TCP
  Must share network with others: congestion control
But must be able to use URL to retrieve content
  Need higher-level protocol like HTTP to coordinate

## Slide 31: What Are The Steps Involved?
Accessing the network from laptop
  Wireless or ethernet
  Network management (someone needs to make it work)
Mapping “real world name” to “network name”
Mapping network name to location
Download content from location
Security?
Notes: Stop for input!

## Slide 32: Ensuring Security
Privacy: prevent sniffers from knowing what she downloaded (“it was for CS353, I promise!”)
Integrity: ensure data wasn’t tampered with during its trip through network
Provenance: ensure that music actually came from the youtube company (and not some imposter)

## Slide 33: Scenario Requires
Media Access Control
Network Routing
Naming and name resolution
Content distribution networks
And perhaps P2P
TCP and Congestion control
HTTP
Security..

## Slide 34
How does Joan’s laptop get access to the Internet?

## Slide 35
Link Hdr
IP Hdr
IP Data
35
IP Hdr
IP Datagram
Network
Link
Transport
Application
Payload
Link Data
Link
Frame
Host IP: 171.67.76.65
Interface: 00:13:72:4C:D9:6a
Layers of Addresses

## Slide 36: The Addressing Problem
A
B
USC gateway
192.168.0.5
171.43.22.5
Interface: 3:3:3:3:3:3
Interface: 9:9:9:9:9:9

## Slide 37: Addressing and Encapsulation
A
B
gateway
192.168.0.5
192.168.0.1
171.43.22.8
171.43.22.5
Interface: 3:3:3:3:3:3
Interface: 00:13:72:AA:BB:6a
Interface: 9:9:9:9:9:9
Interface: 00:13:72:AA:BB:7a

## Slide 38: Example Addressing
A
B
gateway
192.168.0.5
192.168.0.1
Interface: 00:13:72:AA:BB:6a
192.168.0.6
C
192.168.0.7
Internet

## Slide 39: Address Translation Protocol (ARP)
Map IP addresses into physical addresses
  destination host
  next hop router
Techniques
  encode physical address in host part of IP address
  table-based
ARP (Address Resolution Protocol)
  table of IP to physical address bindings
  broadcast request if IP address not in table
  target machine responds with its physical address
  table entries are discarded if not refreshed

## Slide 40: ARP Packet Format (RFC 826)
  HardwareType: type of physical network (e.g., Ethernet)
  ProtocolType: type of higher layer protocol (e.g., IP)
  HLEN & PLEN: length of physical and protocol addresses
  Operation: request or response
  Source/Target Physical/Protocol addresses
48bits
48bits

## Slide 41
How did Joan’s laptop get the IP address in the dorm?

## Slide 42: Configuration
A
B
gateway
192.168.0.5
192.168.0.1
Interface: 00:13:72:AA:BB:6a
192.168.0.6
C
192.168.0.7
Internet
Home
network

## Slide 43: Host Configurations
  Ethernet addresses configured into network by manufacturer and they are unique
  IP addresses must be unique on a given internetwork but also must reflect the structure of the internetwork
  Most host Operating Systems provide a way to manually configure the IP information for the host
  Drawbacks of manual configuration
    A lot of work to configure all the hosts in a large network
    Configuration process is error-prune
  Automated Configuration Process is required

## Slide 44: Dynamic Host Configuration Protocol (DHCP)
DHCP server is responsible for providing configuration information to hosts
There is at least one DHCP server for an administrative domain
DHCP server maintains a pool of available addresses

## Slide 45: DHCP
Newly booted or attached host sends DHCPDISCOVER message to a special IP address (255.255.255.255)
DHCP relay agent unicasts the message to DHCP server and waits for the response

## Slide 46
How can we get to youtube?
http://youtube.com  IP address?

## Slide 47: DNS

## Slide 48: Internet Names & Addresses
Machine addresses: e.g., 128.125.253.146
  router-usable labels for machines
  conforms to network structure (the “where”)
Machine names: e.g., www.usc.edu
  human-usable labels for machines
  conforms to organizational structure (the “who”)
The Domain Name System (DNS) is how we map from one to the other

## Slide 49: DNS: History
Initially all host-address mappings were in a hosts.txt file (in /etc/hosts):
  Maintained by the Stanford Research Institute (SRI)
  Changes were submitted to SRI by email
  New versions of hosts.txt periodically FTP’d from SRI
  An administrator could pick names at their discretion
As the Internet grew this system broke down:
  SRI couldn’t handle the load; names were not unique; hosts had inaccurate copies of hosts.txt
The Domain Name System (DNS) was invented to fix this

## Slide 50: Goals
No naming conflicts (uniqueness)
Scalable
  many names
  (secondary) frequent updates
Distributed, autonomous administration
  Ability to update my own (machines’) names
  Don’t have to track everybody’s updates
Highly available
Lookups are fast
Non-goal?: perfect consistency

## Slide 51: Key idea: Hierarchy
Three intertwined hierarchies
  Hierarchical namespace
    As opposed to original flat namespace
  Hierarchically administered
    As opposed to centralized
  (Distributed) hierarchy of servers
    As opposed to centralized storage

## Slide 52: Hierarchical Namespace
“Top Level Domains” are at the top
Domains are subtrees
  E.g: .edu, usc.edu,
Name is leaf-to-root path
  nsl.ee.usc.edu
Depth of tree is arbitrary (limit 128)
Name collisions trivially avoided
  each domain is responsible
root
edu
com
gov
mil
org
net
uk
fr
usc
ucla
ee
cs
nsl
…

## Slide 53: Hierarchical Administration
root
edu
com
gov
mil
org
net
uk
fr
ucla
ee
cs
nsl
root
edu
com
gov
mil
org
net
uk
fr
usc
A zone corresponds to an administrative authority that is responsible for that portion of the hierarchy
E.g., USC controls names: *.usc.edu and *.cs.usc.edu
E.g., EE controls names: *.ee.usc.edu

## Slide 54: Server Hierarchy
Top of hierarchy: Root servers
  Location hardwired into other servers
Next Level: Top-level domain (TLD) servers
  .com, .edu, etc.
  Managed professionally
Bottom Level: Authoritative DNS servers
  Actually store the name-to-address mapping
  Maintained by the corresponding administrative authority

## Slide 55: Server Hierarchy
Each server stores a (small!) subset of the total DNS database
An authoritative DNS server stores “resource records” for all DNS names in the domain that it has authority for
Each server needs to know other servers that are responsible for the other portions of the hierarchy
  Every server knows the root
  Root server knows about all top-level domains

## Slide 56: DNS Root
Located in Virginia, USA
How do we make the root scale?
Verisign, Dulles, VA

## Slide 57: DNS Root Servers
13 root servers (labeled A-M; see http://www.root-servers.org/)
B USC-ISI Marina del Rey, CA
L ICANN Los Angeles, CA
E NASA Mt View, CA
F Internet Software
Consortium
Palo Alto, CA
I Autonomica, Stockholm
K RIPE London
M WIDE Tokyo
A Verisign, Dulles, VA
C Cogent, Herndon, VA
D U Maryland College Park, MD
G US DoD Vienna, VA
H ARL Aberdeen, MD
J Verisign

## Slide 58: DNS Root Servers
B USC-ISI Marina del Rey, CA
L ICANN Los Angeles, CA
E NASA Mt View, CA
F Internet Software
Consortium,
Palo Alto, CA
(and 37 other locations)
I Autonomica, Stockholm (plus 29 other locations)
K RIPE London (plus 16 other locations)
M WIDE Tokyo
plus Seoul, Paris, San Francisco
A Verisign, Dulles, VA
C Cogent, Herndon, VA (also Los Angeles, NY, Chicago)
D U Maryland College Park, MD
G US DoD Vienna, VA
H ARL Aberdeen, MD
J Verisign (21 locations)
13 root servers (labeled A-M; see http://www.root-servers.org/)
Replicated via any-casting

## Slide 59: Anycast in a nutshell
Routing finds shortest paths to destination
If several locations are given the same address, then the network will deliver the packet to the closest location with that address
This is called “anycast”
  Very robust
  Requires no modification to routing algorithms

## Slide 60: Using DNS (Client/App View)
Two components
  Local DNS servers
  Resolver software on hosts
Local DNS server (“default name server”)
  Usually near the endhosts that use it
  Hosts configured with local server address (e.g., /etc/resolv.conf) or learn server via a host configuration protocol (e.g., DHCP)
Client application
  Obtain DNS name (e.g., from URL)
  Do gethostbyname() to trigger DNS request to its local DNS server

## Slide 61: How Does Resolution Happen?
requesting host
cis.poly.edu
gaia.cs.umass.edu
root DNS server
local DNS server
dns.poly.edu
1
2
3
4
5
6
authoritative DNS server
dns.cs.umass.edu
7
8
TLD DNS server
Host at cis.poly.edu wants IP address for gaia.cs.umass.edu

## Slide 62: Recursive vs. Iterative Queries
Recursive query
  Ask server to get answer for you
  E.g., request 1 and response 8
Iterative query
  Ask server who to ask next
  E.g., all other request-response pairs
requesting host
cis.poly.edu
root DNS server
local DNS server
dns.poly.edu
1
2
3
4
5
6
authoritative DNS server
dns.cs.umass.edu
7
8
TLD DNS server
Notes: Most common case: this mixed usage: host to local: recursive; local to all: iterative

## Slide 63: Inserting Resource Records into DNS
Example: just created company “FooBar”
Get a block of address space from ISP
  Say 212.44.9.128/25
Register foobar.com at registrar (e.g., Network Solutions)
  Provide registrar with names and IP addresses of your authoritative name server (primary and secondary)
  Registrar inserts RR pairs into the .com TLD server:
    (foobar.com, dns1.foobar.com, NS)
    (dns1.foobar.com, 212.44.9.129, A)
You store appropriate records in your server dns1.foobar.com:
  e.g., type A record for www.foobar.com
  e.g., type MX record for foobar.com

## Slide 64
How can we get the content on to Joan’s laptop?
http://youtube.com?watch=xyxtyw13 render in browsers?

## Slide 65: The Web

## Slide 66: The Web – Precursor
1967, Ted Nelson, Xanadu:
  A world-wide publishing network that would allow information to be stored not as separate files but as connected literature
  Owners of documents would be automatically paid via electronic means for the virtual copying of their documents
Coined the term “Hypertext”
Ted Nelson

## Slide 67: The Web – History
World Wide Web (WWW): a distributed database of “pages” linked through Hypertext Transport Protocol (HTTP)
  First HTTP implementation - 1990
    Tim Berners-Lee at CERN
  HTTP/0.9 – 1991
    Simple GET command for the Web
  HTTP/1.0 –1992
    Client/Server information, simple caching
  HTTP/1.1 - 1996
Tim Berners-Lee

## Slide 68: Web Components
Infrastructure:
  Clients
  Servers
Content:
  URL: naming content
  HTML: formatting content
Protocol for exchanging information: HTTP

## Slide 69: Uniform Record Locator (URL)
protocol://host-name[:port]/directory-path/resource
Extend the idea of hierarchical hostnames to include anything in a file system
  http://www.isi.edu/~hussain/
Extend to program executions as well…
  http://us.f413.mail.yahoo.com/ym/ShowLetter?box=%40B%40Bulk&MsgId=2604_1744106_29699_1123_1261_0_28917_3552_1289957100&Search=&Nhead=f&YY=31454&order=down&sort=date&pos=0&view=a&head=b
  Server side processing can be incorporated in the name

## Slide 70: Uniform Record Locator (URL)
protocol://host-name[:port]/directory-path/resource
protocol: http, ftp, https, smtp, rtsp, etc.
hostname: DNS name, IP address
port: defaults to protocol’s standard port; e.g. http: 80 https: 443
directory path: hierarchical, reflecting file system
resource: Identifies the desired resource

## Slide 71: Web and DNS
URLs use hostnames
Thus, content names are tied to specific hosts
Makes persistence of content difficult!

## Slide 72: Hyper Text Transfer Protocol (HTTP)
Client-server architecture
  server is “always on” and “well known”
  clients initiate contact to server
Synchronous request/reply protocol
  Runs over TCP, Port 80
Stateless
ASCII format

## Slide 73: Steps in HTTP Request/Response
Client
Server
TCP Syn
TCP syn + ack
TCP ack + HTTP GET
.
.
.
Establish
connection
Request
response
Client
request
Close connection

## Slide 74: Client-to-Server Communication
GET /somedir/page.html HTTP/1.1
Host: www.someschool.edu
User-agent: Mozilla/4.0
Connection: close
Accept-language: fr
(blank line)
HTTP Request Message
  Request line: method, resource, and protocol version
  Request headers: provide information or modify request
  Body: optional data (e.g., to “POST” data to the server)
request line
header
lines
carriage return line feed
indicates end of message

## Slide 75: Server-to-Client Communication
HTTP Response Message
  Status line: protocol version, status code, status phrase
  Response headers: provide information
  Body: optional data
HTTP/1.1 200 OK
Connection close
Date: Thu, 06 Aug 2006 12:00:15 GMT
Server: Apache/1.3.0 (Unix)
Last-Modified: Mon, 22 Jun 2006 ...
Content-Length: 6821
Content-Type: text/html
(blank line)
data data data data data ...
status line
(protocol, status code, status phrase)
header lines
data
e.g., requested HTML file

## Slide 76: Performance Goals
User
  fast downloads (not identical to low-latency commn.!)
  high availability
Content provider
  happy users (hence, above)
  cost-effective infrastructure
Network (secondary)
  avoid overload

## Slide 77: Improving HTTP Performance: Caching: Where?
Baseline: Many clients transfer same information
  Generate unnecessary server and network load
  Clients experience unnecessary latency
Server
Clients
Tier-1 ISP
ISP-1
ISP-2

## Slide 78: Improving HTTP Performance: Caching with Reverse Proxies
Cache documents close to server  decrease server load
Typically done by content provider
Clients
Backbone ISP
ISP-1
ISP-2
Server
Reverse proxies

## Slide 79: Improving HTTP Performance: Caching with Forward Proxies
Cache documents close to clients
 reduce network traffic and decrease latency
Typically done by ISPs or enterprises
Clients
Backbone ISP
ISP-1
ISP-2
Server
Reverse proxies
Forward proxies

## Slide 80: Improving HTTP Performance: Replication
Replicate popular Web site across many machines
  Spreads load on servers
  Places content closer to clients
  Helps when content isn’t cacheable
Problem: Want to direct client to particular replica
  Balance load across server replicas
  Pair clients with nearby servers
Common solution:
  DNS returns different addresses based on client’s geo location, server load, etc.

## Slide 81: Improving HTTP Performance: Content Distribution Networks
Caching and replication as a service
Large-scale distributed storage infrastructure (usually) administered by one entity
  e.g., Akamai has servers in 20,000+ locations
Combination of (pull) caching and (push) replication
  Pull: Direct result of clients’ requests
  Push: Expectation of high access rate
Also do some processing
  Handle dynamic web pages
  Transcoding
Notes: Transcoding = change compression rate per user’s bandwidth

## Slide 82: Improving HTTP Performance: CDN Example – Akamai
Akamai creates new domain names for each client
  e.g., a128.g.akamai.net for cnn.com
The CDN’s DNS servers are authoritative for the new domains
The client content provider modifies its content so that embedded URLs reference the new domains.
  “Akamaize” content
  e.g.: http://www.cnn.com/image-of-the-day.gif becomes http://a128.g.akamai.net/image-of-the-day.gif
Requests now sent to CDN’s infrastructure…

## Slide 83: Cost-Effective Content Delivery
General theme: multiple sites hosted on shared physical infrastructure
  efficiency of statistical multiplexing
  economies of scale (volume pricing, etc.)
  amortization of human operator costs
Examples:
  Web hosting companies
  CDNs
  Cloud infrastructure