## Slide 1: CS 353 Designing a Network
Spring 2016
Alefiya Hussain

## Slide 2: Administrivia
Quiz and Exam Schedule on Piazza
This week: basics, philosophy, principles,…
Read Chapter 1
Next week: routing!
Slides will be on Piazza right after class

## Slide 3: Need a Notetaker
We need a note taker for this class
One volunteer?
Please contact DSP Note Taking at notetake@usc.edu
  Note Takers receive a token of appreciation $100 at the end of the semester

## Slide 4: Today
What do today’s access networks look like?
  Just for context
How would you build the rest of a network?
  Keys are efficiency and reliability
Packet dynamics
  Delays, queues, and all that….

## Slide 5: Remember our Internet Diagram
end-system
switch
link

## Slide 6: ISP Technologies
ISPs have very similar backbone technologies to connect regions and connect to each other
But they differ substantially in their “last mile”
  The “access technology” that reaches the consumer

## Slide 7: Some ISPs are phone companies
phone company

## Slide 8: Telephony Access Technology
phone company

## Slide 9: Last Mile (logically)
home PC
switch

## Slide 10: Last Mile (in reality)
home PC
switch
DSL modem
DSLAM
central office
phone line
telephone
telephone network
...

## Slide 11: Digital Subscriber Line (DSL)
Twisted pair copper
3 separate channels
  Downstream data channel
  Upstream data channel
  2-way phone channel

## Slide 12: Cable Access Technology
home PC
switch
cable modem
CMTS
cable head end
copper
fiber
...

## Slide 13: Many households share access
switch
CMTS
fiber
cable head end

## Slide 14: Cable
Coaxial copper & fiber
Shared broadcast medium
  Why?

## Slide 15: Enterprise Access Technology
workstation
“aggregate” switch
Ethernet cable
“local” switch
...

## Slide 16: Ethernet
Twisted pair copper
1 Gbps, 10 Gbps, 100Gbps (each direction)

## Slide 17: Other access technologies
Cellular (smart phones)
Satellite (remote areas)
Fiber to the Home (home)

## Slide 18: Access Technologies
From an architectural perspective…
  Access technologies are a boring detail
  Logical equivalent of a wire to the first-hop switch
From an infrastructure perspective…
  That’s where all the money goes
  Deployment, maintenance, speed limitations, etc.
We won’t discuss access networks any more
  But this is what keeps ISP CEOs up at night…
  Routing protocols, etc., are the least of their problems..

## Slide 19: What about the rest of the network?
Access technologies are specialized
What about the rest of the network?
How do you scale such a network?
  Billions of endpoints!

## Slide 20: What about this design?
Advantage:
  Every source-destination pair has its own link
Disadvantages:
  No sharing
  Would require too many links O(n2)

## Slide 21: What about this design?
Advantage:
  Lots of sharing
Disadvantages:
  Too much sharing
  Transport capacity O(1/n)
  Not very resilient

## Slide 22: What about this design?
Advantage:
  Lots of sharing
Disadvantages:
  Too much sharing
  Transport capacity O(1/n)
  Not very resilient
Last two designs were used for local area nets
  Bad for wide area networks

## Slide 23: Requirements for network topology
Resilient to failures
  Several paths between each source and destination
Enough sharing to be feasible
  Number of links not too high
Provide adequate transport capacity
  Number of links not too small

## Slide 24: Switched Networks
Provide reasonable and flexible compromise

## Slide 25: Requires sharing of links/switches
shared link and switch resources

## Slide 26: Two approaches to sharing
Reservations:
  “Flows” reserve bandwidth needed in advance
  Must reserve their peak bandwidth
On demand: (also known as “best effort”)
  Send packets when you have them
  Hope for the best….

## Slide 27: Example of “Statistical Multiplexing”
Statistical multiplexing:
  Combining demands to share resources efficiently
  Long history in computer science
    Processes on an OS
    Cloud computing
    …
Two Types:
Reservation: sharing at flow level
On-demand: sharing at packet level

## Slide 28: Which is better?

## Slide 29: Example: three constant sources
Total bandwidth 30Mbps
Demands: Each source needs 10Mbps
Reservation and on-demand give same result
  Every source gets what they need
  No wasted bandwidth
  ….

## Slide 30: Example: Three “bursty” sources
12Mbps
Time
Link capacity = 30Mbps
11Mbps
13Mbps

## Slide 31: What happens with reservations?
12Mbps
Option #1: allow two flows to reserve peak rate
Time
Link capacity = 30Mbps
11Mbps
13Mbps
Must turn away third flow!

## Slide 32: What happens with reservations?
12Mbps
Option #2: allow flows to reserve equal rates
Time
11Mbps
13Mbps
Link capacity = 30Mbps
Each source gets 10Mbps
Frequent overloading!

## Slide 33: What happens with on-demand?
No overloading
Time
Link capacity = 30Mbps

## Slide 34: Peak vs Average Rates
For each flow, define:
  P = peak rate
  A = average rate
Reservations must reserve P:
  But flows only use A (on average)
  Level of utilization is A/P
On-demand:
  Can achieve higher utilizations
  Depends on degree of sharing, burstiness of flows
  Peak of aggregate approaches sum of averages

## Slide 35: Smooth vs Bursty Applications
Some apps have relatively small P/A ratios
  Voice might have a ratio of 3:1 or so
Data applications tend to be rather bursty
  Ratios of 100 or greater are common
That’s why the phone network used reservations
  And the Internet does not….
  More in next lectures

## Slide 36: Two approaches to sharing
Reservations
On demand
How are these implemented?

## Slide 37: Two approaches to sharing
Reservations  circuit switching
On demand  packet switching

## Slide 38: Circuit Switching
(1) src sends a reservation request for 10Mbps to dst
(2) Switches “establish a circuit”
(3) src starts sending data
(4) src sends a “teardown circuit” message
dst
10Mb/s?
10Mb/s?
10Mb/s?
src
✔
✔
✔

## Slide 39: Circuit Switching
switch
src
dst
Reservation also establishes a “circuit” within a switch

## Slide 40: Many kinds of “circuits”
Time division multiplexing
  divide time in time slots
  separate time slot per circuit
Frequency division multiplexing
  divide frequency spectrum in frequency bands
  separate frequency band per circuit
time
time
frequency

## Slide 41: Timing in Circuit Switching
time

## Slide 42: Timing in Circuit Switching
time

## Slide 43: Timing in Circuit Switching
time

## Slide 44: Timing in Circuit Switching
time

## Slide 45: Timing in Circuit Switching
time
Circuit establishment

## Slide 46: Timing in Circuit Switching
Data
time
Circuit establishment
Data transfer

## Slide 47: Timing in Circuit Switching
Data
time
Circuit establishment
Data transfer
Circuit teardown
Notes: Why the delays in the first pass of the establishment, but not in subsequent passes (or in teardown)?

## Slide 48: Efficiency in Circuit Switching
time
Circuit establishment
Data transfer
Circuit teardown
Notes: Why the delays in the first pass of the establishment, but not in subsequent passes (or in teardown)?