## Slide 1: Two approaches to sharing
Reservations  circuit switching
On demand  packet switching

## Slide 2: Circuit Switching
(1) src sends a reservation request for 10Mbps to dst
(2) Switches “establish a circuit”
(3) src starts sending data
(4) src sends a “teardown circuit” message
dst
10Mb/s?
10Mb/s?
10Mb/s?
src
✔
✔
✔

## Slide 3: Circuit Switching
switch
src
dst
Reservation also establishes a “circuit” within a switch

## Slide 4: Many kinds of “circuits”
Time division multiplexing
  divide time in time slots
  separate time slot per circuit
Frequency division multiplexing
  divide frequency spectrum in frequency bands
  separate frequency band per circuit
time
time
frequency

## Slide 5: Timing in Circuit Switching
time

## Slide 6: Timing in Circuit Switching
time

## Slide 7: Timing in Circuit Switching
time

## Slide 8: Timing in Circuit Switching
time

## Slide 9: Timing in Circuit Switching
time
Circuit establishment

## Slide 10: Timing in Circuit Switching
Data
time
Circuit establishment
Data transfer

## Slide 11: Timing in Circuit Switching
Data
time
Circuit establishment
Data transfer
Circuit teardown
Notes: Why the delays in the first pass of the establishment, but not in subsequent passes (or in teardown)?

## Slide 12: Stopped here on Thursday 1/14/2016….

## Slide 13: Efficiency in Circuit Switching
time
Circuit establishment
Data transfer
Circuit teardown
Notes: Why the delays in the first pass of the establishment, but not in subsequent passes (or in teardown)?

## Slide 14: Efficiency in Circuit Switching
Data
time
Notes: Why the delays in the first pass of the establishment, but not in subsequent passes (or in teardown)?

## Slide 15: Circuit Switching and Failures
A
B
Circuit switching doesn’t “route around trouble”
Circuit is established
Link Fails along path
Must establish new circuit

## Slide 16: Circuit Switching
Pros
  Predictable performance
  Simple/fast switching (once circuit established)
Cons
  Complexity of circuit setup/teardown
  Inefficient when traffic is bursty (or very short)
  Circuit setup adds delay
  Switch fails  its circuit(s) fails
    Requires new circuit establishment phase

## Slide 17: Packet switching
switch
dst
Each packet contains destination (dst)
Each packet treated independently

## Slide 18: Packet switching
With buffers to absorb transient overloads
switch
dst
Each packet contains destination (dst)
Each packet treated independently

## Slide 19: Packet Switching and Failures
A
B
Packet switching “routes around trouble”
Link Fails along path
Route recomputed on the fly

## Slide 20: Packet Switching
Pros
  Efficient use of network resources
  Simpler to implement
  Robust: can “route around trouble” (covered in routing)
Cons
  Unpredictable performance
  Requires buffer management and congestion control

## Slide 21: Packet vs Circuit Switching
Key factors:
  Resiliency: packet switching wins
  Efficiency: packet switching wins (bursty sources)
Internet has chosen packet switching
  Our focus for rest of course
  How can we measure performance of packet switching?

## Slide 22: Performance Metrics in Packet Swtiching?
Delay
Loss
Throughput

## Slide 23: Delay
How long does it take to send a packet from its source to destination?

## Slide 24: Loss
What fraction of the packets sent to a destination are dropped?

## Slide 25: Throughput
At what rate is the destination receiving data from the source?

## Slide 26: Today
Focus on delay
Loss and throughput will become relevant in later lectures….

## Slide 27: A network link
Link bandwidth
  Number of bits sent per unit time (bits/sec or bps)
Propagation delay (sometimes called latency)
  Time for one bit to move through the link (seconds)
Bandwidth-Delay Product (BDP)
  Number of bits “in flight” at any time (sent, not recvd)
  BDP = bandwidth × propagation delay
bandwidth
Propagation delay
delay x bandwidth

## Slide 28: Examples of BDP
Same city over a slow link:
  bandwidth: ~100Mbps
  propagation delay: ~0.1msec
  BDP: 10,000bits (1.25KBytes)
Cross-country over fast link:
  bandwidth: ~10Gbps
  propagation delay: ~10msec
  BDP: 108bits (12.5MBytes)

## Slide 29: What are the components of Delay
Consists of four components
  Transmission delay
  Propagation delay
  Processing delay
  Queueing delay
First consider transmission, propagation delays
Then queueing delays
Ignore processing delays (tiny in most cases)
due to link properties
due to traffic mix and
switch internals

## Slide 30
transmission
End-to-end delay for a packet
propagation
queuing
processing
transmission
propagation
queuing
processing
transmission
propagation

## Slide 31: Transmission Delay
Q: How long does it take to push all the bits of a packet into a link?
A: Packet size / Transmission rate of the link
Example: Packet = 1kb, Rate = 100Mbps
  1000 bits / 100 Mbits per sec = 10-5 sec = 10μsec

## Slide 32: Propagation Delay
Q: How long does it take to move one bit from one end of a link to the other?
A: Link length / Propagation speed of link
  Propagation speed ~ some fraction of speed of light
Example: Length = 30 kilometers
  30 kilometers/3x108 meters per sec = 10-4 sec = 10msec

## Slide 33: Now ask a more practical question
Q: How long does it take for a packet to travel from A to B?
A: The delay combines both transmission and propagation delays
  Perhaps also queueing, but ignore those for now

## Slide 34: Example: 100B packet from A to B
time=0
A
B
100Byte packet
Time
1Mbps, 1ms
Time to transmit one bit = 1/106s
Time to transmit 800 bits=800x1/106s
Time when that bit reaches B = 1/106+1/103s
The last bit reaches B at
(800x1/106)+1/103s
= 1.8ms

## Slide 35: Example: 100B packet from A to B
A
B
100Byte packet
Time
1Mbps, 1ms
1Gbps, 1ms?
The last bit reaches B at
(800x1/106)+1/103s
= 1.8ms
1GB file in 100B packets
The last bit reaches B at
(800x1/109)+1/103s
= 1.0008ms
The last bit in the file reaches B at
(107x800x1/109)+1/103s
= 8001ms
107 x 100B packets

## Slide 36: Three cases with 1msec prop. delay
1GB file, 1Gbps link: transmission time dominant
100B packet, 1Gbps link: propagation delay dominant
100B packet, 1Mbps link: transmission ~ propagation
Design differs based on which dominates
  But in the Internet, can’t know in advance!

## Slide 37: Technology Trends
Propagation delay?
  No change
Transmission delay?
  Getting smaller!
Queueing delay?
  Usually smaller
How does this affect applications?
  CDNs work very hard to move data near clients
  Reduces backbone bandwidth requirements
  But also decreases latency
  Google: time is money!

## Slide 38: What Trend Did I Leave Out?
The dominance of video
Very high fraction of traffic is video
Files getting larger
But also many, many small flows…

## Slide 39: The “pipe” view
A
B
100Byte packet
Time
1Mbps, 10ms
100Byte packet
100Byte packet
time 
BW 
pkt tx time

## Slide 40: The “pipe” view
1Mbps, 10ms (BDP=10,000)
time 
BW 
10Mbps, 1ms (BDP=10,000)
time 
BW 
1Mbps, 5ms (BDP=5,000)
time 
BW 

## Slide 41: The “pipe” view
1Mbps, 10ms (BDP=10,000)
time 
BW 
1Mbps, 10ms (BDP=10,000)
time 
BW 
100b packets
250b packets

## Slide 42: What happens here with on-demand?
What do we do under overload?
Time
Link capacity = 30Mbps
Notes: What we discuss at end of lecture…

## Slide 43: Answer
Packets temporarily buffered (queueing delays)
Or dropped (if buffer overflows)
Let’s talk about queueing for a bit…

## Slide 44: Queueing delay: “pipe” view

## Slide 45: Queueing delay: “pipe” view
No overload!

## Slide 46: Queueing delay: “pipe” view
Transient Overload
Not a rare event!
Queue

## Slide 47: Queueing delay: “pipe” view
Queue
Transient Overload
Not a rare event!

## Slide 48: Queueing delay: “pipe” view
Queue
Transient Overload
Not a rare event!

## Slide 49: Queueing delay: “pipe” view
Queue
Transient Overload
Not a rare event!

## Slide 50: Queueing delay: “pipe” view
Queue
Transient Overload
Not a rare event!

## Slide 51: Queueing delay: “pipe” view
Queue
Transient Overload
Not a rare event!
Queues absorb transient bursts but introduce queueing delay

## Slide 52: Queueing delay: “pipe” view
What about persistent overload?
Will eventually drop packets (“loss”)

## Slide 53: More packet animations….

## Slide 54: The Lifecycle of Packets
Excess Packets
Stored in Buffer
Packet Arriving
at Switch
Packet
Being
Transmitted
Packet Buffer
Link
Packet Currently
Being Transmitted

## Slide 55: The Delays of Their Lives
Queueing
Delay
Transmission
Delay
Propagation Delay is how long it takes
to reach the next switch after transmission
Round-Trip Time (RTT) is the time it takes
a packet to reach the destination and
the response to return to the sender

## Slide 56: Smooth Arrivals = No Queueing Delays

## Slide 57: Bursty Arrivals = Queueing Delays
There is substantial queueing delay even though link is underutilized

## Slide 58: Packet Losses: Buffers Full

## Slide 59: Packet Losses: Corruption

## Slide 60: Queueing Delay
How long does a packet have to sit in a buffer before it is processed?
Depends on traffic pattern
  Arrival rate at the queue
  Nature of arriving traffic (bursty or not?)
  Transmission rate of outgoing link

## Slide 61
arrival rate / departure rate
1
Average queuing delay
Notes: This plot shows the average queuing delay experienced by a packet arriving at a buffer,
as a function of this entity here, which is the arrival rate divided by the departure rate.
As this entity approaches 1 (the arrival rate approaches the departure rate),
the average delay goes to infinity.
The important thing to note about this curve is the shape.
When we approach close to this area here, the curve goes up very fast.
This means that small changes in arrival rate can have a dramatic impact on delay.
This is what happens when you are driving in a congested highway.
The smallest disturbance (like one car braking) can significantly increase your delay.
When you design a queuing system, you want it to operate far from that point.

## Slide 62: Basic Queueing Terminology
Arrival process: how packets arrive
  Average rate A
  Peak rate P
W: average time packets wait in the queue
  W for “waiting time”
L: average number of packets waiting in the queue
  L for “length of queue”

## Slide 63: Little’s Law (1961)
L = A x W
Compute L: count packets in queue every second
  How often does a single packet get counted? W times
Compute A: count packets sent over time
Why do you care?
  Easy to compute L and A, harder to compute W

## Slide 64: Designing the Internet: Layering
Spring 2016
Alefiya Hussain

## Slide 65: Outline
Modularity (technical)
Layering (technical)
Design principles (technical)
If the Internet is the answer, what were the questions? (context)
History of the Internet (context)
Design goals of the Internet (both)

## Slide 66: At the end of this lecture you…
…will have heard Internet’s “why” and “when”
  Not the “how”….that will take the rest of the semester
You won’t understand it all, but that’s ok
  Useful context before diving into details
We will come back to this at end of the course

## Slide 67: No deep technical issues
Invention of the Internet not due to cleverness…
…but to wisdom
The inventors asked the right questions…
  …and were willing to “think differently” to answer them
But there were no technology breakthroughs…
  …or brilliant algorithms

## Slide 68: Modularity

## Slide 69: The Role of Modularity
We can’t build big systems out of spaghetti code
  Impossible to understand, debug
  Hard to update
We need to limit the scope of changes, so that we can update system without rewriting it from scratch
Modularity is how we limit the scope of changes
  And understand the system at a higher level

## Slide 70: Computer System Modularity
Partition system into modules
  Each module has well-defined interface
Interfaces give flexibility in implementation
  Changes have limited scope
Examples:
  Libraries encapsulating set of functionality
  Programming language abstracts away CPU
The trick is to find the right modularity
  The interfaces should be long-lasting
  If interfaces are changing often, modularity is wrong

## Slide 71: Finding the Right Modularity
Decompose problem into tasks or abstractions
  Task: e.g., compute a function
  Abstraction: e.g., provide reliable storage
Define a module for each task/abstraction
  Involves defining a clean interface for each module
  “Clean” means hiding unnecessary details
Implement system a few times:
  If interfaces seem to hold, you are on the right track…

## Slide 72: Network System Modularity
The need for modularity still applies
  And is even more important! (why?)
Network implementations not just distributed across many lines of code
  Normal modularity “organizes” that code
Networking is distributed across many machines
  Hosts
  Routers

## Slide 73: Network Modularity Decisions
How to break system into modules?
  Classic decomposition into tasks
Where are modules implemented?
  Hosts?
  Routers?
  Both?
Where is state stored?
  Hosts?
  Routers?
  Both?

## Slide 74: Leads to three design principles
How to break system into modules?
  Layering
Where are modules implemented?
  End-to-End Principle
Where is state stored?
  Fate-Sharing

## Slide 75: Layering

## Slide 76: Tasks in Networking
What does it take to send packets across country?
Simplistic decomposition:
  Task 1: send along a single wire
  Task 2: stitch these together to go across country
This gives idea of what I mean by decomposition
Next slide presents a much more detailed version

## Slide 77: Tasks in Networking (bottom up)
Electrons on wire
Bits on wire
Packets on wire
Deliver packets across local network
  Local addresses
Deliver packets across country
  Global addresses
Ensure that packets get there
Do something with the data
Notes: Note thatfirst three are making unit of delivery bigger, next two go from wire to global.

## Slide 78: Resulting Modules (layers)
Electrons on wire (contained in next layer)
Bits on wire (Physical)
Packets on wire (contained in next layer)
Deliver packets across local network (Datalink)
  Local addresses
Deliver packets across country (Network)
  Global addresses
Ensure that packets get there (Transport)
Do something with the data (Application)

## Slide 79: Five Layers (top-down)
Application: Providing network support for apps
Transport (L4): (Reliable) end-to-end delivery
Network (L3): Global best-effort delivery
Datalink (L2): Local best-effort delivery
Physical: Bits on wire
Interactions between these components?
  Do all components talk to each other?
  Or are the components limited in their interactions?
Answer: they are strictly layered!