## Slide 1: CS 353 Designing the Internet Layering, E2E, Fate-sharing
Spring 2016
Alefiya Hussain

## Slide 2: Need for Network System Modularity
Network implementations not just distributed across many lines of code
  Normal modularity “organizes” that code
Networking is distributed across many machines
  Hosts
  Routers

## Slide 3: Network Modularity Decisions
How to break system into modules?
  Classic decomposition into tasks
Where are modules implemented?
  Hosts?
  Routers?
  Both?
Where is state stored?
  Hosts?
  Routers?
  Both?

## Slide 4: Leads to three design principles
How to break system into modules?
  Layering
Where are modules implemented?
  End-to-End Principle
Where is state stored?
  Fate-Sharing

## Slide 5: Layering

## Slide 6: Tasks in Networking
What does it take to send packets across country?
Simplistic decomposition:
  Task 1: send along a single wire
  Task 2: stitch these together to go across country
This gives idea of what I mean by decomposition
Next slide presents a much more detailed version

## Slide 7: Resulting Modules (layers)
Electrons on wire (contained in next layer)
Bits on wire (Physical)
Packets on wire (contained in next layer)
Deliver packets across local network (Datalink)
  Local addresses
Deliver packets across country (Network)
  Global addresses
Ensure that packets get there (Transport)
Do something with the data (Application)

## Slide 8: Strictly Layered Dependencies
Applications
…built on…
…built on…
…built on…
…built on…
Reliable (or unreliable) transport
Best-effort global packet delivery
Best-effort local packet delivery
Physical transfer of bits

## Slide 9: Three Observations
Each layer:
  Depends on layer below
  Supports layer above
  Independent of others
Multiple versions in layer
  Interfaces differ somewhat
  Components pick which lower-level protocol to use
But only one IP layer
  Unifying protocol

## Slide 10: Layering Crucial to Internet’s Success
Innovation at most levels
  Applications (lots)
  Transport (few)
  Datalink (few)
  Physical (lots)
Innovation proceeded largely in parallel
Pursued by very different communities
  Like PL and chip designs

## Slide 11: Distributing Layers Across Network
Layers are simple if only on a single machine
  Just stack of modules interacting with those above/below
But we need to implement layers across machines
  Hosts
  Routers (switches)
What gets implemented where?

## Slide 12: Host: what layers are needed?
Bits arrive on wire, must make it up to application
Therefore, all layers must exist at host!

## Slide 13: Router: What layers are needed?
Bits arrive on wire
  Physical layer necessary
Packets must be delivered to next-hop
  Datalink layer necessary
Routers participate in global delivery
  Network layer necessary
Routers don’t support reliable delivery
  Transport layer (and above) not supported

## Slide 14: Complicated Diagram
HTTP
TCP
IP
Ethernet
interface
HTTP
TCP
IP
Ethernet
interface
IP
IP
Ethernet
interface
Ethernet
interface
SONET
interface
SONET
interface
host
host
router
router
HTTP message
TCP segment
IP packet
IP packet
IP packet

## Slide 15: Simple Diagram
Lower three layers implemented everywhere
Top two layers implemented only at hosts
Transport
Network
Datalink
Physical
Transport
Network
Datalink
Physical
Network
Datalink
Physical
Application
Application
Host A
Host B
Router
Notes: Why go up? Why not stay down in the lower levels?

## Slide 16: Logical Communication
Layers interacts with peer’s corresponding layer
Transport
Network
Datalink
Physical
Transport
Network
Datalink
Physical
Network
Datalink
Physical
Application
Application
Host A
Host B
Router

## Slide 17: Physical Communication
Communication goes down to physical network
Then from network peer to peer
Then up to relevant layer
Transport
Network
Datalink
Physical
Transport
Network
Datalink
Physical
Network
Datalink
Physical
Application
Application
Host A
Host B
Router

## Slide 18: Layer Encapsulation
Trans: Connection ID
Net: G Source/Dest
Link: L Src/Dest
Appl: Get index.html
User A
User B
Necessary Header Information
On wire, packet has: Local S/D, Global S/D, Transport ID, and Body
Notes: Deepest level most header

## Slide 19: Example of Layering in the Real World
CEO A writes letter to CEO B
  Folds letter and hands it to administrative aide
Aide:
  Puts letter in envelope with CEO B’s full name
  Takes to FedEx
FedEx Office
  Puts letter in larger envelope
  Puts name and street address on FedEx envelope
  Puts package on FedEx delivery truck
FedEx delivers to other company
Dear Donald,
You may have more hair, but I have more money.
--Michael

## Slide 20: The Path of the Letter
Fedex Envelope (FE)
CEO
Aide
FedEx
CEO
Aide
FedEx
Location
Letter
Envelope
Semantic Content
Identity
“Peers” on each side understand the same things
No one else needs to
Lowest level has most packaging

## Slide 21: Back to Networking Picture
Transport
Network
Datalink
Physical
Transport
Network
Datalink
Physical
Network
Datalink
Physical
Application
Application
Host A
Host B
Router
Semantic Content
Process Identity
Location
Location

## Slide 22: Design Principles

## Slide 23: Three Internet Design Principles
How to break system into modules?
  Layering
Where are modules implemented?
  End-to-End Principle
Where is state stored?
  Fate-Sharing

## Slide 24: Where to place Network Functionality
Influential paper: “End-to-End Arguments in System Design” by Saltzer, Reed, and Clark (‘84)
  End-to-end principle
Basic observation: some types of network functionality can only be correctly implemented end-to-end
In these cases, end hosts:
  Can satisfy the requirement without network’s help
  Must do so, since can’t rely on network’s help
Thus, don’t need to implement them in network
  Debate about what the network does and doesn’t do…
Notes: \

## Slide 25: Example: Reliable File Transfer
Solution 1: make each step reliable, and string them together to make reliable end-to-end process (requires network to handle reliability)
Solution 2: allow steps to be unreliable, but do end-to-end check and try again if necessary
OS
Appl.
OS
Appl.
Host A
Host B
OK

## Slide 26: Discussion
Solution 1 cannot be made perfectly reliable
  What happens if a network element misbehaves?
  Receiver has to do the check anyway!
Solution 2 can also fail, but only if the end system itself fails (i.e., doesn’t follow its own protocol)
Solution 2 only relies on what it can control
  The endpoint behavior
Solution 1 requires endpoints trust other elements
  That’s not what reliable means!

## Slide 27: Robustness: E2E
As long as the network is not partitioned, two endpoints should be able to communicate
Failures should not interfere with endpoint semantics
-> The second requirement implies that we must adopt solution 2 (cannot depend on network).

## Slide 28: Question?
Should you ever implement reliability in network?
One possible Scenario:
Perhaps, if needed for reasonable efficiency
  Don’t aim for perfect reliability, but ok to reduce error rate
If individual links fail 10% of the time, and are traversing 10 links, then E2E error rate is 65%
Implementing two retransmissions on links
  Link error rate reduced to 0.1%, E2E error rate is 1%

## Slide 29: Summarize End-to-End Principle
Implementing such functionality in the network:
Doesn’t reduce host implementation complexity
Increase network complexity
Often imposes delay/overhead on all applications, even if they don’t need functionality
However, implementing in network can enhance performance in some cases
  E.g., very lossy link

## Slide 30: What Does E2E Principle Ignore?
There are other stakeholders besides users
  ISPs care about the operation/security of their network
Some functions more easily done in the network.
  Think of firewalls…..
Thus, we need “middlebox” functionality
  Will cover later in course…

## Slide 31: Three Internet Design Principles
How to break system into modules?
  Layering
Where are modules implemented?
  End-to-End Principle
Where is state stored?
  Fate-Sharing

## Slide 32: Fate-Sharing
Note that E2E principles relied on “fate-sharing”
  Invariants break only when endpoints themselves break
  Minimize dependence on other network elements
This should dictate placement of storage

## Slide 33: General Principle: Fate-Sharing
When storing state in a distributed system, co-locate it with entities that rely on that state
Only way failure can cause loss of the critical state is if the entity that cares about it also fails ...
  … in which case it doesn’t matter
Often argues for keeping network state at end hosts rather than inside routers
  E.g., packet-switching rather than circuit-switching

## Slide 34: A Cynical View of Distributed Systems
“A distributed system is one in which the failure of a computer you didn't even know existed can render your own computer unusable”
  ---Leslie Lamport
Fate Sharing tries to prevent this!

## Slide 35: Decisions and Their Principles
How to break system into modules
  Dictated by Layering
Where modules are implemented
  Dictated by End-to-End Principle
Where state is stored
  Dictated by Fate-Sharing

## Slide 36: If the Internet is the answer, what were the questions?

## Slide 37: Internet Prehistory (late 50’s)
Telephone network is largest comm’n system
  Uses circuit switching
Need to build networks for other tasks
  Defense
  Computers
  …
But people knew that circuit switching was:
  Inefficient (for bursty loads)
  Not resilient
    Which is why AT&T worked so hard to make components reliable

## Slide 38: Three crucial questions arose
Paul Baran (RAND) asked:
  “How can we design a more resilient network?”
  And invented the notion of packet switching
Len Kleinrock (UCLA) asked:
  “How can we design a more efficient network?”
  And invented the notion of packet switching
A few years later Bob Kahn (DARPA) asked:
  “How can we connect these networks together?”
  And invented the notion of the Internet

## Slide 39: Internet Timeline
1961 Baran, Kleinrock advocate packet switching
1962 Licklider’s vision of Galactic Network
1965 Roberts connects two computers via phone
1967 Roberts publishes vision of ARPANET
1969 BBN installs first IMP at UCLA and ISI
  IMP: Interface Message Processor
1971 Network Control Program (protocol)
1972 Public demonstration of ARPANET

## Slide 40: Timeline continued…
1972 Email invented
1972 Telnet introduced
1972 Kahn advocates Open Architecture networking

## Slide 41: The Problem
Many different packet-switching networks
Only nodes on the same network could communicate

## Slide 42: Kahn’s Rules for Interconnection
Each network is independent and must not be required to change (why?)
Best-effort communication (why?)
Boxes (routers) connect networks
No global control at operations level (why?)

## Slide 43: Solution
Gateways

## Slide 44: Kahn’s vision
Kahn imagined there would be only a few networks (~20) and thus only a few routers
  He was wrong (why?)
Proposed gateways to “translate” btwn networks
  Via a universal protocol that they all understood
Search for “universal” protocol is birth of Internet
  The actual design of IP came later (Cerf and Kahn)

## Slide 45: Timeline continued….
1973 FTP introduced
1973 Ethernet invented (Xerox PARC)
1974 Cerf and Kahn paper on TCP/IP
1980 TCP/IP adopted as defense standard
1983 Global NCP to TCP/IP flag day
198x XNS, DECbit, and other protocols
1984 Janet (British research network)
1985 NSFnet (picks TCP/IP) [thank you Al Gore!]
198x Internet meltdowns due to congestion
1986 Van Jacobson saves the Internet (BSD TCP)
1988 Dave Clark steps down from IAB

## Slide 46: Unsung hero of Internet: David Clark
Chief Architect 1981-1988
Great consistency of vision
Kept the Internet true to its basic design principles
Authored End-to-End Principle
Conceives and articulates architectural concepts
  Read “Active Networking and End-To-End Arguments”
Perhaps the only “irreplaceable” Internet pioneer

## Slide 47: Timeline continued…
1988 Deering and Cheriton propose multicast
1989 Birth of the web….Tim Berners-Lee (CERN)
He invented HTTP

## Slide 48: Timeline continued…..
1993 Search engines invented (Excite)
1994 Internet goes commercial
199x ATM rises and falls (as internetworking layer)
Telcos try to kill the Internet
199x QoS rises and falls
I try to kill the Internet
1998 IPv6 specification
1998 Google reinvents search
200x The Internet boom and bust

## Slide 49: Internet Design Goals

## Slide 50: David Clark
Wrote a paper in 1988 that tried to capture why the Internet turned out as it did
In particular, it described an ordered list of priorities that informed the design

## Slide 51: Internet Design Goals (Clark ‘88)
Connect existing networks
Robust in face of failures
Support multiple types of delivery services
Accommodate a variety of networks
Allow distributed management
Easy host attachment
Cost effective
Allow resource accountability

## Slide 52: #1 Connect Existing Networks
Wanted single protocol that could be used to connect any pair of (existing) networks
The Internet Protocol (IP) is that unifying protocol
  All (existing) networks must be able to implement it
This is where the need for best effort arose….
  And this is where circuit switching died
  Why?

## Slide 53: #2 Robust
Def’n A: As long as network is not partitioned, two hosts should be able to communicate (eventually)
  Can recover from failures
Def’n B: Failures (excepting network partition) should not interfere with endpoint semantics
  Can isolate endpoints from failures
A: Very successful, not clear how relevant now
  Availability more important than recovering from disaster
B: This notion of robustness is underappreciated
  Key to modularity of Internet

## Slide 54: The Internet Architecture
Layer | Scope | Granularity | Where | Unique?
Application | Host | Data | Host | No
Reliability | Global | Data | Host | No
Network | Global | Packets | Network | Yes
Link | Local | Packets | Network | No
Physical | Local | Bits | Network | No

## Slide 55: The Telephony Architecture
Layer | Scope | Granularity | Where | Unique?
Application | Host | Data | Network And Host | No
Reliability | Global | Data | Network | No
Network | Global | Packets | Network | Yes
Link | Local | Packets | Network | No
Physical | Local | Bits | Network | No

## Slide 56: #3 Types of Delivery Services
Use of the term “delivery services” already implied an application-neutral network
Built lowest common denominator service
  Allow end-based protocols to provide better service
  For instance, turn unreliable service into reliable service
Example: recognition that TCP wasn’t needed (or wanted) by some applications
  Separated TCP from IP, and introduced UDP

## Slide 57: The paradox of the Internet’s design
The goal is to support many applications
These applications have different requirements
Shouldn’t the Internet support them all?
  That is, provide a service the satisfies all of them
  By meeting the most stringent requirements

## Slide 58: What service should Internet support?
Strict delay bounds?
  Some applications require them
Guaranteed delivery?
  Some applications are sensitive to packet drops
No applications mind getting good service
  Why not require Internet support all these guarantees?

## Slide 59: Important (life) Lessons
(1) People (or applications)
Don’t always need what they think they need
Almost never need what we think they need
(2) Flexibility often more important than performance
But typically only in hindsight!
Example: cell phones vs landlines
(3) Architect for flexibility, engineer for performance
Flexibility ensures longevity
Performance requirements are ephemeral

## Slide 60: Applying lessons to Internet
Requiring performance guarantees would limit variety of networks that could attach to Internet
Many applications don’t need these guarantees
And those that do?
  Well, they don’t either (usually)
  Tremendous ability to mask drops, delays
And ISPs can work hard to deliver good service without changing the architecture (engineering)
If the Internet had focused on voice applications early, it might have made different choices

## Slide 61: Bottom Line
The choice of packet switching service is not as obvious as it might seem today
Great vision on the part of the Internet designers
And lucky that they were focused on applications that did not need great service

## Slide 62: Internet Design Goals (Clark ‘88)
Connect existing networks
Robust in face of failures
Support multiple types of delivery services
Accommodate a variety of networks
Allow distributed management
Easy host attachment
Cost effective
Allow resource accountability

## Slide 63: #4 Variety of Networks
Incredibly successful!
  Minimal requirements on networks
  No need for reliability, in-order, fixed size packets, etc.
  A result of aiming for lowest common denominator
IP over everything
  Then: ARPANET, X.25, DARPA satellite network..
  Now: ATM, SONET, WDM…

## Slide 64: #5 Decentralized Management
Both a curse and a blessing
  Important for easy deployment
  Makes management hard today

## Slide 65: #6 Host Attachment
Clark observes that cost of host attachment may be higher because hosts have to be smart
But the administrative cost of adding hosts is very low, which is probably more important
  Plug-and-play kind of behavior….

## Slide 66: #7 Cost Effective
Cheaper than circuit switching at low end
More expensive than circuit switching at high end
Not a bad compromise:
  Cheap where it counts (low-end)
  More expensive for those who can pay….

## Slide 67: #8 Resource Accountability
Failure!

## Slide 68: Internet Motto
We reject kings, presidents, and voting. We believe in rough consensus and running code.”
David Clark

## Slide 69: Real Goals
Build something that works!
Connect existing networks
Robust in face of failures
Support multiple types of delivery services
Accommodate a variety of networks
Allow distributed management
Easy host attachment
Cost effective
Allow resource accountability

## Slide 70: Questions to think about….
What priorities would a commercial design have?
What would the resulting design look like?
What goals are missing from this list?
Notes: Missing: resource sharing, other considerations of malicious users (traceback, etc.), address concerns of administrative domains visible

## Slide 71: Readings
Chapter 1 in Systems Approach
David Clark “ The Design Philosophy of the DARPA Internet”, In Proceedings of the ACM SIGCOMM Conference, New York, August 1988, pg 106-118
J. Saltzer, D. Reed, and D. Clark, “End to End Arguments in System Design”, In Proceeding of the Second International Conference on Distributed Computing Systems, Paris, April 1981, pg 509-512