## Slide 1: CS 353 Getting Connected Reliable Transport, Ethernet, Wireless
Spring 2016
Alefiya Hussain

## Slide 2: Goals for next few lectures
Different communication medium over which we can send data (Ch 2: 2.1)
  Types of links
  Types of topologies
Make the links reliable in spite of transmission problems
Media Access Control
Carrier Sense Multiple Access (CSMA) networks
Wireless Networks with different available technologies and protocol (next class)

## Slide 3: Three Ways to Share the Media
Channel partitioning MAC protocols (TDMA, FDMA):
  Share channel efficiently and fairly at high load
  Inefficient at low load (where load = # senders):
    1/N bandwidth allocated even if only 1 active node!
“Taking turns” protocols
  Eliminates empty slots without causing collisions
  Overhead in acquiring the token
  Vulnerable to failures (e.g., failed node or lost token)
Random access MAC protocols
  Efficient at low load: single node can fully utilize channel
  High load: collision overhead

## Slide 4: Key Ideas of Random Access
Carrier sense
  Listen before speaking, and don’t interrupt
  Checking if someone else is already sending data
  … and waiting till the other node is done
Collision detection
  If someone else starts talking at the same time, stop
  Realizing when two nodes are transmitting at once
  …by detecting that the data on the wire is garbled
Randomness
  Don’t start talking again right away
  Waiting for a random time before trying again

## Slide 5: Multiple Access Control (MAC)
Single shared broadcast channel
  Must avoid having multiple nodes speaking at once
  Otherwise, collisions lead to garbled data
  Need distributed algorithm for sharing the channel
  Algorithm determines which node can transmit
Classes of techniques
  Channel partitioning: divide channel into pieces
  Taking turns: scheme for trading off who gets to transmit
  Random access: allow collisions, and then recover
We focus on this last approach (most Internet-like!)

## Slide 6: Random Access MAC Protocols
When node has packet to send
  Transmit at full channel data rate
  No a priori coordination among nodes
Two or more transmitting nodes  collision
  Data lost
Random access MAC protocol specifies:
  How to detect collisions
  How to recover from collisions
Examples
  ALOHA and Slotted ALOHA (background)
  CSMA, CSMA/CD, CSMA/CA (used in practice)

## Slide 7: Where it all Started: AlohaNet
Norm Abramson moved to Hawaii in 1970
  So he could surf!
Set up first data communication system for Hawaiian islands
  Hub at U. Hawaii, Oahu
Had two radio channels:
  Random access:
    Sites sending data
  Broadcast:
    Hub rebroadcasting data
Notes: Who is he, and why is he my hero?

## Slide 8: CSMA (Carrier Sense Multiple Access)
CSMA: listen before transmit
  If channel sensed idle: transmit entire frame
  If channel sensed busy, defer transmission
Human analogy: don’t interrupt others!
Does this eliminate all collisions?
  No, because of nonzero propagation delay

## Slide 9: CSMA Collisions
Collisions can still occur:
propagation delay means
two nodes may not hear
each other’s transmission in time.
At time t1, D still hasn’t heard B’s signal sent at the earlier time t0, so D goes ahead and transmits: failure of carrier sense.
Collision:
entire packet transmission
time wasted

## Slide 10: CSMA Collisions
Propagation delay: two nodes may not hear each other’s before sending.
CSMA reduces but does not eliminate collisions
Biggest remaining problem?
Collisions still take full slot!
How do you fix that?
Notes: Ask: who knows? (from knowing ethernet)?
At time t1, D still hasn’t heard B’s signal sent at the earlier time t0, so D goes ahead and transmits: failure of carrier sense.
Someone who doesn’t, how to do this?
Listen before sending to detect possible collision
Why not listen to detect current collision!

## Slide 11: CSMA/CD (Collision Detection)
CSMA/CD: carrier sensing, deferral as in CSMA
  Collisions detected within short time
  Colliding transmissions aborted, reducing wastage
Collision detection
  Easy in wired LANs: measure signal strengths, compare transmitted, received signals
  Difficult in wireless LANs
    Reception shut off while transmitting
    Even if on, might not be able to hear the other sender, even though the receiver can
    Leads to use of collision avoidance instead

## Slide 12: CSMA/CD Collision Detection
Both B and D can tell that collision occurred.
This lets them (1) know that they need to resend the frame,
and (2) recognize that there’s contention and adopt a strategy for dealing with it.
Note: for this to work, we need restrictions on minimum frame size and maximum distance

## Slide 13: Ethernet: CSMA/CD Protocol
Carrier sense: wait for link to be idle
Collision detection: listen while transmitting
  No collision: transmission is complete
  Collision: abort transmission & send jam signal
Random access: exponential back-off
  After collision, wait a random time before trying again
  After mth collision, choose K randomly from {0, …, 2m-1}
  … and wait for K*512 bit times before trying again
The wired LAN technology
  Hugely successful: 3/10/100/1000/10000 Mbps

## Slide 14: Minimum Packet Size
Why enforce a minimum packet size?
Give a host enough time to detect collisions
In Ethernet, minimum packet size = 64 bytes (two 6-byte addresses, 2-byte type, 4-byte CRC, and 46 bytes of data)
If host has less than 46 bytes to send, the adaptor pads (adds) bytes to make it 46 bytes
What is the relationship between minimum packet size and the length of the LAN?

## Slide 15: Minimum Packet Size (more)
propagation delay (d)
a) Time = t; Host 1
starts to send frame
Host 1
Host 2
propagation delay (d)
Host 1
Host 2
b) Time = t + d; Host 2
starts to send a frame,
just before it hears from
host 1’s frame
propagation delay (d)
Host 1
Host 2
c) Time = t + 2*d; Host 1
hears Host 2’s frame 
detects collision
LAN length = (min_frame_size)*(light_speed)/(2*bandwidth) =
= (8*64b)*(2.5*108mps)/(2*107 bps) = 6400m approx
What about 100 mbps? 1 gbps? 10 gbps?

## Slide 16: Limits on CSMA/CD Network Length
Latency depends on physical length of link
  Time to propagate a packet from one end to the other
Suppose A sends a packet at time t
  And B sees an idle line at a time just before t+d
  … so B happily starts transmitting a packet
B detects a collision, and sends jamming signal
  But A can’t see collision until t+2d
latency d
A
B

## Slide 17: Limits on CSMA/CD Network Length
A needs to wait for time 2d to detect collision
  So, A should keep transmitting during this period
  … and keep an eye out for a possible collision
Imposes restrictions. E.g., for 10 Mbps Ethernet:
  Maximum length of the wire: 2,500 meters
  Minimum length of a frame: 512 bits (64 bytes)
    512 bits = 51.2 sec (at 10 Mbit/sec)
    For light in vacuum, 51.2 sec ≈ 15,000 meters vs. 5,000 meters “round trip” to wait for collision
latency d
A
B

## Slide 18: Ethernet Frame Structure
Sending adapter encapsulates packet in frame
Preamble: synchronization
  Seven bytes with pattern 10101010, followed by one byte with pattern 10101011
  Used to synchronize receiver & sender
Type: indicates the higher layer protocol
  Usually IP (but also Novell IPX, AppleTalk, …)
CRC: cyclic redundancy check
  Receiver checks & simply drops frames with errors

## Slide 19: Ethernet Frame Structure (Continued)
Addresses: 48-bit source and destination MAC addresses
  Receiver’s adaptor passes frame to network-level protocol
    If destination address matches the adaptor’s
    Or the destination address is the broadcast address (ff:ff:ff:ff:ff:ff)
    Or the destination address is a multicast group receiver belongs to
    Or the adaptor is in promiscuous mode
  Addresses are globally unique
    Assigned by NIC vendors (top three octets specify vendor)
      During any given week, > 500 vendor codes seen at LBNL
Data:
  Maximum: 1,500 bytes
  Minimum: 46 bytes (+14 bytes header + 4 byte trailer = 512 bits)

## Slide 20: Ethernet, con’t
Connectionless
  No handshaking between sending and receiving adapter
Unreliable
  Receiving adapter doesn’t send ACKs or NACKs
  Packets passed to network layer can have gaps
  Gaps will be filled if application is using TCP
  Otherwise, application will see the gaps
2,700 page IEEE 802.3 standardization
  http://standards.ieee.org/getieee802/802.3.html
Note, “classical” Ethernet has no length field …
  … instead, sender pauses 9.2 sec when done
  802.3 shoehorns in a length field

## Slide 21: Benefits of Ethernet
Easy to administer and maintain
Inexpensive
Increasingly higher speed
Evolved from shared media to switches
  And from electrical signaling to also optical
  Changes everything except the frame format
  A good general lesson for evolving the Internet:
    The right interface (service model) can often accommodate unanticipated changes

## Slide 22: Shuttling Data at Different Layers
Different devices switch different things
  Physical layer: electrical signals (repeaters and hubs)
  Link layer: frames (bridges and switches)
  Network layer: packets (routers)
Application gateway
Transport gateway
Router
Bridge, switch
Repeater, hub
Frame header
Packet header
TCP header
User
data

## Slide 23: Physical Layer: Repeaters
Distance limitation in local-area networks
  Electrical signal becomes weaker as it travels
  Imposes a limit on the length of a LAN
    In addition to limit imposed by collision detection
Repeaters join LANs together
  Analog electronic device
  Continuously monitors electrical signals on each LAN
  Transmits an amplified copy
Repeater

## Slide 24: Physical Layer: Hubs
Joins multiple input lines electrically
  Do not necessarily amplify the signal
Very similar to repeaters
  Also operates at the physical layer
hub
hub
hub
hub

## Slide 25: Limitations of Repeaters and Hubs
One large collision domain
  Every bit is sent everywhere
  So, aggregate throughput is limited
  E.g., three departments each get 10 Mbps independently
  … and then if connect via a hub must share 10 Mbps
Cannot support multiple LAN technologies
  Repeaters/hubs do not buffer or interpret frames
  So, can’t interconnect between different rates or formats
  E.g., no mixing 10 Mbps Ethernet & 100 Mbps Ethernet
Limitations on maximum nodes and distances
  Does not circumvent limitations of shared media
  E.g., still cannot go beyond 2500 meters on Ethernet

## Slide 26: Link Layer: Switches / Bridges
Connect two or more LANs at the link layer
  Extracts destination address from the frame
  Looks up the destination in a table
  Forwards the frame to the appropriate LAN segment
    Or point-to-point link, for higher-speed Ethernet
Each segment is its own collision domain
hub
switch/bridge
collision domain
collision domain
collision domain

## Slide 27: Switches & Concurrent Comunication
Host A can talk to C, while B talks to D
switch
A
B
C
D
If host has (dedicated) point-to-point link to switch:
  Full duplex: each connection can send in both directions
    At the same time (otherwise, “half duplex”)
  Completely avoids collisions
    No need for carrier sense, collision detection, and so on

## Slide 28: Advantages Over Hubs & Repeaters
Only forwards frames as needed
  Filters frames to avoid unnecessary load on segments
  Sends frames only to segments that need to see them
Extends the geographic span of the network
  Separate collision domains allow longer distances
Improves privacy by limiting scope of frames
  Hosts can “snoop” the traffic traversing their segment
  … but not all the rest of the traffic
If needed, applies carrier sense & collision detection
  Does not transmit when the link is busy
  Applies exponential back-off after a collision
Joins segments using different technologies

## Slide 29: Disadvantages Over Hubs & Repeaters
Higher cost
  More complicated devices that cost more money
Delay in forwarding frames
  Bridge/switch must receive and parse the frame
  … and perform a look-up to decide where to forward
  Introduces store-and-forward delay
    Can ameliorate using cut-through switching
      Start forwarding after only header received
Need to learn where to forward frames
  Bridge/switch needs to construct a forwarding table
  Ideally, without intervention from network administrators
  Solution: self-learning