## Slide 1: CS 353 Getting Connected Reliable Transport, Ethernet, Wireless
Spring 2016
Alefiya Hussain

## Slide 2: Shuttling Data at Different Layers
Different devices switch different things
  Physical layer: electrical signals (repeaters and hubs)
  Link layer: frames (bridges and switches)
  Network layer: packets (routers)
Application gateway
Transport gateway
Router
Bridge, switch
Repeater, hub
Frame header
Packet header
TCP header
User
data

## Slide 3: Link Layer: Switches / Bridges
Connect two or more LANs at the link layer
  Extracts destination address from the frame
  Looks up the destination in a table
  Forwards the frame to the appropriate LAN segment
    Or point-to-point link, for higher-speed Ethernet
Each segment is its own collision domain
hub
switch/bridge
collision domain
collision domain
collision domain

## Slide 4: Which Frames to forward where?
hub
switch/bridge
Domain A
Domain B
Domain C

## Slide 5: Motivation For Self Learning
Large benefit if switch/bridge forward frames only on segments that need them
  Allows concurrent use of other links
Switch table
  Maps destination MAC address to outgoing interface
  Goal: construct the switch table automatically
switch
A
B
C
D

## Slide 6: Self Learning Step
Build a Table
Handle misses
Dealing with Loops

## Slide 7: Self Learning: Building the Table
When a frame arrives
  Inspect source MAC address
  Associate address with the incoming interface
  Store mapping in the switch table
  Use time-to-live field to eventually forget the mapping
    Soft state
A
B
C
D
Switch just learned how to reach A.
Incoming Int | Src MAC (TTL) | Outgoing Int | Dst MAC (TTL)
1 | A (5) |  | 
1
2
3
4
A
C

## Slide 8: Self Learning: Handling Misses
When frame arrives with unfamiliar destination
  Forward the frame out all of the interfaces (“flooding”)
    … except for the one where the frame arrived
  Hopefully, this case won’t happen very often
  When destination replies, switch learns that node, too
A
B
C
D
When in doubt, shout!

## Slide 9: Forwarding Algorithm
When switch receives a frame:
index the switch table using MAC dest address
if entry found for destination {
if dest on segment from which frame arrived then drop frame
else forward frame on interface indicated
}
else flood
forward on all but the interface
on which the frame arrived
Problems?

## Slide 10: Self Learning: Handling Misses
When a frame arrives
  Inspect source MAC address
  Associate address with the incoming interface
  Store mapping in the switch table
  Use time-to-live field to eventually forget the mapping
    Soft state
A
B
C
D
Switch just learned how to reach A and C
Incoming Int | Src MAC (TTL) | Outgoing Int | Dst MAC (TTL)
1 | A (5) | 4 | C(5)
1
2
3
4
A
C

## Slide 11: Flooding Can Lead to Loops
Switches sometimes need to broadcast frames
  Upon receiving a frame with an unfamiliar destination
  Upon receiving a frame sent to the broadcast address
  Implemented by flooding
Flooding can lead to forwarding loops
  E.g., if the network contains a cycle of switches
    Either accidentally, or by design for higher reliability
  “Broadcast storm”

## Slide 12: Solution: Spanning Trees
Ensure the forwarding topology has no loops
  Avoid using some of the links when flooding
  … to prevent loop from forming
Spanning tree
  Sub-graph that covers all vertices but contains no cycles
  Links not in the spanning tree do not forward frames

## Slide 13: Constructing a Spanning Tree
Distributed algorithm
  Switches cooperate to build the spanning tree
  … and adapt automatically when failures occur
Algorithm
  Switches need to elect a root
    The switch with smallest identifier (MAC addr)
  Each switch determines if its interface is on the shortest path from the root
    Excludes it from the tree if not
  Messages (Y, d, X)
    Propose Y as the root
    Distance is d
    From node X
root
One hop
Three hops

## Slide 14: Steps in Spanning Tree Algorithm
Initially, each switch proposes itself as the root
  Switch sends a message out every interface
  proposing itself as the root with distance 0
  Example: switch X announces (X, 0, X)
Switches update their view of the root
  Upon receiving message (Y, d, Z) from Z, check Y’s id
  If new id smaller, start viewing that switch as root
Switches compute their distance from the root
  Add 1 to the distance received from a neighbor
  Identify interfaces not on shortest path to the root
  … and exclude them from the spanning tree
If root or shortest distance to it changed, flood updated message (Y, d+1, X)

## Slide 15: Example From Switch #4’s Viewpoint
Switch #4 thinks it is the root
  Sends (4, 0, 4) message to 2 and 7
Then, switch #4 hears from #2
  Receives (2, 0, 2) message from 2
  … and thinks that #2 is the root
  And realizes it is just one hop away
Then, switch #4 hears from #7
  Receives (2, 1, 7) from 7
  And realizes this is a longer path
  So, prefers its own one-hop path
  And removes 4-7 link from the tree
1
2
3
4
5
6
7

## Slide 16: Example From Switch #4’s Viewpoint
Switch #2 hears about switch #1
  Switch 2 hears (1, 1, 3) from 3
  Switch 2 starts treating 1 as root
  And sends (1, 2, 2) to neighbors
Switch #4 hears from switch #2
  Switch 4 starts treating 1 as root
  And sends (1, 3, 4) to neighbors
Switch #4 hears from switch #7
  Switch 4 receives (1, 3, 7) from 7
  And realizes this is a longer path
  So, prefers its own three-hop path
  And removes 4-7 Iink from the tree
1
2
3
4
5
6
7

## Slide 17: Robust Spanning Tree Algorithm
Algorithm must react to failures
  Failure of the root node
    Need to elect a new root, with the next lowest identifier
  Failure of other switches and links
    Need to recompute the spanning tree
Root switch continues sending messages
  Periodically reannouncing itself as the root (1, 0, 1)
  Other switches continue forwarding messages
Detecting failures through timeout (soft state)
  Switch waits to hear from others
  Eventually times out and claims to be the root

## Slide 18: Evolution Toward Virtual LANs
In the olden days…
  Thick cables snaked through cable ducts in buildings
  Every computer they passed was plugged in
  All people in adjacent offices were put on the same LAN
  Independent of whether they belonged together or not
More recently…
  Hubs and switches changed all that
  Every office connected to central wiring closets
  Often multiple LANs (k hubs) connected by switches
  Flexibility in mapping offices to different LANs
Group users based on organizational structure, rather than the physical layout of the building

## Slide 19: Why Group by Organizational Structure?
Security
  Ethernet is a shared media
  Any interface card can be put into “promiscuous” mode
  … and get a copy of all of the traffic (e.g., midterm exam)
  So, isolating traffic on separate LANs improves security
Load
  Some LAN segments are more heavily used than others
  E.g., researchers running experiments get out of hand
  … can saturate their own segment and not the others
  Plus, there may be natural locality of communication
  E.g., traffic between people in the same research group

## Slide 20: People Move, and Roles Change
Organizational changes are frequent
  E.g., faculty office becomes a grad-student office
  E.g., graduate student becomes a faculty member
Physical rewiring is a major pain
  Requires unplugging the cable from one port
  … and plugging it into another
  … and hoping the cable is long enough to reach
  … and hoping you don’t make a mistake
Would like to “rewire” the building in software
  The resulting concept is a Virtual LAN (VLAN)

## Slide 21: Example: Two Virtual LANs
Red VLAN and Orange VLAN
Bridges forward traffic as needed
R
RO
RO
O
RO

## Slide 22: Example: Two Virtual LANs
Red VLAN and Orange VLAN
Switches forward traffic as needed
R
O
RO
R
R
R
O
O
O
R
O
R
R
R
O
O
O

## Slide 23: Making VLANs Work
Bridges/switches need configuration tables
  Saying which VLANs are accessible via which interfaces
Approaches to mapping to VLANs
  Each interface has a VLAN color
    Only works if all hosts on same segment belong to same VLAN
  Each MAC address has a VLAN color
    Useful when hosts on same segment belong to different VLANs
    Useful when hosts move from one physical location to another
Changing the Ethernet header
  Adding a field for a VLAN tag
  Implemented on the bridges/switches
  … but can still interoperate with old Ethernet cards

## Slide 24: Summary
Ethernet as an exemplar of link-layer technology
Simplest form, single segment:
  Carrier sense, collision detection,
  random access and BEB
Extended to span multiple segments:
  Hubs & repeaters: physical-layer interconnects
  Bridges / switches: link-layer interconnects
Key ideas in switches
  Self learning of the switch table
  Spanning trees