## Slide 1: The Transport Layer
CS 353
Spring 2016
Alefiya Hussain

## Slide 2
The Transport Layer
(brief review from last lecture)

## Slide 3: Review: Transport Layer
Layer at end-hosts, between the application and network layer
Transport
Network
Datalink
Physical
Transport
Network
Datalink
Physical
Network
Datalink
Physical
Application
Application
Host A
Host B
Router

## Slide 4: Why a transport layer?
IP packets are addressed to a host but end-to-end communication is between application processes at hosts
  Need a way to decide which packets go to which applications (mux/demux)
IP provides a weak service model (best-effort)
  Packets can be corrupted, delayed, dropped, reordered, duplicated
  No guidance on how much traffic to send and when
  Dealing with this is tedious for application developers

## Slide 5: Role of the Transport Layer
Communication between application processes
  Mux and demux from/to application processes
  Implemented using ports

## Slide 6: Role of the Transport Layer
Communication between application processes
Provide common end-to-end services for app layer [optional]
  Reliable, in-order data delivery
  Well-paced data delivery
    too fast may overwhelm the network
    too slow is not efficient

## Slide 7: Role of the Transport Layer
Communication between processes
Provide common end-to-end services for app layer [optional]
TCP and UDP are the common transport protocols
  also SCTP, MTCP, SST, RDP, DCCP, …

## Slide 8: Role of the Transport Layer
Communication between processes
Provide common end-to-end services for app layer [optional]
TCP and UDP are the common transport protocols
UDP is a minimalist, no-frills transport protocol
  only provides mux/demux capabilities

## Slide 9: Role of the Transport Layer
Communication between processes
Provide common end-to-end services for app layer [optional]
TCP and UDP are the common transport protocols
UDP is a minimalist, no-frills transport protocol
TCP is the whole-hog protocol
  offers apps a reliable, in-order, bytestream abstraction
  with congestion control
  but no performance guarantees (delay, bw, etc.)

## Slide 10
Transport Design Issues

## Slide 11: Context: Applications and Sockets
Socket: software abstraction by which an application process exchanges network messages with the (transport layer in the) operating system
  socketID = socket(…, socket.TYPE)
  socketID.sendto(message, …)
  socketID.recvfrom(…)
  will cover in detail after midterm
Two important types of sockets
  UDP socket: TYPE is SOCK_DGRAM
  TCP socket: TYPE is SOCK_STREAM

## Slide 12: Ports
Problem: deciding which app (socket) gets which packets
  Solution: port as a transport layer identifier (16 bits)
    packet carries source/destination port numbers in transport header
OS stores mapping between sockets and ports
  Port: in packets
  Socket: in OS
For UDP ports (SOCK_DGRAM)
  OS stores (local port, local IP address)  socket
For TCP ports (SOCK_STREAM)
  OS stores (local port, local IP, remote port, remote IP)  socket

## Slide 13: Two Questions
Why the difference?
  For UDP ports (SOCK_DGRAM)
    OS stores (local port, local IP address)  socket
  For TCP ports (SOCK_STREAM)
    OS stores (local port, local IP, remote port, remote IP )  socket
Why do you need to include local IP?

## Slide 14
4-bit
Version
4-bit
Header
Length
8-bit
Type of Service
(TOS)
16-bit Total Length (Bytes)
16-bit Identification
3-bit
Flags
13-bit Fragment Offset
8-bit Time to
Live (TTL)
8-bit Protocol
16-bit Header Checksum
32-bit Source IP Address
32-bit Destination IP Address
Options (if any)
Payload

## Slide 15
4
5
8-bit
Type of Service
(TOS)
16-bit Total Length (Bytes)
16-bit Identification
3-bit
Flags
13-bit Fragment Offset
8-bit Time to
Live (TTL)
8-bit Protocol
16-bit Header Checksum
32-bit Source IP Address
32-bit Destination IP Address
Payload

## Slide 16
4
5
8-bit
Type of Service
(TOS)
16-bit Total Length (Bytes)
16-bit Identification
3-bit
Flags
13-bit Fragment Offset
8-bit Time to
Live (TTL)
6 = TCP 17 = UDP
16-bit Header Checksum
32-bit Source IP Address
32-bit Destination IP Address
Payload

## Slide 17
4
5
8-bit
Type of Service
(TOS)
16-bit Total Length (Bytes)
16-bit Identification
3-bit
Flags
13-bit Fragment Offset
8-bit Time to
Live (TTL)
6 = TCP 17 = UDP
16-bit Header Checksum
32-bit Source IP Address
32-bit Destination IP Address
Payload
16-bit Source Port
16-bit Destination Port
More transport header fields ….

## Slide 18: Recap: Multiplexing and Demultiplexing
Host receives IP packets
  Each IP header has source and destination IP address
  Each Transport Layer header has source and destination port number
Host uses IP addresses and port numbers to direct the message to appropriate socket
  UDP maps local destination port and address to socket
  TCP maps address pair and port pair to socket

## Slide 19: Rest of Lecture
More on ports
UDP
Reliable Transport
Next lecture: Details of TCP

## Slide 20: More on Ports
Separate 16-bit port address space for UDP and TCP
“Well known” ports (0-1023): everyone agrees which services run on these ports
  e.g., ssh:22, http:80
  helps client know server’s port
  Services can listen on well-known port
Ephemeral ports (most 1024-65535): given to clients

## Slide 21: UDP: User Datagram Protocol
Lightweight communication between processes
  Avoid overhead and delays of ordered, reliable delivery
UDP described in RFC 768 – (1980!)
  Destination IP address and port to support demultiplexing
  Optional error checking on the packet contents
    (checksum field = 0 means “don’t verify checksum”)
SRC port
DST port
checksum
length
DATA

## Slide 22: Why a transport layer?
IP packets are addressed to a host but end-to-end communication is between application processes at hosts
  Need a way to decide which packets go to which applications (mux/demux)
IP provides a weak service model (best-effort)
  Packets can be corrupted, delayed, dropped, reordered, duplicated

## Slide 23: Reliable Transport
@Sender
  send packets
@Receiver
  wait for packets
In a perfect world, reliable transport is easy

## Slide 24: Reliable Transport
In a perfect world, reliable transport is easy
All the bad things best-effort can do
  a packet is corrupted (bit errors)
  a packet is lost (why?)
  a packet is delayed (why?)
  packets are reordered (why?)
  a packet is duplicated (why?)

## Slide 25: Reliable Transport
Mechanisms for coping with bad events
  Checksums: to detect corruption
  ACKs: receiver tells sender that it received packet
  NACK: receiver tells sender it did not receive packet
  Sequence numbers: a way to identify packets
  Retransmissions: sender resends packets
  Timeouts: a way of deciding when to resend a packet
  Forward error correction: a way to mask errors without retransmission
  Network encoding: an efficient way to repair errors
  ….

## Slide 26: Dealing with Packet Corruption
Time
Sender
Receiver
1
2
2


ack
nack

## Slide 27: Dealing with Packet Corruption
Time
Sender
Receiver
1
1


ack(1)
ack(1)
What if the ACK/NACK is corrupted?
Packet #1 or #2?
2
P(2)
P(1)
P(1)
Data and ACK packets carry sequence numbers

## Slide 28: Dealing with Packet Loss
Time
Sender
Receiver
1
1

ack(1)
P(1)
P(1)
Timer-driven loss detection Set timer when packet is sent; retransmit on timeout
Timeout
P(2)

## Slide 29: Dealing with Packet Loss (of ack)
Time
Sender
Receiver
1
1

ack(1)
P(1)
P(1)
Timeout
P(2)
duplicate!

## Slide 30: Dealing with Packet Loss
Time
Sender
Receiver
1
.
.
.
1
ack(1)
P(1)
P(1)
Timer-driven retx. can lead to duplicates
Timeout
P(2)
duplicate!
ack(1)

## Slide 31: Components of a solution (so far)
checksums (to detect bit errors)
timers (to detect loss)
acknowledgements (positive or negative)
sequence numbers (to deal with duplicates)
But we haven’t put them together into a coherent design…

## Slide 32
Designing Reliable Transport

## Slide 33: A Solution: “Stop and Wait”
We have a correct reliable transport protocol!
Probably the world’s most inefficient one (why?)
@Sender
  send packet(I); (re)set timer; wait for ack
  If (ACK)
    I++; repeat
  If (NACK or TIMEOUT)
    repeat
@Receiver
  wait for packet
  if packet is OK, send ACK
  else, send NACK
  repeat

## Slide 34: Stop & Wait is Inefficient
ACK
DATA
Sender
Receiver
RTT
If TRANS << RTT then
Throughput ~ DATA/RTT
TRANS

## Slide 35: Three Design Decisions
Which packets can sender send?
  Sliding window
How does receiver ack packets?
  Cumulative
  Selective
Which packets does sender resend?
  GBN
  Selective repeat

## Slide 36: Sliding Window
window = set of adjacent sequence numbers
  The size of the set is the window size; assume window size is n
General idea: send up to n packets at a time
  Sender can send packets in its window
  Receiver can accept packets in its window
  Window of acceptable packets “slides” on successful reception/acknowledgement
  Window contains all packets that might still be in transit
Sliding window often called “packets in flight”

## Slide 37: Sliding Window
Let A be the last ack’d packet of sender without gap; then window of sender = {A+1, A+2, …, A+n}
Let B be the last received packet without gap by receiver, then window of receiver = {B+1,…, B+n}
n
B
Received and ACK’d
Acceptable but not yet received
Cannot be received
n
A
Already ACK’d
Sent but not ACK’d
Cannot be sent
sequence number 

## Slide 38: Throughput of Sliding Window
If window size is n, then throughput is roughly
MIN[ nDATA/RTT, Link Bandwidth]
Compare to Stop and Wait: Data/RTT
questions:
  What happens when n gets too large?
  How do we choose n?

## Slide 39: Acknowledgements w/ Sliding Window
Two common options
  cumulative ACKs: ACK carries next in-order sequence number that the receiver expects

## Slide 40: Cumulative Acknowledgements (1)
At receiver
n
B
Received and ACK’d
Acceptable but not yet received
Cannot be received
After receiving B+1, B+2
n
Bnew= B+2
Receiver sends ACK(B+3) = ACK(Bnew+1)

## Slide 41: Cumulative Acknowledgements (2)
At receiver
n
B
Received and ACK’d
Acceptable but not yet received
Cannot be received
After receiving B+4, B+5
n
B
Receiver sends ACK(B+1)

## Slide 42: Acknowledgements w/ Sliding Window
Two common options
  cumulative ACKs: ACK carries next in-order sequence number the receiver expects
  selective ACKs: ACK individually acknowledges correctly received packets
Selective ACKs offer more precise information but require more complicated book-keeping

## Slide 43: Sliding Window Protocols
Resending packets: two canonical approaches
  Go-Back-N
  Selective Repeat
Many variants that differ in implementation details

## Slide 44: GBN Example w/o Errors
Time
Window size = 3 packets
Sender
Receiver
1
{1}
2
{1, 2}
3
{1, 2, 3}
4
{2, 3, 4}
5
{3, 4, 5}
Sender Window
Receiver Window
6
{4, 5, 6}
.
.
.
.
.
.

## Slide 45: GBN Example with Errors
Window size = 3 packets
Sender
Receiver
1
2
3
4
5
6
Timeout
Packet 4
4
5
6

## Slide 46: Selective Repeat (SR)
Sender: transmit up to n unacknowledged packets
Assume packet k is lost, k+1 is not
Receiver: indicates packet k+1 correctly received
Sender: retransmit only packet k on timeout
Efficient in retransmissions but complex book-keeping
  need a timer per packet

## Slide 47: SR Example with Errors
Time
Sender
Receiver
1
2
3
4
5
6
4
7
ACK=5
Window size = 3 packets
{1}
{1, 2}
{1, 2, 3}
{2, 3, 4}
{3, 4, 5}
{4, 5, 6}
{4,5,6}
{7, 8, 9}
ACK=6
{4,5,6}
Timeout
Packet 4
ACK=4

## Slide 48: Observations
With sliding windows, it is possible to fully utilize a link, provided the window size is large enough.
Sender has to buffer all unacknowledged packets, because they may require retransmission
Receiver may be able to accept out-of-order packets, but only up to its buffer limits
Implementation complexity depends on protocol details (GBN vs. SR)

## Slide 49: Recap: components of a solution
Checksums (for error detection)
Timers (for loss detection)
Acknowledgments
  cumulative
  selective
Sequence numbers (duplicates, windows)
Sliding Windows (for efficiency)
Reliability protocols use the above to decide when and what to retransmit or acknowledge

## Slide 50: What does TCP do?
Most of our previous tricks + a few differences
Sequence numbers are byte offsets
Sender and receiver maintain a sliding window
Receiver sends cumulative acknowledgements (like GBN)
Sender maintains a single retx. timer
Receivers do not drop out-of-sequence packets (like SR)
Introduces fast retransmit : optimization that uses duplicate ACKs to trigger early retx (next time)
Introduces timeout estimation algorithms (next time)

## Slide 51: TCP
TCP
  Reliability
  Congestion control

## Slide 52
Until Now
  Flow control: adjusting the sending rate to keep from overwhelming a slow receiver
Today
  Congestion control: adjusting the sending rate to keep from overloading the network

## Slide 53: Statistical Multiplexing  Congestion
If two packets arrive at a router at the same time
  Router will transmit one and buffer/drop the other
Internet traffic is bursty
If many packets arrive close in time
  the router cannot keep up  gets congested
  causes packet delays and drops

## Slide 54: A few design considerations
How do we know the network is congested?
Who takes care of congestion?
  network, end hosts, both, …
How do we handle of congestion?
…If you were starting with TCP?

## Slide 55: TCP’s approach
End hosts adjust sending rate
Based on implicit feedback from network
Not the only approach
  A consequence of history rather than planning

## Slide 56: Some History: TCP in the 1980s
Sending rate only limited by flow control
  Dropped packets  senders (repeatedly!) retransmit
Led to “congestion collapse” in Oct. 1986
  Throughput on the NSF network dropped from 32Kbits/s to 40bits/sec
“Fixed” by Van Jacobson’s development of TCP’s congestion control (CC) algorithms

## Slide 57: Van Jacobson
Leader of the networking research group at LBL
Many contributions to the early TCP/IP stack
  Most notably congestion control
Creator of many widely used network tools
  Traceroute, tcpdump, pathchar, Berkeley Packet Filter
Later Chief Scientist at Cisco, now Fellow at PARC

## Slide 58: Jacobson’s Approach
Extend TCP’s existing window-based protocol but adapt the window size in response to congestion
A pragmatic and effective solution
  required no upgrades to routers or applications!
  patch of a few lines of code to TCP implementations
Extensively researched and improved upon
  Especially now with datacenters and cloud services