## Slide 1: TCP
CS 353
Spring 2016
Alefiya Hussain

## Slide 2
The Transport Layer
(brief review from last lecture)

## Slide 3: Important Distinctions
Functionality implemented in network
  Keep minimal (easy to build, broadly applicable)
Functionality implemented in the application
  Keep minimal (easy to write)
  Restricted to application-specific functionality
Functionality implemented in the “network stack”
  The shared networking code on the host
  This relieves burden from both app and network
  The transport layer is a key component here
Notes: So when I say an app needs reliable service, I mean that the app wants to offer the user that serivice.
It is one thing to say uses want relaibliity, another to say the network must provide it!

## Slide 4: Role of Transport Layer
Bridging the gap between
  The abstractions application designers want
  The abstractions networks can easily support
Provide common end-to-end services for app layer
  Deal with network on behalf of applications
  Deal with applications on behalf of networks
Could have been built into apps, but want common implementations to make app development easier
  Transport runs on end host, so this is about software modularity, not overall network architecture

## Slide 5: Role of Transport Layer
Application layer
  Communication for specific applications
  E.g., HyperText Transfer Protocol (HTTP), File Transfer Protocol (FTP), Simple Mail Transfer Protocol (SMTP)
Transport layer
  What do we need here?
Network layer
  Logical communication between nodes
  Hides details of the link technology
  E.g., IP

## Slide 6: Role of Transport Layer
Application layer
  Communication for specific applications
  E.g., HyperText Transfer Protocol (HTTP), File Transfer Protocol (FTP), Simple Mail Transfer Protocol (SMTP)
Transport layer
  What do we need here?
Network layer
  Global communication between nodes
  Hides details of the link technology
  E.g., IP

## Slide 7: Role of Transport Layer
Application layer
  Communication for specific applications
  E.g., HyperText Transfer Protocol (HTTP), File Transfer Protocol (FTP), Simple Mail Transfer Protocol (SMTP)
Transport layer
  What do we need here?
Network layer
  Logical communication between nodes
  Hides details of the link technology
  E.g., IP

## Slide 8: What Problems Should Be Solved Here?
Where does host put incoming data?
  IP just points towards next protocol
  How do you get data to the right application?
  Transport needs to demultiplex incoming data (ports)
Applications think in terms of files or bytestreams
  Network deals with packets
  Transport layer needs to translate between them
Reliability (for those apps that want it)
Corruption
Avoid overloading the receiving host
Avoid overloading the network

## Slide 9: What Is Needed to Address These?
Demultiplexing: identifier for application process
  Going from host-to-host (IP) to process-to-process
Translating between bytestreams and packets
  Do segmentation and reassembly
Reliability: ACKs and all that stuff
Corruption: checksum
Not overloading receiver: “Flow Control”
  Limit data in recvr’s buffer
Not overloading network: “Congestion Control”
  Limit data based on network capacity

## Slide 10: Conclusion?
Transport is easy!
  Except congestion control, which we cover later…
Rest of lecture just diving into details
  Nothing is fundamental
  These are just current implementation choices
Recap of UDP
Longer discussion of TCP

## Slide 11: Logical View of Transport Protocols
Provide logical communication between application processes running on different hosts
Sender: breaks application messages into segments, and passes to network layer
Receiver: reassembles segments into messages, passes to application layer
application
transport
network
data link
physical
application
transport
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
logical end-end transport

## Slide 12: UDP: Datagram messaging service
No-frills extension of “best-effort” IP
Multiplexing/Demultiplexing among processes
Discarding corrupted packets (optional)

## Slide 13: TCP: Reliable, in-order delivery
What UDP provides, plus:
Retransmission of lost and corrupted packets
Flow control (to not overflow receiver)
Congestion control (to not overload network)
“Connection” set-up & tear-down

## Slide 14: Connections (or sessions)
Reliability requires keeping state
  Sender: packets sent but not ACKed, and related timers
  Receiver: noncontiguous packets
Each bytestream is called a connection or session
  Each with their own connection state
  State is in hosts, not network!
Example: I am using HTTP to access content on two different servers, and I’m also ssh’ing into another host. How many sessions is this?

## Slide 15: Services not available
Delay and/or bandwidth guarantees
  This cannot be offered by transport
  Requires support at IP level (and let’s not go there)
Sessions that survive change-of-IP-address
  This is an artifact of current implementations
  As we shall see….

## Slide 16: UDP: User Datagram Protocol
Lightweight communication between processes
  Avoid overhead and delays of ordered, reliable delivery
  Send messages to and receive them from a socket
UDP described in RFC 768 – (1980!)
  IP plus port numbers to support (de)multiplexing
  Optional error checking on the packet contents
    (checksum field = 0 means “don’t verify checksum”)
SRC port
DST port
checksum
length
DATA

## Slide 17: Why Would Anyone Use UDP?
Finer control over what data is sent and when
  As soon as an application process writes into the socket
  … UDP will package the data and send the packet
No delay for connection establishment
  UDP just blasts away without any formal preliminaries
  … which avoids introducing any unnecessary delays
No connection state
  No allocation of buffers, sequence #s, timers …
  … making it easier to handle many active clients at once
Small packet header overhead
  UDP header is only 8 bytes

## Slide 18: Popular Applications That Use UDP
Some interactive streaming apps
  Retransmitting lost/corrupted packets often pointless - by the time the packet is retransmitted, it’s too late
  E.g., telephone calls, video conferencing, gaming
  Modern streaming protocols using TCP (and HTTP)
Simple query protocols like Domain Name System
  Connection establishment overhead would double cost
  Easier to have application retransmit if needed
“Address for bbc.co.uk?”
“212.58.224.131”

## Slide 19: TCP
TCP
  Reliability
  Congestion control

## Slide 20: Three Issues to Consider
Discovering the available (bottleneck) bandwidth
Adjusting to variations in bandwidth
Sharing bandwidth between flows

## Slide 21: Abstract View
Ignore internal structure of router and model it as a single queue for a particular input-output pair
Sending Host
Buffer in Router
Receiving Host
A
B

## Slide 22: Discovering available bandwidth
Pick sending rate to match bottleneck bandwidth
  Without any a priori knowledge
  Could be gigabit link, could be a modem
A
B
100 Mbps

## Slide 23: Adjusting to variations in bandwidth
Adjust rate to match instantaneous bandwidth
  Assuming you have rough idea of bandwidth
A
B
BW(t)

## Slide 24: Multiple flows and sharing bandwidth
Two Issues:
Adjust total sending rate to match bandwidth
Allocation of bandwidth between flows
A2
B2
BW(t)
A1
A3
B3
B1

## Slide 25: Reality
Congestion control is a resource allocation problem involving many flows, many links, and complicated global dynamics
1Gbps
600Mbps
1Gbps

## Slide 26: Possible Approaches
(0) Send without care
  Many packet drops

## Slide 27: Possible Approaches
(0) Send without care
(1) Reservations
  Pre-arrange bandwidth allocations
  Requires negotiation before sending packets
  Low utilization

## Slide 28: Possible Approaches
(0) Send without care
(1) Reservations
(2) Pricing
  Don’t drop packets for the high-bidders
  Requires payment model

## Slide 29: Possible Approaches
(0) Send without care
(1) Reservations
(2) Pricing
(3) Dynamic Adjustment
  Hosts infer level of congestion; adjust
  Network reports congestion level to hosts; hosts adjust
  Combinations of the above
  Simple to implement but suboptimal, messy dynamics

## Slide 30: Possible Approaches
(0) Send without care
(1) Reservations
(2) Pricing
(3) Dynamic Adjustment
All three techniques have their place
Generality of dynamic adjustment has proven powerful
Doesn’t presume business model, traffic characteristics, application requirements
But does assume good citizenship!

## Slide 31: TCP’s Approach in a Nutshell
TCP connection has window
  Controls number of packets in flight
Sending rate: ~Window/RTT
Vary window size to control sending rate

## Slide 32: Announcements:
Ubuntu
Wednesday April 6th, 5-6pm, Leavey basement 3L.
Friday April 8th, 7-8pm, Leavey basement 3L.
Mac:
Next week
Assignment 3 Due: 4/22
Assignment clinic: 4/7
Quiz 3: Friday 4/15
Assignment 2 grades on BB
Office Hours for Grader: Ubuntu and Mac
Summer internships? Contact me

## Slide 33: TCP
We have discussed the general nature of reliable transport on Friday. We now focus on it is implemented today.

## Slide 34: Transmission Control Protocol (TCP)
Reliable, in-order delivery
  Ensures byte stream (eventually) arrives intact
    In the presence of corruption and loss
Connection oriented
  Explicit set-up and tear-down of TCP session
Full duplex stream-of-bytes service
  Sends and receives a stream of bytes, not messages
Flow control
  Ensures that sender doesn’t overwhelm receiver
Congestion control
  Dynamic adaptation to network path’s capacity

## Slide 35: Basic Components of Reliability
ACKs
  Can’t be reliable without knowing whether data has arrived
  TCP uses byte sequence numbers to identify payloads
Checksums (to detect corruption)
  Can’t be reliable without knowing whether data is corrupted
  TCP does checksum over TCP and pseudoheader
Timeouts and retransmissions
  Can’t be reliable without retransmitting lost/corrupted data
  TCP retransmits based on timeouts and duplicate ACKs
  Timeout based on estimate of RTT

## Slide 36: Other TCP Design Decisions
Sliding window flow control
  Allow W contiguous bytes to be in flight
Cumulative acknowledgements
  Selective ACKs (full information) also supported (ignore)
Single timer set after each payload is ACKed
  Timer is effectively for the “next expected payload”
  When timer goes off, resend that payload and wait
    And double timeout period
Various tricks related to “fast retransmit”
  Using duplicate ACKs to trigger retransmission

## Slide 37: TCP Header
Source port
Destination port
Sequence number
Acknowledgment
Advertised window
HdrLen
Flags
0
Checksum
Urgent pointer
Options (variable)
Data

## Slide 38: TCP Header
Source port
Destination port
Sequence number
Acknowledgment
Advertised window
HdrLen
Flags
0
Checksum
Urgent pointer
Options (variable)
Data
These should
be familiar

## Slide 39: Segments and Sequence Numbers

## Slide 40: TCP “Stream of Bytes” Service…
Byte 0
Byte 1
Byte 2
Byte 3
Byte 0
Byte 1
Byte 2
Byte 3
Application @ Host A
Application @ Host B
Byte 80
Byte 80

## Slide 41: … Provided Using TCP “Segments”
Byte 0
Byte 1
Byte 2
Byte 3
Byte 0
Byte 1
Byte 2
Byte 3
Host A
Host B
Byte 80
TCP Data
TCP Data
Byte 80
Segment sent when:
Segment full (Max Segment Size),
Not full, but times out

## Slide 42: TCP Segment
IP packet
  No bigger than Maximum Transmission Unit (MTU)
  E.g., up to 1500 bytes with Ethernet
TCP packet
  IP packet with a TCP header and data inside
  TCP header  20 bytes long
TCP segment
  No more than Maximum Segment Size (MSS) bytes
  E.g., up to 1460 consecutive bytes from the stream
  MSS = MTU – (IP header) – (TCP header)
IP Hdr
IP Data
TCP Hdr
TCP Data (segment)

## Slide 43: Sequence Numbers
Host A
ISN (initial sequence number)
Sequence number = 1st byte in segment = ISN + k
k bytes

## Slide 44: Sequence Numbers
Host B
TCP Data
TCP Data
TCP
HDR
TCP
HDR
ACK sequence number
= next expected byte
= seqno + length(data)
Host A
ISN (initial sequence number)
Sequence number = 1st byte in segment = ISN + k
k

## Slide 45: ACKing and Sequence Numbers
Sender sends packet
  Data starts with sequence number X
  Packet contains B bytes
    X, X+1, X+2, ….X+B-1
Upon receipt of packet, receiver sends an ACK
  If all data prior to X already received:
    ACK acknowledges X+B (because that is next expected byte)
  If highest contiguous byte received is smaller value Y
    ACK acknowledges Y+1
    Even if this has been ACKed before

## Slide 46: Normal Pattern
Sender: seqno=X, length=B
Receiver: ACK=X+B
Sender: seqno=X+B, length=B
Receiver: ACK=X+2B
Sender: seqno=X+2B, length=B
Seqno of next packet is same as last ACK field

## Slide 47: TCP Header
Source port
Destination port
Sequence number
Acknowledgment
Advertised window
HdrLen
Flags
0
Checksum
Urgent pointer
Options (variable)
Data
Starting byte offset of data
carried in this segment
Notes: Number of first byte

## Slide 48: TCP Header
Source port
Destination port
Sequence number
Acknowledgment
Advertised window
HdrLen
Flags
0
Checksum
Urgent pointer
Options (variable)
Data
Acknowledgment gives seqno just beyond highest seqno received in order
(“What Byte is Next”)

## Slide 49: TCP Header
Source port
Destination port
Sequence number
Acknowledgment
Advertised window
HdrLen
Flags
0
Checksum
Urgent pointer
Options (variable)
Data

## Slide 50: Sliding Window Flow Control
Advertised Window: W
  Can send W bytes beyond the next expected byte
Receiver uses W to prevent sender from overflowing buffer
Limits number of bytes sender can have in flight

## Slide 51: Filling the Pipe
Simple example:
  W (in bytes), window which we assume is constant
  RTT (in sec), which we assume is constant
  B (in bytes/sec), bandwidth
How fast will data be transferred?
If W/RTT < B, the transfer has speed W/RTT
If W/RTT > B, the transfer has speed B

## Slide 52: Performance with Sliding Window
Consider USC - NYC 1 Mbps path (100msec RTT)
  Q1: How fast can we transmit with W=12.5KB? (~8pkts)
  A: 12.5KB/100msec ~ 1Mbps (we can fill the pipe)
Q2: What if path is 1Gbps?
  A2: We can still only send 1Mbps
What Window required to fully utilize path:
  Bandwidth-delay product
  1 Gbps * 100 msec = 100 Mb = 12.5 MB
  12.5 MB ~ 8333 packets of 1500bytes (lots of packets!)
Notes: Check old lecture; did I do this???

## Slide 53: Advertised Window Limits Rate
Sender can send no faster than W/RTT bytes/sec
Receiver only advertises more space when it has consumed old arriving data
In original TCP design, that was the sole protocol mechanism controlling sender’s rate
What’s missing?
Notes: Being fair to others

## Slide 54: Implementing Sliding Window
Both sender & receiver maintain a window
  Sender: not yet ACK’ed
  Receiver: not yet delivered to application
Left edge of window:
  Sender: beginning of unacknowledged data
  Receiver: beginning of undelivered data
For the sender:
  Window size = maximum amount of data in flight
For the receiver:
  Window size = maximum amount of undelivered data
Notes: Picture on board

## Slide 55: Sliding Window
Allow a larger amount of data “in flight”
  Allow sender to get ahead of the receiver
  … though not too far ahead
Sending process
Receiving process
Last byte ACKed
Last byte can send
TCP
TCP
Next byte needed
Last byte written
Last byte read
Last byte received
Sender Window
Receiver Window

## Slide 56: Sliding Window
For the sender, when receives an acknowledgment for new data, window advances (slides forward)
Sending process
Last byte ACKed
Last byte can send
TCP
Last byte written
Sender Window

## Slide 57: Sliding Window
For the sender, when receives an acknowledgment for new data, window advances (slides forward)
Sending process
Last byte ACKed
Last byte can send
TCP
Last byte written
Sender Window

## Slide 58: Sliding Window
For the receiver, as the receiving process consumes data, the window slides forward
Receiving process
TCP
Next byte needed
Last byte read
Last byte received
Receiver Window

## Slide 59: Sliding Window
For the receiver, as the receiving process consumes data, the window slides forward
Receiving process
TCP
Next byte needed
Last byte read
Last byte received
Receiver Window

## Slide 60: Sliding Window Summary
Sender: window advances when new data ack’d
Receiver: window advances as receiving process consumes data
Receiver advertises to the sender where the receiver window currently ends (“righthand edge”)
  Sender agrees not to exceed this amount
  It makes sure by setting its own window size to a value that can’t send beyond the receiver’s righthand edge

## Slide 61: TCP Header: What’s left?
Source port
Destination port
Sequence number
Acknowledgment
Advertised window
HdrLen
Flags
0
Checksum
Urgent pointer
Options (variable)
Data
“Must Be Zero” 6 bits reserved
Number of 4-byte words in TCP header; 5 = no options

## Slide 62: TCP Header: What’s left?
Source port
Destination port
Sequence number
Acknowledgment
Advertised window
HdrLen
Flags
0
Checksum
Urgent pointer
Options (variable)
Data
Used with URG flag to indicate urgent data

## Slide 63: TCP Header: What’s left?
Source port
Destination port
Sequence number
Acknowledgment
Advertised window
HdrLen
Flags
0
Checksum
Urgent pointer
Options (variable)
Data

## Slide 64: TCP Connection Establishment and Initial Sequence Numbers

## Slide 65: Initial Sequence Number (ISN)
Sequence number for the very first byte
  E.g., Why not just use ISN = 0?
Practical issue
  IP addresses and port #s uniquely identify a connection
  Eventually, though, these port #s do get used again
  … small chance an old packet is still in flight
TCP therefore requires changing ISN
  Set from 32-bit clock that ticks every 4 microseconds
  … only wraps around once every 4.55 hours
To establish a connection, hosts exchange ISNs
  How does this help?

## Slide 66: Establishing a TCP Connection
Three-way handshake to establish connection
  Host A sends a SYN (open; “synchronize sequence numbers”) to host B
  Host B returns a SYN acknowledgment (SYN ACK)
  Host A sends an ACK to acknowledge the SYN ACK
SYN
SYN ACK
ACK
A
B
Data
Data
Each host tells its ISN to the other host.

## Slide 67: TCP Header
Source port
Destination port
Sequence number
Acknowledgment
Advertised window
HdrLen
Flags
0
Checksum
Urgent pointer
Options (variable)
Data
Flags:
SYN
ACK
FIN
RST
PSH
URG
See /usr/include/netinet/tcp.h on Unix Systems

## Slide 68: Step 1: A’s Initial SYN Packet
A’s port
B’s port
A’s Initial Sequence Number
(Irrelevant since ACK not set)
Advertised window
5=20B
Flags
0
Checksum
Urgent pointer
Options (variable)
Flags:
SYN
ACK
FIN
RST
PSH
URG
A tells B it wants to open a connection…

## Slide 69: Step 2: B’s SYN-ACK Packet
B’s port
A’s port
B’s Initial Sequence Number
ACK = A’s ISN plus 1
Advertised window
20B
0
Checksum
Urgent pointer
Options (variable)
Flags:
SYN
ACK
FIN
RST
PSH
URG
B tells A it accepts, and is ready to hear the next byte…
… upon receiving this packet, A can start sending data
Flags

## Slide 70: Step 3: A’s ACK of the SYN-ACK
A’s port
B’s port
B’s ISN plus 1
Advertised window
20B
Flags
0
Checksum
Urgent pointer
Options (variable)
Flags:
SYN
ACK
FIN
RST
PSH
URG
A tells B it’s likewise okay to start sending
A’s Initial Sequence Number
… upon receiving this packet, B can start sending data

## Slide 71: Timing Diagram: 3-Way Handshaking
Client (initiator)
Server
SYN, SeqNum = x
SYN + ACK, SeqNum = y, Ack = x + 1
ACK, Ack = y + 1
Active Open
Passive Open
connect()
listen()
accept()

## Slide 72: What if the SYN Packet Gets Lost?
Suppose the SYN packet gets lost
  Packet is lost inside the network, or:
  Server discards the packet (e.g., listen queue is full)
Eventually, no SYN-ACK arrives
  Sender sets a timer and waits for the SYN-ACK
  … and retransmits the SYN if needed
How should the TCP sender set the timer?
  Sender has no idea how far away the receiver is
  Hard to guess a reasonable length of time to wait
  SHOULD (RFCs 1122 & 2988) use default of 3 seconds
    Other implementations instead use 6 seconds

## Slide 73: SYN Loss and Web Downloads
User clicks on a hypertext link
  Browser creates a socket and does a “connect”
  The “connect” triggers the OS to transmit a SYN
If the SYN is lost…
  3-6 seconds of delay: can be very long
  User may become impatient
  … and click the hyperlink again, or click “reload”
User triggers an “abort” of the “connect”
  Browser creates a new socket and another “connect”
  Essentially, forces a faster send of a new SYN packet!
  Sometimes very effective, and the page comes quickly

## Slide 74: Tearing Down the Connection

## Slide 75: Normal Termination, One Side At A Time
Finish (FIN) to close and receive remaining bytes
  FIN occupies one octet in the sequence space
Other host ack’s the octet to confirm
Closes A’s side of the connection, but not B’s
  Until B likewise sends a FIN
  Which A then acks
SYN
SYN ACK
ACK
Data
FIN
ACK
ACK
time
A
B
FIN
ACK
Timeout:
Avoid reincarnation
B will retransmit FIN if ACK is lost
Connection now half-closed
Connection now closed
Notes: Why timer? Will get packet with no state!!

## Slide 76: Normal Termination, Both Together
Same as before, but B sets FIN with their ack of A’s FIN
SYN
SYN ACK
ACK
Data
FIN
FIN + ACK
ACK
time
A
B
ACK
Connection now closed
Timeout:
Avoid reincarnation
Can retransmit FIN ACK if ACK lost

## Slide 77: Abrupt Termination
A sends a RESET (RST) to B
  E.g., because app. process on A crashed
That’s it
  B does not ack the RST
  Thus, RST is not delivered reliably
  And: any data in flight is lost
  But: if B sends anything more, will elicit another RST
SYN
SYN ACK
ACK
Data
RST
ACK
time
A
B
Data
RST

## Slide 78: TCP State Transitions
Data, ACK exchanges are in here

## Slide 79: An Simpler View of the Client Side
CLOSED
TIME_WAIT
FIN_WAIT2
FIN_WAIT1
ESTABLISHED
SYN_SENT
SYN (Send)
Rcv. SYN+ACK, Send ACK
Send FIN
Rcv. ACK, Send Nothing
Rcv. FIN, Send ACK