## Slide 1: Routers: Fair Sharing
CS 353
Spring 2016
Alefiya Hussain

## Slide 2: Announcements:
Assignment 3 Due: 4/22
Homework 2: Due 4/29 at 10am
Quiz 4 Grades Up
Avoid a 50% score reduction by:
1. Include a Makefile
2. The executable has to be named "watchdog" or "desman" and should accept any order of command line parameters
3. Executable has to be generated in the same location as the makefile
4. Flushing when writing to logfiles or before quitting while reading an interface.
5. Code has to work on on Ubuntu or Mac (please ensure the latest version of xcode for Mac and gcc for Ubuntu)
6. Assignment description: page 2 say "UID can be"  "UID must be"
7. Do not include the angle bracket "<" and ">" in logfile.

## Slide 3: How can routers ensure each flow gets its “fair share”?

## Slide 4: Isolation
Treat each “flow” separately
  For now, flows are packets between same Source/Dest.
Each flow has its own FIFO queue in router
Service flows in a round-robin fashion
  When line becomes free, take packet from next flow
Assuming all flows are sending MTU packets, all flows can get their fair share

## Slide 5: Benefits
Each flow can use their own adjustment algorithm
  Perhaps aided by the router telling them how fast to send
This solves the innovation problem!
  People can experiment with any CC algorithm
And the cheating problem!
  No matter what you do, you can’t get more than your share

## Slide 6: Four Challenges
What is fair?
How to implement fairness in general
  Going beyond round-robin
Are there simpler ways to implement this?
And what’s wrong with this approach?

## Slide 7: Four Challenges
What is fair?
How to implement fairness in general
  Going beyond round-robin
Are there simpler ways to implement this?
And what’s wrong with this approach?

## Slide 8: Fairness
When all flows want the same rate, fair is easy
  Fair share = C/N
  C = capacity of link
  N = number of flows
Notes:
  This is fair share per link. This is not a global fair share.
When not all flows have the same demand?
  Either flow isn’t high bandwidth
  Or limited by C/N on some other link

## Slide 9: Example 1
Requests: ri Allocations: ai
C=20
  Requests: r1=6, r2=5, r3=4
Solution: a1=6, a2=5, a3=4
When bandwidth is plentiful, everyone gets their request
This is the easy case

## Slide 10: Example 2
C=12
  Requests: r1=6, r2=5, r3=4
One solution: a1=4, a2=4, a3=4
  Everyone gets the same
Why not proportional to their demands?
  ai = (12/15)ri
Asking for more gets you more!
  Not incentive compatible (i.e., cheating works)

## Slide 11: Example 3
C=14; Requests: r1=6, r2=5, r3=4
a3=4 (can’t give more than a flow wants)
Remaining bandwidth is 10, with demands 6 and 5
  From previous example, if both want more than their share, they both get half
  a1=a2=5

## Slide 12: Max-Min Fairness
Given set of bandwidth demands ri and total bandwidth C, max-min bandwidth allocations are:
ai = min(f, ri)
where f is the unique value such that Sum(ai) = C
or set f to be infinite if no such value exists
This is what round-robin service gives
  if all packets are MTUs
Property:
  If you don’t get full demand, no one gets more than you
  Use it or lose it: you don’t get credit for not using link

## Slide 13: Example
Assume link speed C is 10mbps
Have three flows:
  Flow 1 is sending at a rate 8mbps
  Flow 2 is sending at a rate 6mbps
  Flow 3 is sending at a rate 2mbps
How much bandwidth should each get?
  According to max-min fairness?

## Slide 14: Example
C = 10; r1 = 8, r2 = 6, r3 = 2; N = 3
C/3 = 3.33 
  Can service all of r3
  Remove r3 from the accounting: C = C – r3 = 8; N = 2
C/2 = 4 
  Can’t service all of r1 or r2
  So hold them to the remaining fair share: f = 4
8
6
2
4
4
2
f = 4:
min(8, 4) = 4
min(6, 4) = 4
min(2, 4) = 2
10

## Slide 15: Four Challenges
What is fair?
How to implement fairness in general
  Going beyond round-robin
Are there simpler ways to implement this?
And what’s wrong with this approach?

## Slide 16: Dealing with different packet sizes
Mental model: Bit-by-bit round robin (“fluid flow”)
Can you do this in practice?
No, packets cannot be preempted
But we can approximate it
  This is what “fair queuing” routers do

## Slide 17: Fair Queuing (FQ)
For each packet, compute the time at which the last bit of a packet would have left the router if flows are served bit-by-bit
Then serve packets in the increasing order of their deadlines

## Slide 18: Example
1
2
3
4
5
1
2
3
4
1
2
3
1
2
4
3
4
5
5
6
1
2
1
3
2
3
4
4
5
6
5
5
6
Flow 1
(arrival traffic)
Flow 2
(arrival traffic)
Service
in fluid flow
system
FQ Packet
system
time
time
time
time

## Slide 19: Fair Queuing (FQ)
Implementation of round-robin generalized to case where not all packets are MTUs
Weighted fair queueing (WFQ) lets you assign different flows different shares
WFQ is implemented in almost all routers
  Not true in the 1980-90s, when CC was being developed
  Mostly used to isolate larger granularities (e.g., per-prefix)

## Slide 20: FQ vs. FIFO
FQ advantages:
  : cheating flows don’t benefit
  Bandwidth share does not depend on RTT
  Flows can pick any rate adjustment scheme they want
Disadvantages:
  More complex than FIFO: per flow queue/state, additional per-packet book-keeping

## Slide 21: Four Challenges
What is fair?
How to implement fairness in general
  Going beyond round-robin
Are there simpler ways to implement this?
And what’s wrong with this approach?

## Slide 22: Fairness Through Dropping
Traditional FQ uses scheduling to achieve fairness
But note that dropping is sufficient to give fairness
Assume a set of incoming rates ri
Dropping at rates pi yields fairness
ri(1-pi) = f

## Slide 23: Two Dropping Approaches
Estimate rate ri at edge, stick in packet header
  Then individual routers drop with probability 1=f/ri
  Where each router computes its own f
Estimate rate at every router using “shadow buffer”
  See how many packets of a flow are in shadow buffer
  Use this to estimate ri
  Why does this work?
  Implemented on significant fraction of Cisco product line

## Slide 24: Four Challenges
What is fair?
How to implement fairness in general
  Going beyond round-robin
Are there simpler ways to implement this?
And what’s wrong with this approach?

## Slide 25: Giving equal shares to “flows” is silly
What if you have 8 flows, and I have 4…
  Why should you get twice the bandwidth?
What if your flow goes over 4 congested hops, and mine only goes over 1?
  Why not penalize for using more scarce bandwidth?
And what is a flow anyway?
  TCP connection
  Source-Destination pair?
  Source?

## Slide 26: Charge people for congestion!
Use ECN as congestion markers
Whenever I get ECN bit set, I have to pay $$$
No debate over what a flow is, or what fair is…
Idea started by Frank Kelly, backed by much math
  Great idea: simple, elegant, effective
  Hard to practice

## Slide 27: Summary of Router Assisted CC
Adjustment: helps get flows up to speed
  Huge improvement in FTC performance
Isolation: helps protect flows from cheaters
  Gives each flow fair share
  Allows innovation in CC algorithms