## Slide 1: TCP: Concept of Fair Sharing
CS 353
Spring 2016
Alefiya Hussain

## Slide 2: Announcements:
Assignment 3 Due: 4/22
Homework 2: Given Today Due 4/29 at 10am
Discussed in the discussion at 12noon.
Avoid a 50% score reduction by:
1. Include a Makefile
2. The executable has to be named "watchdog" or "desman" and should accept any order of command line parameters
3. Executable has to be generated in the same location as the makefile
4. Flushing when writing to logfiles or before quitting while reading an interface.
5. Code has to work on on Ubuntu or Mac (please ensure the latest version of xcode for Mac and gcc for Ubuntu)
6. Assignment description: page 2 say "UID can be"  "UID must be"
7. Do not include the angle bracket "<" and ">" in logfile.

## Slide 3
The Transport Layer
(brief review from last lecture)

## Slide 4: What Is Needed to Address These?
Demultiplexing: identifier for application process
  Going from host-to-host (IP) to process-to-process
Translating between bytestreams and packets
  Do segmentation and reassembly
Reliability: ACKs and all that stuff
Corruption: checksum
Not overloading receiver: “Flow Control”
  Limit data in recvr’s buffer
Not overloading network: “Congestion Control”
  Limit data based on network capacity

## Slide 5: Recall: Three Issues
Discovering the available (bottleneck) bandwidth
  Slow Start
Adjusting to variations in bandwidth
  AIMD
Sharing bandwidth between flows

## Slide 6: Bandwidth Discovery with Slow Start
Goal: estimate available bandwidth
  start slow (for safety)
  but ramp up quickly (for efficiency)
For each RTT: double CWND
Simpler implementation: for each ACK, CWND += 1

## Slide 7: AIMD
Additive increase
  Window grows by one MSS for every RTT with no loss
  For each successful RTT, CWND = CWND + 1
  Simple implementation:
    for each ACK, CWND = CWND+ 1/CWND
Multiplicative decrease
  On loss of packet, divide congestion window in half
  On loss, CWND = CWND/2

## Slide 8: Slow-Start vs. AIMD
What are two ways to stop Slow start?
Loss: DupACK
Introduce a “slow start threshold” (ssthresh)
  Initialized to a large value
  On timeout, ssthresh = CWND/2
When CWND = ssthresh, sender switches from slow-start to AIMD-style increase

## Slide 9: TCP Throughput Equation

## Slide 10: A Simple Model for TCP Throughput
A
Loss
time
cwnd
1
RTT
½ Wmax RTTs between drops
Avg. ¾ Wmax packets per RTTs

## Slide 11: A Simple Model for TCP Throughput
A
Loss
time
cwnd
½ Wmax RTTs between drops
Avg. ¾ Wmax packets per RTTs

## Slide 12
Last Lecture
  TCP Congestion control: the gory details
Today
  Wrap-up CC details (fast retransmit)
  Critically examining TCP
  Advanced techniques

## Slide 13: A Critical Analysis of TCP

## Slide 14: The Many Failings of TCP CC
Cumulative ACKs are silly
Fills up queues (large delays)
Depends on losses (noncongestive losses)
Does not scale to high-speed
Produces irregular saw-tooth behavior
Depends on RTT (unfair)
Takes a long time to reach steady state
Easy to cheat
Relies on homogeneity for performance/fairness

## Slide 15: (1) Cumulative ACK Stupidity
When we have cumulative ACKs, we must:
  Guess which data has arrived
  Play games with CWND to send additional packets
TCP SACK:
  Selective Acknowledgements
    Think: complete listing of all received packets
  Would remove need for “fast recovery”
Could design very simple CC algorithm
  Just slow-start, congestion avoidance, fast-retransmit
  Much more robust to drops (almost never time out)

## Slide 16: (2) TCP fills up queues
TCP only slows down when queues fill up
Means that delays are large for everyone
And many packets are dropped when buffer fills
  Not always, but it does tend to increase packet drops
Alternative: Random Early Drop (Sally Floyd)
  Drop packets on purpose before queue is full

## Slide 17: Random Early Drop (or Detection)
Measure avg queue size A with exp. weighting
  Allows short bursts of packets without over-reacting
Drop probability is a function of A
  No drops if A is very small
  Low drop rate for moderate A’s
  Drop everything if A is too big
Drop probability applied to incoming packets
Intuition: link is fully utilized well before buffer is full

## Slide 18: RED Dropping Probability

## Slide 19: Advantages of RED
Keeps queues smaller, while allowing bursts
  Just using small buffers in routers can’t do the latter
Reduces synchronization between flows
  Not all flows are dropping packets at once
  Increase/decrease are more gentle

## Slide 20: Why Isn’t RED Fair?
RED gives all flows roughly the same drop rate
The TCP equation gives the following
Resulting throughputs depend on RTT…

## Slide 21: (3) Non-congestion-related Losses?
Can use Explicit Congestion Notification (ECN)
Bit in IP packet header (actually two)
  TCP receiver returns this bit in ACK
When RED router would drop, it sets bit instead
  Congestion semantics of bit exactly like that of drop
Advantages:
  Separate corruption from congestion
  Separate recovery from rate adjustment

## Slide 22: (4) Does AIMD work at high speed?
Throughput = (MSS/RTT) sqrt(3/2p)
  Assume that RTT = 100ms, MSS=1500bytes
What value of p is required to go 100Gbps?
  Roughly 2 x 10-12
How long between drops?
  Roughly 16.6 hours
How much data has been sent in this time?
  Roughly 6 petabits
These are not practical numbers!

## Slide 23: Adapting TCP to High Speed
One approach:
  Let AIMD “constants” depend on CWND
At very high speeds,
  Increase CWND by more than MSS in a RTT
  Decrease CWND by less than ½ after a loss
We will discuss other approaches later…

## Slide 24: High-Speed TCP Proposal (Floyd)
Bandwidth | AvgCwnd (pkts) | Increase a(w) | Decrease b(w)
1.5 Mbps | 12.5 | 1 | 0.50
10 Mbps | 83 | 1 | 0.50
100 Mbps | 833 | 6 | 0.35
1 Gbps | 8333 | 26 | 0.22
10 Gbps | 83333 | 70 | 0.10

## Slide 25: High-Speed TCP

## Slide 26: This changes the TCP Equation
Throughput ~ p-.8 (rather than p-.5)
  Packet drops every tens of seconds
To achieve high throughput:
  Don’t need such a tiny drop rate…
  Can ramp up more quickly
How can this coexist with normal TCP?
  Only invoke new parameters at large window sizes
  Competes fairly with normal TCP at normal speeds

## Slide 27: (5) Sawtooth Behavior Uneven
TCP throughput is “choppy”
  Repeated swings between W/2 to W
Some apps would prefer sending at a steady rate
  e.g., streaming apps
A solution: “Equation-Based Congestion Control”
  Ditch TCP’s increase/decrease rules and just follow the equation
  Measure drop percentage p, and set rate accordingly
Following the TCP equation ensures we’re “TCP friendly”
  i.e., use no more than TCP does in similar setting

## Slide 28: These Problems Are All Solved
With published and often standardized solutions
TCP-SACK
RED (and its many variants)
ECN
High-Speed TCP
Equation-based congestion control (EBCC)
Datagram congestion control protocol (DCCP)
Not widely used, as far as I know (but Apple just adopted ECN a few months ago!)

## Slide 29: (6) Bias Against Long RTTs
Flows get throughput inversely proportional to RTT
TCP unfair in the face of heterogeneous RTTs!
A1
A2
B2
B1
bottleneck
link
100ms
200ms

## Slide 30: Possible Solutions?
Make additive constant proportional to RTT
But people don’t really care about this….

## Slide 31: (7) How do short flows fare?
50% of flows have < 1500B to send; 80% < 100KB
Short flows are slowed down by slow-start
  It takes several round-trips to send 8 packets!
    Handshake, CWND=1, CWND=2, CWND=4, CWND=8
Too few packets to trigger dupACKs
  Isolated loss may lead to timeouts
At typical timeout values of ~500ms…
  ...might severely impact flow completion time

## Slide 32: Possible Solutions?
Larger initial window?
  Google proposed moving from ~4KB to ~15KB
  Covers ≈90% of HTTP Web
  Decreases delay by ~5%
Recursively cautious congestion control (RC3)
  Run normal TCP at normal priority
  Send aggressively at lower priorities
  With a limit on each priority level
  Ramps up to full speed immediately, no harm to others

## Slide 33: (8) Cheating
TCP was designed assuming a cooperative world
No attempt was made to prevent cheating
Many ways to cheat, will present three

## Slide 34: Cheating #1: ACK-splitting (Rcvr)
Round-
Trip
Time
(RTT)
Sender
Receiver
ACK 486
Data 4381:5841
Data 1461:2921
Data 2921:4381
Data 5841:7301
ACK 973
ACK 1461
Data 1:1461
Rule: grow window by one
full-sized packet for each
valid ACK received
Send M (distinct) ACKs for one packet
Growth factor proportional
to M
What’s the fix?

## Slide 35: 10 line change to Linux TCP
(Courtesy of
Stefan Savage)

## Slide 36: Cheating #2: Increasing CWND Faster
Limit rates:
x = 2y
C
x
y
x increases by 2 per RTT
y increases by 1 per RTT

## Slide 37: Cheating #3: Open Many Connections
A
B
x
D
E
y
Assume
A starts 10 connections to B
D starts 1 connection to E
Each connection gets about the same throughput
Then A gets 10 times more throughput than D

## Slide 38: Cheating
Either sender or receiver can independently cheat!
Why hasn’t Internet suffered congestion collapse yet?
How can we prevent cheating?
  Verify TCP implementations?
  Controlling end points is hopeless!
So what should we do?

## Slide 39: (9) Converse of Cheating
To be fair, need to be TCP-friendly
Everyone uses “similar” CC algorithm
Slows down innovation!

## Slide 40: How do you solve these problems?
Bias against long RTTs
Slow to ramp up (for short flows)
Cheating
Need for uniformity

## Slide 41: Get the Network Involved!
Routers can help by:
  Providing guidance for speed to send at
  Providing isolation/fairness
Guidance for sending rate deals with
  Slow to ramp up
  Bias against long RTTs
Providing Isolation/Fairness deals with
  Cheating
  Need for uniformity

## Slide 42: Routers tell hosts how fast to send
Packets carry “rate field”
Routers insert “fair share” f in packet header
End-hosts set sending rate (or window size) to f
  Hopefully (still need some policing of endhosts!)
This is the basic idea behind the “Rate Control Protocol” (RCP) from Dukkipati et al. ’07

## Slide 43: A Few More Details
How does this work?
  Router estimates rate f that will use its capacity
  Adaptive process of guessing (why not exact?)
  This is what it tells hosts
Why does this work?
  Flows get immediately up to speed
  And no need to “probe” (gently or otherwise)
How do you evaluate the resulting performance?

## Slide 44: Why the improvement?

## Slide 45: How can routers ensure each flow gets its “fair share”?

## Slide 46: Isolation
Treat each “flow” separately
  For now, flows are packets between same Source/Dest.
Each flow has its own FIFO queue in router
Service flows in a round-robin fashion
  When line becomes free, take packet from next flow
Assuming all flows are sending MTU packets, all flows can get their fair share

## Slide 47: Benefits
Each flow can use their own adjustment algorithm
  Perhaps aided by the router telling them how fast to send
This solves the innovation problem!
  People can experiment with any CC algorithm
And the cheating problem!
  No matter what you do, you can’t get more than your share

## Slide 48: Four Challenges
What is fair?
How to implement fairness in general
  Going beyond round-robin
Are there simpler ways to implement this?
And what’s wrong with this approach?

## Slide 49: Four Challenges
What is fair?
How to implement fairness in general
  Going beyond round-robin
Are there simpler ways to implement this?
And what’s wrong with this approach?

## Slide 50: Fairness
When all flows want the same rate, fair is easy
  Fair share = C/N
  C = capacity of link
  N = number of flows
Notes:
  This is fair share per link. This is not a global fair share.
When not all flows have the same demand?
  Either flow isn’t high bandwidth
  Or limited by C/N on some other link

## Slide 51: Example 1
Requests: ri Allocations: ai
C=20
  Requests: r1=6, r2=5, r3=4
Solution: a1=6, a2=5, a3=4
When bandwidth is plentiful, everyone gets their request
This is the easy case

## Slide 52: Example 2
C=12
  Requests: r1=6, r2=5, r3=4
One solution: a1=4, a2=4, a3=4
  Everyone gets the same
Why not proportional to their demands?
  ai = (12/15)ri
Asking for more gets you more!
  Not incentive compatible (i.e., cheating works)

## Slide 53: Example 3
C=14; Requests: r1=6, r2=5, r3=4
a3=4 (can’t give more than a flow wants)
Remaining bandwidth is 10, with demands 6 and 5
  From previous example, if both want more than their share, they both get half
  a1=a2=5

## Slide 54: Max-Min Fairness
Given set of bandwidth demands ri and total bandwidth C, max-min bandwidth allocations are:
ai = min(f, ri)
where f is the unique value such that Sum(ai) = C
or set f to be infinite if no such value exists
This is what round-robin service gives
  if all packets are MTUs
Property:
  If you don’t get full demand, no one gets more than you
  Use it or lose it: you don’t get credit for not using link

## Slide 55: Example
Assume link speed C is 10mbps
Have three flows:
  Flow 1 is sending at a rate 8mbps
  Flow 2 is sending at a rate 6mbps
  Flow 3 is sending at a rate 2mbps
How much bandwidth should each get?
  According to max-min fairness?

## Slide 56: Example
C = 10; r1 = 8, r2 = 6, r3 = 2; N = 3
C/3 = 3.33 
  Can service all of r3
  Remove r3 from the accounting: C = C – r3 = 8; N = 2
C/2 = 4 
  Can’t service all of r1 or r2
  So hold them to the remaining fair share: f = 4
8
6
2
4
4
2
f = 4:
min(8, 4) = 4
min(6, 4) = 4
min(2, 4) = 2
10

## Slide 57: Four Challenges
What is fair?
How to implement fairness in general
  Going beyond round-robin
Are there simpler ways to implement this?
And what’s wrong with this approach?