## Slide 1: TCP: More Congestion Control
CS 353
Spring 2016
Alefiya Hussain

## Slide 2: Announcements:
Assignment 3 Due: 4/22
Quiz 3: Tomorrow 4/15
Avoid a 50% score reduction by:
1. Include a Makefile
2. The executable has to be named "watchdog" or "desman" and should accept any order of command line parameters
3. Executable has to be generated in the same location as the makefile
4. Flushing when writing to logfiles or before quitting while reading an interface.
5. Code has to work on on Ubuntu or Mac (please ensure the latest version of xcode for Mac and gcc for Ubuntu)
6. Assignment description: page 2 say "UID can be"  "UID must be"
7. Do not include the angle bracket "<" and ">" in logfile.

## Slide 3
The Transport Layer
(brief review from last lecture)

## Slide 4: Role of Transport Layer
Application layer
  Communication for specific applications
  E.g., HyperText Transfer Protocol (HTTP), File Transfer Protocol (FTP), Simple Mail Transfer Protocol (SMTP)
Transport layer
  What do we need here?
Network layer
  Logical communication between nodes
  Hides details of the link technology, ex: IP

## Slide 5: What Is Needed to Address These?
Demultiplexing: identifier for application process
  Going from host-to-host (IP) to process-to-process
Translating between bytestreams and packets
  Do segmentation and reassembly
Reliability: ACKs and all that stuff
Corruption: checksum
Not overloading receiver: “Flow Control”
  Limit data in recvr’s buffer
Not overloading network: “Congestion Control”
  Limit data based on network capacity

## Slide 6: Timeouts and Retransmissions
Reliability requires retransmitting lost data
Involves setting timer and retransmitting on timeout
TCP resets timer whenever new data is ACKed
  Retx of packet containing “next byte” when timer goes off

## Slide 7: Setting the Timeout Value
1
1
Timeout too long  inefficient
1
1
Timeout too short 
duplicate packets
RTT
Timeout
Timeout
RTT

## Slide 8: RTT Estimation
Use exponential averaging of RTT samples
EstimatedRTT
Time
SampleRTT

## Slide 9: Karn/Partridge Algorithm
Measure SampleRTT only for original transmissions
  Once a segment has been retransmitted, do not use it for any further measurements
  Computes EstimatedRTT using α = 0.875
Timeout value (RTO) = 2 × EstimatedRTT
Use exponential backoff for repeated retransmissions
  Every time RTO timer expires, set RTO  2·RTO
    (Up to maximum  60 sec)
  Every time new measurement comes in (= successful original transmission), collapse RTO back to 2 × EstimatedRTT

## Slide 10: Jacobson/Karels Algorithm
Problem: need to better capture variability in RTT
  Directly measure deviation
Deviation = | SampleRTT – EstimatedRTT |
EstimatedDeviation: exponential average of Deviation
RTO = EstimatedRTT + 4 x EstimatedDeviation

## Slide 11
Advertised Window
  Flow control: adjusting the sending rate to keep from overwhelming a slow receiver
Self-Clocking
  Congestion control: adjusting the sending rate to keep from overloading the network

## Slide 12: Statistical Multiplexing  Congestion
If two packets arrive at a router at the same time
  Router will transmit one and buffer/drop the other
Internet traffic is bursty
If many packets arrive close in time
  the router cannot keep up  gets congested
  causes packet delays and drops

## Slide 13: Congestion is Harmful
Average
Packet
delay
Load
Typical queuing system with bursty arrivals
Must balance utilization versus delay and loss
Average
Packet
loss
Load

## Slide 14: TCP’s Approach in a Nutshell
TCP connection has window
  Controls number of packets in flight
Sending rate: ~Window/RTT
Vary window size to control sending rate

## Slide 15: All These Windows…
Congestion Window: CWND
  How many bytes can be sent without overflowing routers
  Computed by the sender using congestion control algorithm
Flow control window: AdvertisedWindow (RWND)
  How many bytes can be sent without overflowing receiver’s buffers
  Determined by the receiver and reported to the sender
Sender-side window = minimum{CWND, RWND}
    Assume for this lecture that RWND >> CWND

## Slide 16: Two Basic Questions
How does the sender detect congestion?
How does the sender adjust its sending rate?
  To address three issues
    Finding available bottleneck bandwidth
    Adjusting to bandwidth variations
    Sharing bandwidth

## Slide 17: Detecting Congestion
Packet delays
  Tricky: noisy signal (delay often varies considerably)
Routers tell endhosts when they’re congested
Packet loss
  Fail-safe signal that TCP already has to detect
  Complication: non-congestive loss (e.g., checksum errors)

## Slide 18: Not All Losses the Same
Duplicate ACKs: isolated loss
  Still getting ACKs
Timeout: much more serious
  Not enough dupacks
  Must have suffered several losses
Will adjust rate differently for each case

## Slide 19: Rate Adjustment
Basic structure:
  Upon receipt of ACK (of new data): increase rate
  Upon detection of loss: decrease rate
How we increase/decrease the rate depends on the phase of congestion control we’re in:
  Discovering available bottleneck bandwidth vs.
  Adjusting to bandwidth variations

## Slide 20: Bandwidth Discovery with Slow Start
Goal: estimate available bandwidth
  start slow (for safety)
  but ramp up quickly (for efficiency)
Consider
  RTT = 100ms, MSS=1000bytes
  Window size to fill 1Mbps of BW = 12.5 packets
  Window size to fill 1Gbps = 12,500 packets
  Either is possible!

## Slide 21: “Slow Start” Phase
Sender starts at a slow rate but increases exponentially until first loss
Start with a small congestion window
  Initially, CWND = 1
  So, initial sending rate is MSS/RTT
Double the CWND for each RTT with no loss
Notes: MSS vs MTU??

## Slide 22: Slow Start in Action
For each RTT: double CWND
Simpler implementation: for each ACK, CWND += 1
Linear increase per ACK(CWND+1)  exponential increase per RTT (2xCWND)

## Slide 23: Slow Start in Action
For each RTT: double CWND
Simpler implementation: for each ACK, CWND += 1
D
A
D
D
A
A
D
D
Src
Dest
D
D
1
2
4
3
A
A
A
A
8

## Slide 24: Adjusting to Varying Bandwidth
Slow start gave an estimate of available bandwidth
Now, want to track variations in this available bandwidth, oscillating around its current value
  Repeated probing (rate increase) and backoff (decrease)
TCP uses: “Additive Increase Multiplicative Decrease” (AIMD)
  We’ll see why shortly…

## Slide 25: AIMD
Additive increase
  Window grows by one MSS for every RTT with no loss
  For each successful RTT, CWND = CWND + 1
  Simple implementation:
    for each ACK, CWND = CWND+ 1/CWND
Multiplicative decrease
  On loss of packet, divide congestion window in half
  On loss, CWND = CWND/2

## Slide 26: Leads to the TCP “Sawtooth”
Loss
Exponential “slow start”
t
Window

## Slide 27: Slow-Start vs. AIMD
When does a sender stop Slow-Start and start Additive Increase?
Introduce a “slow start threshold” (ssthresh)
  Initialized to a large value
  On timeout, ssthresh = CWND/2
When CWND = ssthresh, sender switches from slow-start to AIMD-style increase

## Slide 28: Why AIMD?

## Slide 29: Recall: Three Issues
Discovering the available (bottleneck) bandwidth
  Slow Start
Adjusting to variations in bandwidth
  AIMD
Sharing bandwidth between flows

## Slide 30: Goals for bandwidth sharing
Efficiency: High utilization of link bandwidth
Fairness: Each flow gets equal share

## Slide 31: Why AIMD?
Some rate adjustment options: Every RTT, we can
  Multiplicative increase or decrease: CWND a*CWND
  Additive increase or decrease: CWND CWND + b
Four alternatives:
  AIAD: gentle increase, gentle decrease
  AIMD: gentle increase, drastic decrease
  MIAD: drastic increase, gentle decrease
  MIMD: drastic increase and decrease

## Slide 32: Simple Model of Congestion Control
User 1’s rate (x1)
User 2’s rate (x2)
Fairness line (x1 =x2)
Efficiency line (x1+x2 = 1)
1
1
Two users
  rates x1 and x2
Congestion when x1+x2 > 1
Unused capacity when x1+x2 < 1
Fair when x1 =x2
congested 
 inefficient

## Slide 33: Example
User 1: x1
User 2: x2
fairness
line
efficiency
line
1
1
Inefficient: x1+x2=0.7
(0.2, 0.5)
Congested: x1+x2=1.2
(0.7, 0.5)
Efficient: x1+x2=1
Fair
(0.5, 0.5)
congested 
 inefficient
Efficient: x1+x2=1
Not fair
(0.7, 0.3)

## Slide 34: AIAD
User 1: x1
User 2: x2
fairness
line
efficiency
line
(x1,x2)
(x1-aD,x2-aD)
(x1-aD+aI), x2-aD+aI))
Increase: x + aI
Decrease: x - aD
Does not converge to fairness
congested 
 inefficient

## Slide 35: AIAD Sharing Dynamics
A
B
x1
D
E
x2

## Slide 36: MIMD
User 1: x1
User 2: x2
fairness
line
efficiency
line
(x1,x2)
(bdx1,bdx2)
(bIbDx1, bIbDx2)
Increase: x*bI
Decrease: x*bD
Does not converge to fairness
congested 
 inefficient

## Slide 37: AIMD
(bDx1+aI, bDx2+aI)
User 1: x1
User 2: x2
fairness
line
efficiency
line
(x1,x2)
(bDx1,bDx2)
Increase: x+aI
Decrease: x*bD
Converges to fairness
congested 
 inefficient

## Slide 38: AIMD Sharing Dynamics
A
50 pkts/sec
B
x1
D
E
Rates equalize  fair share
x2

## Slide 39: TCP Congestion Control Details

## Slide 40: Implementation
State at sender
  CWND (initialized to a small constant)
  ssthresh (initialized to a large constant)
  [Also dupACKcount and timer, as before]
Events
  ACK (new data)
  dupACK (duplicate ACK for old data)
  Timeout

## Slide 41: Event: ACK (new data)
If CWND < ssthresh
  CWND += 1
CWND packets per RTT
Hence after one RTT with no drops: CWND = 2xCWND

## Slide 42: Event: ACK (new data)
If CWND < ssthresh
  CWND += 1
Else
  CWND = CWND + 1/CWND
Slow start phase
CWND packets per RTT
Hence after one RTT with no drops: CWND = CWND + 1
“Congestion Avoidance” phase (additive increase)

## Slide 43: Event: TimeOut
On Timeout
  ssthresh  CWND/2
  CWND  1

## Slide 44: Event: dupACK
dupACKcount ++
If dupACKcount = 3 /* fast retransmit */
  ssthresh = CWND/2
  CWND = CWND/2

## Slide 45: Example
t
Window
Slow-start restart: Go back to CWND = 1 MSS, but take advantage of knowing the previous value of CWND
Slow start in operation until it reaches half of previous CWND, I.e., SSTHRESH
Timeout
Fast Retransmission
SSThresh
Set to Here

## Slide 46: One Final Phase: Fast Recovery
The problem: congestion avoidance too slow in recovering from an isolated loss

## Slide 47: Example
Consider a TCP connection with:
  CWND=10 packets
  Last ACK was for packet # 101
    i.e., receiver expecting next packet to have seq. no. 101
10 packets [101, 102, 103,…, 110] are in flight
  Packet 101 is dropped
  What ACKs do they generate?
  And how does the sender respond?

## Slide 48: Timeline (at sender)
In flight: 101, 102, 103, 104, 105, 106, 107, 108, 109, 110
ACK 101 (due to 102) cwnd=10 dupACK#1 (no xmit)
ACK 101 (due to 103) cwnd=10 dupACK#2 (no xmit)
ACK 101 (due to 104) cwnd=10 dupACK#3 (no xmit)
RETRANSMIT 101 ssthresh=5 cwnd= 5
ACK 101 (due to 105) cwnd=5 + 1/5 (no xmit)
ACK 101 (due to 106) cwnd=5 + 2/5 (no xmit)
ACK 101 (due to 107) cwnd=5 + 3/5 (no xmit)
ACK 101 (due to 108) cwnd=5 + 4/5 (no xmit)
ACK 101 (due to 109) cwnd=5 + 5/5 (no xmit)
ACK 101 (due to 110) cwnd=6 + 1/5 (no xmit)
ACK 111 (due to 101)  only now can we transmit new packets
Plus no packets in flight so ACK “clocking” (to increase CWND) stalls for another RTT
✗
101

## Slide 49: Solution: Fast Recovery
Idea: Grant the sender temporary “credit” for each dupACK so as to keep packets in flight
If dupACKcount = 3
  ssthresh = cwnd/2
  cwnd = ssthresh + 3
While in fast recovery
  cwnd = cwnd + 1 for each additional duplicate ACK
Exit fast recovery after receiving new ACK
  set cwnd = ssthresh

## Slide 50: Timeline (at sender)
In flight: 101, 102, 103, 104, 105, 106, 107, 108, 109, 110
ACK 101 (due to 102) cwnd=10 dup#1
ACK 101 (due to 103) cwnd=10 dup#2
ACK 101 (due to 104) cwnd=10 dup#3
REXMIT 101 ssthresh=5 cwnd= 8 (5+3)
ACK 101 (due to 105) cwnd= 9 (no xmit)
ACK 101 (due to 106) cwnd=10 (no xmit)
ACK 101 (due to 107) cwnd=11 (xmit 111)
ACK 101 (due to 108) cwnd=12 (xmit 112)
ACK 101 (due to 109) cwnd=13 (xmit 113)
ACK 101 (due to 110) cwnd=14 (xmit 114)
ACK 111 (due to 101) cwnd = 5 (xmit 115)  exiting fast recovery
Packets 111-114 already in flight
ACK 112 (due to 111) cwnd = 5 + 1/5  back in congestion avoidance
✗

## Slide 51: Recap: Implementation
State at sender
  CWND (initialized to a small constant)
  ssthresh (initialized to a large constant)
Events
  ACK (new data)
  dupACK (duplicate ACK for old data)
  Timeout

## Slide 53: TCP Flavors
TCP-Tahoe
  CWND =1 on triple dupACK
TCP-Reno
  CWND =1 on timeout
  CWND = CWND/2 on triple dupack
TCP-newReno
  TCP-Reno + improved fast recovery
TCP-SACK
  incorporates selective acknowledgements
Our default assumption