## Slide 1: Datacenters
CS353
Alefiya Hussain

## Slide 2: What you need to know
Characteristics of a datacenter environment
  goals, constraints, workloads, etc.
How and why DC networks are different (vs. WAN)
  e.g., latency, geo, autonomy, …
How traditional solutions fare in this environment
  e.g., IP, Ethernet, TCP, ARP, DHCP
Specific design approaches we cover in class

## Slide 3: Disclaimer
Material is emerging (not established) wisdom
Material is incomplete
  many details on how and why datacenter networks operate aren’t public

## Slide 4: Plan
Today
Characteristics and goals of datacenter networks
Focus on differences relative to the Internet
Explore
Emerging solutions

## Slide 5: What goes into a datacenter (network)?
Servers organized in racks

## Slide 6: What goes into a datacenter (network)?
Servers organized in racks
Each rack has a `Top of Rack’ (ToR) switch

## Slide 7: What goes into a datacenter (network)?
Servers organized in racks
Each rack has a `Top of Rack’ (ToR) switch
`Aggregation switches interconnect ToR switches

## Slide 8: What goes into a datacenter (network)?
Servers organized in racks
Each rack has a `Top of Rack’ (ToR) switch
`Aggregation switches interconnect ToR switches
Connected to the outside via `core’ switches
  note: blurry line between aggregation and core
With 2x redundancy for fault-tolerance

## Slide 9: E.g., Brocade Reference Design

## Slide 10: E.g., Cisco Reference Design
CR
CR
AR
AR
AR
AR
. . .
S
S
Internet
S
S
A
A
A
…
S
S
A
A
A
…
. . .
~ 40-80 servers/rack

## Slide 11: Datacenters have been around for a while
1961, Information Processing Center at the National Bank of Arizona

## Slide 12: What’s new?

## Slide 13: What’s new?
Scale
Applications
  Large-scale computations (“big data”)
  Customer-facing, revenue generating services
Service model
  Clouds (jargon: SaaS, PaaS, DaaS, IaaS, …)
  Multi-tenancy

## Slide 14: SCALE!

## Slide 15: How big exactly?
1M servers/site [Microsoft/Amazon/Google]
> $1B to build one site [Facebook]
>$20M/month/site operational costs [Microsoft ’09]
But only O(10-100) sites

## Slide 16: Implications (1)
Scale
  Need scalable designs (duh): e.g., avoid flooding
  Low cost designs: e.g., use commodity technology
  High utilization (efficiency): e.g., >80% avg. utilization
    Contrast: avg. utilization on Internet links often ~30%
  Tolerate frequent failure
    Large number of (low cost) components
  Automate

## Slide 17: Implications (2)
Service model: clouds / multi-tenancy
  performance guarantees
  isolation guarantees
  portability
  Network Virtualization – SDN

## Slide 18: Applications
Common theme: parallelism
  Applications decomposed into tasks
  Running in parallel on different machines
Two common paradigms
  “Partition Aggregate”
  Map Reduce

## Slide 19: Partition-Aggregate
Router / Load Balancer
Web Server
Web Server
Web Server
Data
Cache
Data
Cache
Database
Database
Front-End
Proxy
Front-End
Proxy
user requests from the Internet

## Slide 20: “North – South” Traffic
Interactive / query-response exchange between external clients and datacenter
Handled by front-end (web) servers, mid-tier application servers, and back-end databases

## Slide 21: Map-Reduce
Distributed
Storage
Distributed
Storage
Map
Tasks
Reduce
Tasks

## Slide 22: Map-Reduce
Distributed
Storage
Distributed
Storage
Map
Tasks
Reduce
Tasks
Often doesn’t cross the network
Always goes over the network
Some fraction (typically 2/3) crosses the network

## Slide 23: “East-West” Traffic
CR
CR
AR
AR
AR
AR
S
S
S
S
A
A
A
…
S
S
A
A
A
…
. . .
S
S
S
S
A
A
A
…
S
S
A
A
A
…

## Slide 24: “East-West” Traffic
Traffic between servers in the datacenter
Communication within “big data” computations
Traffic may shift on small timescales (< minutes)

## Slide 25: Common traffic pattern: “Elephants” and “Mice”
55% of flows
3% of bytes
5% of flows
35% of bytes
<100KB
>10MB
  Web search, data mining (Microsoft) [Alizadeh 2010]

## Slide 26: Implications (3)
Applications
  High bandwidth any-to-any communication (“bisection bandwidth”)
  Low latency is critical
  Worst-case (“tail”) latency is critical

## Slide 27: High Bandwidth
Ideal: Each server can talk to any other server at its full access link rate
Conceptually: DC network as one giant switch

## Slide 28: DC Network: Just a Giant Switch!
H1
H2
H3
H4
H5
H6
H7
H8
H9

## Slide 29: DC Network: Just a Giant Switch!
H1
H2
H3
H4
H5
H6
H7
H8
H9
H1
H2
H3
H4
H5
H6
H7
H8
H9
H1
H2
H3
H4
H5
H6
H7
H8
H9
TX
RX

## Slide 30: DC Network: Just a Giant Switch!
H1
H2
H3
H4
H5
H6
H7
H8
H9
H1
H2
H3
H4
H5
H6
H7
H8
H9
TX
RX

## Slide 31: High Bandwidth
Ideal: Each server can talk to any other server at its full access link rate
Conceptually: DC network as one giant switch
  Would require a 10 Pbits/sec switch!
    1M ports (one port/server)
    10Gbps per port
Practical approach: build a network of switches (“fabric”) with high “bisection bandwidth”
  Each switch has practical #ports and link speeds

## Slide 32: Bisection Bandwidth
Partition a network into two equal parts
Minimum bandwidth between the partitions is the bisection bandwidth
Full bisection bandwidth: bisection bandwidth in an N node network is N/2 times the bandwidth of a single link
  nodes of any two halves can communicate at full speed with each other.

## Slide 33: Achieving Full Bisection Bandwidth
CR
CR
AR
AR
AR
AR
. . .
S
S
Internet
S
S
A
A
A
…
S
S
A
A
A
…
. . .
~ 40 servers/rack
10Gbps links
O(40x10) Gbps
O(40x10x100)Gbps
“scale up” approach

## Slide 34: Achieving Full Bisection Bandwidth
Problem: “Scaling up” a traditional tree topology is expensive!
  requires non-commodity / impractical / link and switch components
Solutions?
  Over-subscribe (i.e., provision less than full BBW)
  Better topologies

## Slide 35: Oversubscription
Need techniques to avoid congesting oversubscribed links!
10G
20G
40G
10G
10G
20G

## Slide 36: Better topologies?
10G
20G
40G
“scale up” approach
“scale out” approach

## Slide 37: Better topologies?
“scale out” approach
E.g., `Clos’ topology
  Multi-stage network
  All switches have k ports
  k/2 ports up, k/2 down
E.g., with 3 stages, k=48
  k3/4 hosts = 27,648 servers
All links have same speed

## Slide 38: Low Latency
Two (related) issues:
1) Very low RTTs within the DC (approaching 1μsec)
  Implications?
  BW x delay: 10Gbps x 1μsec = 10000 bits = 2.5 packets
  Consider TX 500B @ 10Gbps = 0.4μs per hop = 2μs if a packet traverses 5 hops and waits behind one packet at every hop
  What does this mean for buffering and switch design?
  What does this mean for congestion control?

## Slide 39: Low Latency
Two (related) issues:
Very low RTTs within the DC (approaching 1μsec)
Applications want low latency
  predictable / guaranteed bounds on flow completion time, including the worst-case! (recall: `best effort’ vs. `guaranteed service’ debates)
  How is still an open question

## Slide 40: What’s different about DC networks?
Characteristics
Huge scale
  ~20,000 switches/routers
  contrast: AT&T ISP ~500 routers

## Slide 41: What’s different about DC networks?
Characteristics
Huge scale
Limited geographic scope
  High bandwidth: 10/40/100G (Contrast: DSL/WiFi)
  Very low RTT: 1-10s μsecs. (Contrast: 100s msecs)

## Slide 42: What’s different about DC networks?
Characteristics
Huge scale
Limited geographic scope
Limited heterogeneity
  link speeds, technologies, latencies, …

## Slide 43: What’s different about DC networks?
Characteristics
Huge scale
Limited geographic scope
Limited heterogeneity
Regular/planned topologies (e.g., trees)
  Contrast: ad-hoc evolution of wide-area topologies

## Slide 44: What’s different about DC networks?
Goals
Extreme bisection bandwidth requirements
  recall: all that east-west traffic
  target: any server can communicate at its full link speed

## Slide 45: What’s different about DC networks?
Goals
Extreme bisection bandwidth requirements
Extreme latency requirements
  real money on the line
  current target: 1μs RTTs

## Slide 46: What’s different about DC networks?
Goals
Extreme bisection bandwidth requirements
Extreme latency requirements
Predictable, deterministic performance
  “your packet will reach in Xms, or not at all”
  “your VM will always see at least YGbps throughput”
  How is still an open question

## Slide 47: What’s different about DC networks?
Goals
Extreme bisection bandwidth requirements
Extreme latency requirements
Predictable, deterministic performance
Differentiating between tenants is key
  e.g., “No traffic between VMs of tenant A and tenant B”
  “Tenant X cannot consume more than XGbps”
  “Tenant Y’s traffic is low priority”
  SDN

## Slide 48: What’s different about DC networks?
Goals
Extreme bisection bandwidth requirements
Extreme latency requirements
Predictable, deterministic performance
Differentiating between tenants is key
Scalability (of course)

## Slide 49: What’s different about DC networks?
Goals
Extreme bisection bandwidth requirements
Extreme latency requirements
Predictable, deterministic performance
Differentiating between tenants is key
Scalability (of course)
Cost/efficiency
  focus on commodity solutions, ease of management

## Slide 50: What’s different about DC networks?
New degrees of (design) freedom
Single administrative domain
  Can deviate from standards, invent your own, etc.
  “Green field” deployment is still feasible

## Slide 51: What’s different about DC networks?
New degrees of (design) freedom
Single administrative domain
Control over network and endpoint(s)
  can change (say) addressing, congestion control, etc.
  can add mechanisms for security/policy/etc. at the endpoints (typically in the hypervisor)

## Slide 52: What’s different about DC networks?
New degrees of (design) freedom
Single administrative domain
Control over network and endpoint(s)
Control over the placement of traffic source/sink
  e.g., map-reduce scheduler chooses where tasks run
  Can control what traffic crosses which links

## Slide 53: Summary
Recap: datacenters
  new characteristics and goals
  some liberating, some constraining
  scalability is the baseline requirement
  more emphasis on performance
  less emphasis on heterogeneity
  less emphasis on interoperability
Notes: -- incast?
-- one big switch abstraction…

## Slide 54: What you need to know
Characteristics of a datacenter environment
  goals, constraints, workloads, etc.
How and why DC networks are different (vs. WAN)
  e.g., latency, geo, autonomy, …
How traditional solutions fare in this environment
  E.g., IP, Ethernet, TCP, DHCP, ARP
Specific design approaches

## Slide 55: Recap:
Key requirements
  High “bisection bandwidth”
  Low latency, even in the worst-case
  Large scale
  Low cost

## Slide 56: E.g., “Fat Tree” Topology [Sigcomm’08]
Notes: Few things to notice:
3 stages (can think of as edge / aggregation / core)
All switches have same number of ports (=4) [hence k^3/4=16 end hosts]
All links have same speed
Many paths

## Slide 57: Next: Questions
L2/L3 design:
  addressing / routing / forwarding in the Fat-Tree
L4 design:
  Transport protocol design (w/ Fat-Tree)

## Slide 58: Using multiple paths well

## Slide 59: Questions for today
L2/L3 design:
  addressing / routing / forwarding in the Fat-Tree
Goals:
  Routing protocol must expose all available paths
  Forwarding must spread traffic evenly over all paths

## Slide 60: Extend DV / LS ?
Routing
  Distance-Vector: Remember all next-hops that advertise equal cost to a destination
  Link-State: Extend Dijkstra’s to compute all equal cost shortest paths to each destination
Forwarding: how to spread traffic across next hops?

## Slide 61: Forwarding
Per-packet load balancing
to D
to D
to D
from A (to D)
from B (to D)
from C (to D)

## Slide 62: Forwarding
Per-packet load balancing
  + traffic well spread (even w/ elephant flows)
  − Interacts badly w/ TCP
to D
to D
to D
from A (to D)
from B (to D)
from C (to D)

## Slide 63: TCP w/ per-packet load balancing
Consider:
  sender sends seq#: 1,2,3,4,5
  receiver receives: 5,4,3,2,1
  sender will enter fast retx, reduce CWND, retx #1, …
  repeatedly!
Also: one RTT and timeout estimator for multiple paths
Also: CWND halved when a packet is dropped on any path
Multipath TCP (MP-TCP) is an ongoing effort to extend TCP to coexist with multipath routing
  Value beyond datacenters (e.g., spread traffic across wifi and 4G access)

## Slide 64: Forwarding
  Per-flow load balancing (ECMP, “Equal Cost Multi Path”)
  E.g., based on HASH(source-addr, dst-addr, source-port, dst-port)
to D
to D
to D
from A (to D)
from B (to D)
from C (to D)

## Slide 65: Forwarding
  Per-flow load balancing (ECMP, “Equal Cost Multi Path”)
  E.g., based on HASH(source-addr, dst-addr, source-port, dst-port)
  Pro: a flow follows a single path ( TCP is happy)
  Con: non optimal load-balancing; elephants are a problem
to D
to D
to D
from A (to D)
from B (to D)
from C (to D)

## Slide 66: Extend DV / LS ?
How:
  Simple extensions to DV/LS
  ECMP for load balancing
Benefits
  + Simple; reuses existing solutions
Problem: scales poorly
  With N destinations, O(N) routing entries and messages
  N now in the millions!

## Slide 67: Design a scalable routing solution
Design for this specific topology
Take 5 minutes, then tell me:
  #routing entries per switch your solution needs
  many solutions possible; remember: you’re now free from backward compatibility (can redesign IP, routing algorithms, switch designs, etc.)

## Slide 68: Solution 1: Topology-aware addressing
10.0.*.*
10.1.*.*
10.2.*.*
10.3.*.*
Notes: Few things to notice:
3 stages (can think of as edge / aggregation / core)
All switches have same number of ports (=4) [hence k^3/4=16 end hosts]
All links have same speed
Many paths

## Slide 69: Solution 1: Topology-aware addressing
10.0.0.*
10.1.0.*
10.2.0.*
10.3.0.*
10.0.1.*
10.1.1.*
10.2.1.*
10.3.1.*
Notes: Few things to notice:
3 stages (can think of as edge / aggregation / core)
All switches have same number of ports (=4) [hence k^3/4=16 end hosts]
All links have same speed
Many paths

## Slide 70: Solution 1: Topology-aware addressing
10.0.0.0
10.0.0.1
10.0.1.0
10.0.1.1
10.1.0.0
10.1.0.1
10.1.1.0
10.1.1.1
10.2.0.0
10.2.0.1
10.2.1.0
10.2.1.1
10.3.0.0
10.3.0.1
10.3.1.0
10.3.1.1
Notes: Few things to notice:
3 stages (can think of as edge / aggregation / core)
All switches have same number of ports (=4) [hence k^3/4=16 end hosts]
All links have same speed
Many paths

## Slide 71: Solution 1: Topology-aware addressing
10.0.0.0
10.0.0.1
10.0.1.0
10.0.1.1
10.1.0.0
10.1.0.1
10.1.1.0
10.1.1.1
10.2.0.0
10.2.0.1
10.2.1.0
10.2.1.1
10.3.0.0
10.3.0.1
10.3.1.0
10.3.1.1
10.0.*.*  1
10.1.*.*  2
10.2.*.*  3
10.3.*.*  4
1
2
3
4
Notes: Few things to notice:
3 stages (can think of as edge / aggregation / core)
All switches have same number of ports (=4) [hence k^3/4=16 end hosts]
All links have same speed
Many paths

## Slide 72: Solution 1: Topology-aware addressing
10.0.0.0
10.0.0.1
10.0.1.0
10.0.1.1
10.1.0.0
10.1.0.1
10.1.1.0
10.1.1.1
10.2.0.0
10.2.0.1
10.2.1.0
10.2.1.1
10.3.0.0
10.3.0.1
10.3.1.0
10.3.1.1
10.0.0.*  1
10.0.1.*  2
*.*.*.*  3, 4
1
2
3
4
Notes: Few things to notice:
3 stages (can think of as edge / aggregation / core)
All switches have same number of ports (=4) [hence k^3/4=16 end hosts]
All links have same speed
Many paths

## Slide 73: Solution 1: Topology-aware addressing
10.0.0.0
10.0.0.1
10.0.1.0
10.0.1.1
10.1.0.0
10.1.0.1
10.1.1.0
10.1.1.1
10.2.0.0
10.2.0.1
10.2.1.0
10.2.1.1
10.3.0.0
10.3.0.1
10.3.1.0
10.3.1.1
10.0.0.*  1
10.0.1.*  2
*.*.*.0  3
*.*.*.1  4
1
2
3
4
Notes: Few things to notice:
3 stages (can think of as edge / aggregation / core)
All switches have same number of ports (=4) [hence k^3/4=16 end hosts]
All links have same speed
Many paths

## Slide 74: Solution 1: Topology-aware addressing
10.0.0.0
10.0.0.1
10.0.1.0
10.0.1.1
10.1.0.0
10.1.0.1
10.1.1.0
10.1.1.1
10.2.0.0
10.2.0.1
10.2.1.0
10.2.1.1
10.3.0.0
10.3.0.1
10.3.1.0
10.3.1.1
10.0.0.0  1
10.0.0.1  2
*.*.*.0  3
*.*.*.1  4
1
2
3
4
Notes: Few things to notice:
3 stages (can think of as edge / aggregation / core)
All switches have same number of ports (=4) [hence k^3/4=16 end hosts]
All links have same speed
Many paths

## Slide 75: Solution 1: Topology-aware addressing
Idea: addresses embed location in regular topology
Maximum #entries/switch: k ( = 4 in example)
  Constant, independent of #destinations!
No route computation / messages / protocols
  Topology is “hard coded”
  (but still need localized link failure detection)
Problems?
  VM migration: ideally, VM keeps its IP address when it moves
  Vulnerable to misconfiguration (in topology or addresses)
Notes: Few things to notice:
3 stages (can think of as edge / aggregation / core)
All switches have same number of ports (=4) [hence k^3/4=16 end hosts]
All links have same speed
Many paths

## Slide 76: Solution 2: Centralize + Source Routes
Centralized “controller” server knows topology and computes routes
Controller hands server all paths to each destination
  O(#destinations) state per server
  But server memory cheap (e.g., 1M routes x 100B/route=100MB)
Server inserts entire path vector into packet header (“source routing”)
  E.g., header=[dst=D | index=0 | path={S5,S1,S2,S9}]
Switch forwards based on packet header
  index++; next-hop = path[index]
Notes: Few things to notice:
3 stages (can think of as edge / aggregation / core)
All switches have same number of ports (=4) [hence k^3/4=16 end hosts]
All links have same speed
Many paths

## Slide 77: Solution 2: Centralize + Source Routes
#entries per switch?
  None!
#routing messages?
  akin to a broadcast from controller to all servers
Pro:
  switches very simple and scalable
  flexibility: end-points (hence apps) control route selection
Cons:
  scalability / robustness of controller (SDN addresses this)
  Clean-slate design of everything
Notes: Few things to notice:
3 stages (can think of as edge / aggregation / core)
All switches have same number of ports (=4) [hence k^3/4=16 end hosts]
All links have same speed
Many paths

## Slide 78: Questions for today
L2/L3 design:
  addressing / routing / forwarding in the Fat-Tree
L4 design:
  Transport protocol design (w/ Fat-Tree)
Many slides courtesy of Mohammad Alizadeh, Stanford University

## Slide 79: Workloads
Partition/Aggregate
(Query)
Short messages [50KB-1MB]
(Coordination, Control state)
Large flows [1MB-50MB]
(Data update)
Delay-sensitive
Delay-sensitive
Throughput-sensitive
Slide from Mohammad Alizadeh, Stanford University
Notes: Replace PDF

## Slide 80: Tension Between Requirements
High Throughput
Low Latency
DCTCP
Deep queues at switches:
Queuing delays
increase latency
Shallow queues at switches:
Bad for bursts &
throughput
Objective:
Low Queue Occupancy & High Throughput
vs.
Slide from Mohammad Alizadeh, Stanford University
Notes: Deep Buffers – bad for latency
Shallow Buffers – bad for bursts & throughput
Reduce RTOmin – no good for latency
AQM – Difficult to tune, not fast enough for incast-style micro-bursts, lose throughput in low stat-mux

## Slide 81: Data Center TCP (DC-TCP)
Proposal from Microsoft Research, 2010
  Incremental fixes to TCP for DC environments
  Deployed in Microsoft datacenters (~rumor)
Leverages Explicit Congestion Notification (ECN)

## Slide 82: Explicit Congestion Notification (ECN)
Defined in RFC 3168 using ToS/DSCP bits in the IP header
Single bit in packet header; set by congested routers
  If data packet has bit set, then ACK has ECN bit set
Routers typically set ECN bit based on average queue length
Congestion semantics exactly like that of drop
  I.e., sender reacts as though it saw a drop

## Slide 83: Review: The TCP/ECN Control Loop
Sender 1
Sender 2
Receiver
ECN Mark (1 bit)
ECN = Explicit Congestion Notification
Slide from Mohammad Alizadeh, Stanford University
Notes: DCTCP is based on the existing Explicit Congestion Notification framework in TCP.

## Slide 84: DC-TCP: key ideas
React early and quickly: use ECN
React in proportion to the extent of congestion, not its presence
ECN Marks | TCP | DCTCP
1 0 1 1 1 1 0 1 1 1 | Cut window by 50% | Cut window by 40%
0 0 0 0 0 0 0 0 0 1 | Cut window by 50% | Cut window by 5%
Slide from Mohammad Alizadeh, Stanford University

## Slide 85: At the switch
  If Queue Length > K (note: queue length is instantaneous, not average)
    Set ECN bit in packet
K
Don’t
Mark
Mark
Slide from Mohammad Alizadeh, Stanford University

## Slide 86: At the sender
  α equal to 1 (high congestion): (same as TCP!)
  Maintain running average of the fraction of packets marked (α).
  Window adapts based on α:
Slide from Mohammad Alizadeh, Stanford University

## Slide 87: DCTCP in Action
Setup: Win 7, Broadcom 1Gbps Switch
Scenario: 2 long-lived flows, K = 30KB
(Kbytes)
Slide from Mohammad Alizadeh, Stanford University
Notes: Not ns2.

## Slide 88: DC-TCP: why it works
React early and quickly: use ECN
 Avoid large buildup in queues  lower latency
React in proportion to the extent of congestion, not its presence
  Maintain high throughput by not over-reacting to congestion
  Reduces variance in sending rates, lowering queue buildups
Slide from Mohammad Alizadeh, Stanford University

## Slide 89: Data Center TCP (DC-TCP)
Proposal from Microsoft Research, 2010
  Incremental fixes to TCP for DC environments
  Deployed in Microsoft datacenters (~rumor)
Leverages Explicit Congestion Notification (ECN)
An improvement; but still far from “ideal”

## Slide 90: What’s “ideal” ?
What is the best measure of performance for a data center transport protocol?
  When the flow is completely transferred?
  Latency of each packet in the flow?
  Number of packet drops?
  Link utilization?
  Average queue length at switches?

## Slide 91: Flow Completion Time (FCT)
Time from when flow started at the sender, to when all packets in the flow were received at the receiver

## Slide 92: FCT with DCTCP
Chart: Load
| 0.1 | 0.2 | 0.3 | 0.4 | 0.5 | 0.6 | 0.7 | 0.8
Ideal | 1.0066 | 1.0018 | 1.0026 | 1.0035 | 1.0051 | 1.0061 | 1.007 | 1.008
DCTCP | 1.2777 | 1.5442 | 1.7916 | 2.0476 | 2.3294 | 2.662 | 3.0631 | 3.596
TCP-DropTail | 2.7128 | 3.8866 | 5.0537 | 6.5398 | 8.4256 | 11.0812 | 15.0502 | 20.3733
Slide from Mohammad Alizadeh, Stanford University

## Slide 93: Recall: “Elephants” and “Mice”
55% of flows
3% of bytes
5% of flows
35% of bytes
<100KB
>10MB
  Web search, data mining (Microsoft) [Alizadeh 2010]
Slide from Mohammad Alizadeh, Stanford University

## Slide 94: FCT with DCTCP
Chart: Load
| 0.1 | 0.2 | 0.3 | 0.4 | 0.5 | 0.6 | 0.7 | 0.8
Ideal | 1.0066 | 1.0018 | 1.0026 | 1.0035 | 1.0051 | 1.0061 | 1.007 | 1.008
DCTCP | 1.2777 | 1.5442 | 1.7916 | 2.0476 | 2.3294 | 2.662 | 3.0631 | 3.596
TCP-DropTail | 2.7128 | 3.8866 | 5.0537 | 6.5398 | 8.4256 | 11.0812 | 15.0502 | 20.3733
Slide from Mohammad Alizadeh, Stanford University
Problem: the mice are delayed by the elephants

## Slide 95: Solution: use priorities! [pFabric, Sigcomm 2013]
Packets carry a single priority number
  priority = remaining flow size (e.g., #bytes un-acked)
Switches
  very small queues (e.g., 10 packets)
  send highest priority / drop lowest priority packet
Servers
  Transmit/retransmit aggressively (at full link rate)
  Drop transmission rate only under extreme loss (timeouts)
Slide from Mohammad Alizadeh, Stanford University

## Slide 96: FCT
Chart: Load
| 0.1 | 0.2 | 0.3 | 0.4 | 0.5 | 0.6 | 0.7 | 0.8
Ideal | 1.0066 | 1.0018 | 1.0026 | 1.0035 | 1.0051 | 1.0061 | 1.007 | 1.008
DCTCP | 1.2777 | 1.5442 | 1.7916 | 2.0476 | 2.3294 | 2.662 | 3.0631 | 3.596
TCP-DropTail | 2.7128 | 3.8866 | 5.0537 | 6.5398 | 8.4256 | 11.0812 | 15.0502 | 20.3733
Slide from Mohammad Alizadeh, Stanford University

## Slide 97: FCT
Chart: Load
| 0.1 | 0.2 | 0.3 | 0.4 | 0.5 | 0.6 | 0.7 | 0.8
Ideal | 1.0066 | 1.0018 | 1.0026 | 1.0035 | 1.0051 | 1.0061 | 1.007 | 1.008
pFabric | 1.0192 | 1.0359 | 1.0528 | 1.0707 | 1.0896 | 1.1088 | 1.1279 | 1.1435
DCTCP | 1.2777 | 1.5442 | 1.7916 | 2.0476 | 2.3294 | 2.662 | 3.0631 | 3.596
TCP-DropTail | 2.7128 | 3.8866 | 5.0537 | 6.5398 | 8.4256 | 11.0812 | 15.0502 | 20.3733
Slide from Mohammad Alizadeh, Stanford University

## Slide 98: Why does pFabric work?
Consider problem of scheduling N jobs at a single queue/processor
  J1, J2, … , Jn with duration T1, T2, …Tn respectively
“Shortest Job First” (SJF) scheduling minimizes average Job Completion Time
  Pick job with minimum Ti ; de-queue and run ; repeat
  I.e., job that requires minimum runtime has max priority
Solution for a network of queues is NP-hard
Setting priority=remaining flow size is a heuristic to approximate SJF

## Slide 99: DIY exercise: why does SJF work?
Consider 4 jobs with duration 1,2,4,8
Compute finish times w/ Round-Robin vs. SJF
Assume scheduler:
  Picks best job (as per scheduling policy)
  Runs job for one time unit
  Update job durations
  repeat
Job completion times:
  With RR: 1, 5, 10, 15
  With SJF: 1, 3, 7, 15

## Slide 100: Summary
Learn more:
  https://code.facebook.com/posts/360346274145943/introducing-data-center-fabric-the-next-generation-facebook-data-center-network/
Notes: -- incast?
-- one big switch abstraction…